## Slide 1
In collaboration with
M.J. Choi, M. Kim, J. Lee, W. Lee, G.S. Yun (POSTECH), C.W. Domier, N.C. Luhmann, Jr.
(UC Davis), Y.S. Bae, Y.M. Jeon, J.H. Lee, S.W. Yoon (NFRI), I. Joseph, W. Meyer, X.Q. Xu (LLNL), A.J.H. Donné (DIFFER/Eindhoven Univ. of Tech.), W.W. Xiao (SWIP)
Hyeon K. Park
POSTECH,
Pohang, Korea
24th IAEA FEC
Oct. 8 - 12, 2012
San Diego, CA, USA
ELMs in KSTAR
Simulated
image
Measured
image
Visualization of ELM dynamics and response to external perturbations via 2D/3D ECEI in KSTAR
2D ECEI
window
Notes: Mention advantages of the last day talk
Last IAEA - 2D this IAEA – 3D
Real time ELM and simulation result from BOUT++

## Slide 2: Outline
Why 2D/3D Visualization (ECEI)?
  Improvement of the predictive capability of complex dynamics of MHDs, Waves and Turbulence
  Verification of the ELMs in KSTAR (ECEI)
    ELM dynamics in KSTAR H-mode plasmas
    Comparison with the BOUT++ simulation results
Response to the external perturbations and comparison w/ the stability model
  Relevancy with the peeling/ballooning mode model
3D imaging on KSTAR & physics issues that can be further verified

## Slide 3
Alfvén waves (DIII-D)
B. Tobias et al., PRL (2010)
Sawtooth crashes (TEXTOR)
H.K. Park et al., PRL (2006)
Tearing modes (TEXTOR)
I. Classen et al., PRL (2007)
ELMs (KSTAR)
G.S. Yun et al., PRL (2011)
Improve predictive capability of MHD and wave physics
(e.g. Sawtooth, NTM, Alfvén waves, and ELMs)
Analogous to evolution of
diagnostic capabilities from
Stethoscope to MRI/CT
Why 2D/3D visualization (ECEI)?
Test of the Ballooning mode
model

## Slide 4
G
H
~1m
shot 4362
B0 ~ 2 T
Te0 ~ 2 keV
ne0 ~ m-3
First simultaneous
2D visualization of the internal kink (m=1)
and
Edge-Localized Modes
(ELMs)
H
G
KSTAR (2012)
Comibined
with MIR
KSTAR 2D/3D ECE imaging systems

## Slide 5
G.S. Yun et al.,
PRL 107 (2011)
1
2
3
100 ms
200 ms
0 ms
Initial growth to saturation
Shot=4431
ECEI (V)
1
2
3
Time (ms)
crash phase
4
855 ms
4
ELM dynamics in KSTAR plasmas
Time evolution of a single ELM

## Slide 6
215
220
225
230
R [cm]
KSTAR shot #6123 @ t~3.6s
Verification of the stationary ELM
2D image of an ELM
Toroidal mode number (n=5) is identified by the magnetics
q- and pressure profiles from EFIT are used to get the 2D image of the n=5 mode w/ the max. growth rate
BOUT++ Simulation of the n=5 ELM
Outcomes
Poloidal mode spacing is
incorrect !
Radial thickness is too thin !

## Slide 7
Parametric dependence of the mode structure
A) Poloidal mode spacing is sensitive to the local q-value
#1
#2
#3
B) Radial thickness of the mode and growth rates depends on P’
#1
#2
#4
Identification of the bootstrap current (Jb) due to P’ and n* changes w/ 3D system !!
Notes: Effective radius of curvature at the mid plane
𝑥(𝑡)=𝑎 cos⁡(𝑡+𝛿 sin⁡𝑡 )
𝑧(𝑡)=𝜅 𝑎 sin⁡(𝑡)
𝑟𝑎𝑑𝑖𝑢𝑠 𝑜𝑓 𝑐𝑢𝑟𝑣𝑎𝑡𝑢𝑟𝑒, 𝑎′= (𝑥^′2+𝑧^′2 )^(3/2)/|𝑥^′ 𝑧^′′−𝑧^′ 𝑥^′′ | =(𝑎 𝜅)/(1+𝛿)^2
Other method to estimate the field line pitch angle
𝑥(𝜃,𝜙)={𝑅_0+𝑎 cos(𝜃+𝛿 𝑠𝑖𝑛𝜃)} cos⁡𝜙
𝑦(𝜃,𝜙)={𝑅_0+𝑎 cos(𝜃+𝛿 𝑠𝑖𝑛𝜃)} sin⁡𝜙
𝑧(𝜃, 𝜙)=𝜅𝑎 sin⁡𝜃
𝑝𝑖𝑡𝑐ℎ 𝑎𝑛𝑔𝑙𝑒:tan⁡〖𝛼=〗 ├ Δ𝑧/(Δ𝑥 )]_(𝜃=0, 𝜙=0)=

## Slide 8
Comparison with the measured 2D images
Measured image
Synthetic image
Simulated image
Synthetic image
Radial resolution of the system (~1 cm) is comparable to the radial thickness of the mode
Broadening of the emissivity
The synthetic 2D images for n=5 and n=10 are in a good agreement with the measured 2D images.
n=5
ELM
n=10
ELM
Notes: Effective radius of curvature at the mid plane
𝑥(𝑡)=𝑎 cos⁡(𝑡+𝛿 sin⁡𝑡 )
𝑧(𝑡)=𝜅 𝑎 sin⁡(𝑡)
𝑟𝑎𝑑𝑖𝑢𝑠 𝑜𝑓 𝑐𝑢𝑟𝑣𝑎𝑡𝑢𝑟𝑒, 𝑎′= (𝑥^′2+𝑧^′2 )^(3/2)/|𝑥^′ 𝑧^′′−𝑧^′ 𝑥^′′ | =(𝑎 𝜅)/(1+𝛿)^2
Other method to estimate the field line pitch angle
𝑥(𝜃,𝜙)={𝑅_0+𝑎 cos(𝜃+𝛿 𝑠𝑖𝑛𝜃)} cos⁡𝜙
𝑦(𝜃,𝜙)={𝑅_0+𝑎 cos(𝜃+𝛿 𝑠𝑖𝑛𝜃)} sin⁡𝜙
𝑧(𝜃, 𝜙)=𝜅𝑎 sin⁡𝜃
𝑝𝑖𝑡𝑐ℎ 𝑎𝑛𝑔𝑙𝑒:tan⁡〖𝛼=〗 ├ Δ𝑧/(Δ𝑥 )]_(𝜃=0, 𝜙=0)=

## Slide 9
Response of the ELMs to perturbations
A
B
Peeling/Ballooning
mode model (T. Osborne)
RMP case
unstable n~10 to marginally
unstable n~5,10) requires a
reduction of Jb & P’ (observed
reductions in P’ & n*)
No signature of the applied
stochastic magnetic island (i.e.
interference in magnetic
diffusion time scale)
Resonant Magnetic Perturbation (n=1)
A
B
Supersonic Molecular Beam Injection
SMBI case
L1 – L2 is correlated w/ the [increasedn* (decreased P’)]
L2 – L3 is correlated w/ the [decreased n* (increased P’)]
L1~L3 > L2
Consistent with this model?
No change in n number?
Jb change – local q change?
m(q) is in wrong direction !!
C
Notes: Low (High) collisionality regimes
n mode change is wrong direction based on P’
m(q) mode change is also in wrong direction

## Slide 10
Response of the ELMs from RMP (n=1)
3.1 3.2 3.3 3.4 3.5
ELM frequency increases (6 to 8 kHz)
No change in poloidal spacing
of the mode (n~10)
Te gradient increases
Time (s)
Da(AU)
Pedestal
Te (AU)
Line
density
Da(AU)
Te (AU)
Te (AU)
Freq.
(KHz))
Pedestal
ch#5
LCFS ch #3
RMP
~35 ms
Unstable n~10 ELM
Marginally stable n~5 and n~10 ELM
Time
Transition from stable to marginally stable

## Slide 11
Marginally unstable n~5,10 modes during RMP
ELM crash
ELM crash
After every crash of the n~5 ELM, small change of p’ & n*, then the n~10 mode briefly appears.
Peeling dominated regime (low n ) – role of Jb is important for marginally unstable n~5 and n~10
Qualitatively consistent with the peeling/ballooning mode model
n~5
n~5
n~10
Te(A.U.)
Freq. (kHz)
Frequency change is due to the change in plasma rotation not toroidal/ poloidal mode number change
Rotation changes from Er ?
Er from charge imbalance ?
Charge imbalance from loss of density (primarily electrons)
Single n=5 ELM

## Slide 12
Short localized
heat pulse
3D imaging in KSTAR
  Equilibrium study (w/ known MHD modes; m=1, m=2, ELM, etc.) (local measurement of q, Jb, etc.)
  Toroidal asymmetry and transient bursting
Rotation speeds (toroidal, poloidal, and flow speed)
Heat pulse experiment (short pulse or sharp leading edge)
  Short time scale (t < 10ms) – local pitch angle
  Intermediate time scale (10ms < t < 1ms) - transient asymmetry in “burst” and toroidal mode interference
  longer time scale (10ms < t < 1ms) –
  poloidal, and radial transport
Demonstration of 3D
measurement of the
Tearing Mode with
two ECEI systems
(this week)

## Slide 13
Demonstration of 3D imaging in KSTAR
Raw imaging data are illustrated and 3D analysis is in progress

## Slide 14
Summary
Visualization via ECEI is effective for validation of the MHD turbulence and wave physics in tokamak plasmas
Synthetic image from the BOUT++ code verifies the measurement
  Poloidal mode spacing is a sensitive function of the local q value for a fixed toroidal n number [n, m(q)]: P’ is for growth rates.
  Synthetic images (w/ the instrumental and emissivity broadenings) are in good agreement with the measured images
Response of the ELMs to the external perturbations and comparison with stability model
  No continuum of the toroidal mode number in KSTAR configuration
  RMP(n=1) changes the unstable n~10 ELM into marginally unstable n~ 5,10 ELMs and then stabilizes all.
  Mode number changes are qualitatively consistent with the peeling/ballooning mode model
  3D measurement of the local pitch angle change of the ELM is critical (hence the role of Jb)