## Slide 1: Dynamics of energetic particle driven modes and MHD modes in wall-stabilized high beta plasmas on JT-60U and DIII-D
G. Matsunaga1), M. Okabayashi2), N. Aiba1), J. A. Boedo3), J. R. Ferron4),
J. M. Hanson5), G. Z. Hao6), W. W. Heidbrink7), C. T. Holcomb8),
Y. In9), G. L. Jackson4), Y. Q. Liu10), T. C. Luce4), G. R. McKee11),
T. H. Osborne4),D. C. Pace4), K. Shinohara1), P. B. Snyder4),
W. M. Solomon2), E. J. Strait4), A. D. Turnbull4),
M. A. Van Zeeland4), J. G. Watkins12), L. Zeng13),
the DIII-D Team and the JT-60 Team
1)JAEA, 2)PPPL, 3)UCSD, 4)GA, 5)Columbia Univ., 6)SWIP, 7)UCI,
8)LLNL, 9)FAR-TECH, 10)CCFE, 11)Univ. Wisconsin, 12)SNL and 13)UCLA
EX5-1
24th IAEA Fusion Energy Conference
8-13 October 2012
San Diego, USA

## Slide 2: JT-60U/DIII-D have discovered ELM triggering by EP driven mode (EPdM) in wall stabilized high-β plasmas
↓
  Important for edge stability
  in high-β burning plasmas
High-βN operation is advantageous to gain higher fusion output density,
  High-βN region above no-wall limit  ”wall-stabilized high-β region”
However, wall-stabilized high-βN region is not fully understood.
DIII-D
JT-60U
Energetic Particles (EPs)
& EP driven modes
MHD modes

## Slide 3: Outline
  EP driven mode to trigger ELM and
  its EP transport
  2. Waveform distortion of EPdM
  3. Conditions of ELM triggering/pacing by EPdM
  4. Possible mechanisms of
  ELM triggering by EPdM
  5. Summary

## Slide 4: Outline
  EP driven mode to trigger ELM and
  its EP transport
  2. Waveform distortion of EPdM
  3. Conditions of ELM triggering/pacing by EPdM
  4. Possible mechanisms of
  ELM triggering by EPdM
  5. Summary

## Slide 5: What is EP driven Mode (EPdM) to trigger ELM?
DIII-D
JT-60U
NOTE: These modes have been named “Off-axis Fishbone Mode (OFM)” on DIII-D and “Energetic particle driven Wall Mode (EWM)” on JT-60U.
Appear at high-βN > no-wall βN-limit,
Initial mode frequency ~ Precession frequency of trapped EPs,
Toroidally: mainly n=1, Poloidally: m=3~4 (localized at low field side)
Radially: global(peak @ q=2),
Strong distorted waveform,

## Slide 6: EP diagnostics indicate intense EP transport/loss
DIII-D
Trapped EPs (V||/V = 0.2~0.3,E=65-70keV) are transported by EPdM
Beacon transport/loss
1
2
3
4
5
6
like a sprinkler…

## Slide 7: Strong correlation between waveform distortion and EP transport
EP density near plasma edge increases monotonically with distortion increase
DIII-D

## Slide 8: Outline
  EP driven mode to trigger ELM and
  its EP transport
  2. Waveform distortion of EPdM
  3. Conditions of ELM triggering/pacing by EPdM
  4. Possible mechanisms of
  ELM triggering by EPdM
  5. Summary

## Slide 9: Waveform distortion has helical structure existing only at low field side(LFS).
Waveform distortion is toroidally localized Snake behavior
EP transport/loss ride on this helical structure
DIII-D

## Slide 10: Waveform distortion is composed of higher harmonics
Experimentally obtained δBθ(θ, φ) can be reproduced by n=1 & n=2 modes.
Unstable n=1, 2, and 3 modes w/o wall,
(ideal MHD analysis)
Distortion component always rides on maximum amplitude of fundamental component.
non-linear process?
DIII-D
Experiment
MARS-F analysis

## Slide 11: Outline
  EP driven mode to trigger ELM and
  its EP transport
  2. Waveform distortion of EPdM
  3. Conditions of ELM triggering/pacing by EPdM
  4. Possible mechanisms of
  ELM triggering by EPdM
  5. Summary

## Slide 12: ELM triggering by EPdMs occurs with some level of waveform distortion
Some level of waveform distortion seems to be needed,
Not always trigger ELM even with significant distortion level
 need other conditions satisfied?
DIII-D
JT-60U

## Slide 13: ELM triggering depends on time delay since the previous ELM
ELM triggering by EPdMs infrequently occurs after ELM crash,
Pedestal recovery (marginal edge stability) is needed
DIII-D

## Slide 14: Difference of ELM triggering by EPdMs on DIII-D and JT-60U
Partially synchronized
DIII-D
JT-60U
Fully synchronized

## Slide 15: ELM pacing occurs when the EPdM repetition frequency is larger than natural ELM frequency
Frequent EPdM cycle can pace ELM,
Pacing frequency is determined by balance between pedestal recovery and EP transport.
DIII-D
fEPdM < fELM
JT-60U
  fELM ≤ fEPdM
ELM
Pacing

## Slide 16: Outline
  EP driven mode to trigger ELM and
  its EP transport
  2. Waveform distortion of EPdM
  3. Conditions of ELM triggering/pacing by EPdM
  4. Possible mechanisms of
  ELM triggering by EPdM
  5. Summary

## Slide 17: Transported EPs to edge affect edge stability
Peeling-ballooning
Transported EPs may act as an additional pressure gradient
or change edge stability boundary
DIII-D
JT-60U
&
Possibility 1
Possibility 2
(1) Additional p can violate peeling-ballooning stability,
pped = (pth + δpEP)
(2) EP contribution (δWk) can narrow stable region.

## Slide 18: Analytic study says that EPs can destabilize marginal mode
Marginal mode can be destabilized by EP contributions.
From EPs
From bulk plasma w/o wall
From bulk plasma with an ideal wall
Dispersion relation (with resistive wall) + kinetic contribution:
From EPs

## Slide 19: Interpretation of ELM triggering by EPdM
Trapped EP can drive EPdM,
EPdM waveform distortion enhances EP transport to edge,
Transported EPs affect edge stability,
ELM triggering occurs.

## Slide 20: Summary
• ELM triggering by the EPdMs has been discovered on JT-60U and DIII-D,
  • Waveform distortion composed of higher harmonics strongly correlates with EP transport to edge,
• ELM triggering/pacing by the EPdMs need, (i)some level of waveform distortion and (ii) pedestal recovery,
• Transported EPs to edge affect edge stability as additional pressure or contribute to change stability.
New gate has been opened!
New approach to ELM pacing on ITER and DEMO.