## Slide 1
Physics Guidelines for a Tokamak DEMO
1H. Zohm, 1C. Angioni, 1E. Fable, 2G. Federici, 3G. Gantenbein, 1T. Hartmann,
1K. Lackner, 1E. Poli, 4L. Porte, 4O. Sauter, 5D. Ward, 1M. Wischmeier
1MPI for Plasma Physics, D-85748 Garching, Germany, EURATOM Association
2EFDA PPP&T Department, D-85748 Garching, Germany
3KIT, IHM, D-76021 Karlsruhe, Germany, EURATOM Association
4CRPP, EPFL, CH-1015 Lausanne, EURATOM Association
5CCFE Culham, Oxfordshire OX14 3DB, United Kingdom, EURATOM Association
Introduction: ITER Physics Guidelines
Towards DEMO Physics Guidelines
Application: An ‚improved H-mode‘ DEMO
Conclusions
Presented at 27th IAEA FEC, San Diego, USA, 12.10.2012

## Slide 2
ITER will address key issues for DEMO beyond present day experiments, the most prominent example being a-heating
ITER design based on sound physics base, first outlined in ‘ITER Physics Design Guidelines’ and then augmented by the ‘ITER Physics Base’
The EU programme has identified ‘DEMO physics issues’ (items not needed for ITER Q=10, but absolutely vital for DEMO and an FPP)
Steady state tokamak operation (bDEMO  2 bITER)
High density operation (n/nGW,DEMO  1)
Power exhaust (RDEMO/RITER = 1.2, but PDEMO/PITER = 4)
Disruptions (WDEMO/WITER > 5)
Reliable control with minimum sensors and actuators
In the following the ITER physics base is examined and updates are proposed related to the issues above (points 4 and 5 not covered today)
N.B.: where needed, DEMO technology constraints into account, too
Introduction – ITER Physics Guidelines

## Slide 3
Area | Issues
Equilibrium | Shaping vs. A
MHD stability | Fast particle effects on bmax,th, stability of fast particle driven modes
Energy balance | Transport at high b, n/nGW and Prad, Te profile shape
Particle balance | Density profile shapes @ n/nGW, impurity transport
Power exhaust | Detachment physics, lpower in detached divertor, other divertor concepts, ELM mitigation
H&CD physics | Full optimisation NBCD localisation
Dynamical phases | Realistic times for recharge
Disruptions | Timescales
Areas examined in our work

## Slide 4
Equilibrium
The physics of MHD equilibrium is well understood
Plasma configuration has to be consistent with DEMO-like coil set
shaping and control will be more restricted than in present day devices
important for larger A and ‚new‘ divertor configurations
TF ripple should be considered consistently
Example: ‚natural‘ elongation
k = 0.5/(A-1) + 1
Adjusting for ITER geometry:
k = 0.5/(A-1) + 1.5
li = 0.5 li = 1
A ~ 1.5
A ~ 2
A ~ 3
A ~ 5

## Slide 5
Stability – limits to thermal bN
Ideal MHD limits well understood
Troyon scaling bN,max = 4 li
corrections for pressure peaking
and active RWM control?
Resistive (NTM) stability important
conventional operational points
will be metastable to NTMs
active avoidance/control (ECCD)?
N=/(I/aB)=3.5
DEMO
(indicative)
R. Buttery et al., FEC 2008

## Slide 6
Stability – limits to fast particle b
Fast particle contribution is twofold
destabilisation of otherwards stable modes (XAEs, EPMs)
orbit effects can stabilise global MHD modes (example: RWM)
Depends on subtleties of profiles / nonlinear saturation – can trends be captured by 0-d fits?
stabilised by
precession
drift
stabilised
by bounce
modtion
NSTX, J. Berkery et al., Phy. Rev. Lett (2010)

## Slide 7
Particle transport – density profiles
Initial ITER assumption: density profiles are flat at n~nGW
Recent finding: peaking depends on neff rather than n/nGW
proposal: density limit applies to ne,ped/nGW (< 1)
calculate density peaking from first principles (include also b!)
Angioni et al. 2003
AUG

## Slide 8
Particle transport – density profiles
Initial ITER assumption: density profiles are flat at n~nGW
Recent finding: peaking depends on neff rather than n/nGW
proposal: density limit applies to ne,ped/nGW (< 1)
calculate density peaking from first principles (include also b!)
r (m)
n (1019m-3)
ITER, low b
G. Pereverzev et al NF 2005 P.T. Lang et al., this conference
ASDEX Upgrade
pellet fuelling

## Slide 9
ITER
DEMO
Due to the higher bN, n/nGW and Prad,core (see later), IPB98(y,2) not necessarily valid for DEMO
Heat transport: validity of IPB98(y,2)
Notes: 9

## Slide 10
Heat transport: validity of IPB98(y,2)
H-mode confinement tends to increase with higher bN (IPB98: ~ b-0.9)
H-mode confinement tends to decrease with higher n/nGW (IPB98: n0.4)
in addition, not clear how to correct for highly radiating discharges
This should be addressed, based on our increasing physics understanding
Same dataset, normalised to:
Kardaun 2006
IPB98(y,2)
AUG
C-Mod
JET
(but note n*, r* variation)
A. Kallenbach et al., this conference

## Slide 11
Exhaust of power through a divertor in DEMO
Technology limit stricter than in ITER (high n-fluence): Ptarget ≤ 5 MW/m2
Under attached conditions, no R-scaling of lq
expect 1-2 mm in midplane, 1-2 cm at the target  200 MW/m2
need to (partially) detach divertor and add substantial radiative losses
T. Eich et al. Phys. Rev. Lett. 2011

## Slide 12
Exhaust of power through a divertor in DEMO
Technology limit stricter than in ITER (high n-fluence): Ptarget ≤ 5 MW/m2
Under attached conditions, no R-scaling of lq
expect 1-2 mm in midplane, 1-2 cm at the target  200 MW/m2
need to (partially) detach divertor and add substantial radiative losses

## Slide 13
Design guidelines for power exhaust in DEMO
Long term: develop predictive capability for divertor detachment
Interim solution: use Psep/R divertor scaling together with Psep>PHL:
Lower bound: ASDEX Upgrade result: Psep / R = 7 MW/m
Upper bound: ITER assumption: Psep /R = 15 MW/m
An unprecedented ‚core‘ radiation level will be needed in DEMO!
Prad(r) must be tailored consistent with confinement needs
N.B.: we are also missing quantitative guide lines for the first wall load!

## Slide 14
Double Radiation Feedback on ASDEX Upgrade
Prad,main controlled by Ar-seeding, Tdiv controlled by N-seeding
Pheat,tot = 23 MW, but qdiv < 5 MW/m2 and Prad,core = 15 MW (67%)
close to Pthres, but still H=1 and bN = 3!
A. Kallenbach, subm. to Nucl. Fusion

## Slide 15
Heating and current drive in DEMO
 | LHCD | ECCD | FWCD | NBCD
g [A/(Wm2)] | 0.3-0.4 (indep. of Te) | 0.1-0.2 (ITER prediction) | ≤ 0.1 (ITER prediction) | 0.3-0.4 (ITER prediction)
Remark | very peripheral absorption | potential for optimisation (next slides) | small exp. Basis | off-axis CD not fully understood
Physics is relatively well understood, but efficiencies can be improved
w.r.t. ITER by a targeted optimisation, trading off flexibility

## Slide 16
Higher fECCD gives higher gCD, limited by parasitic 2nd harmonic absorption
This can be circumvented by using top launch!
Example: Optimisation of ECCD for DEMO
E. Poli et al.,
subm. to Nucl. Fusion

## Slide 17
Results for top launch (here, fECCD = 230 GHz)
Increasing fECCD, on-axis CD efficiency can go up to gCD = 0.4 (!)
launch position must be optimised for each desired CD position
then, current drive efficiencies come close to values for NBCD!
Efficiency gCD
Deposition radius
Poloidal launch angle
Poloidal launch angle
Toroidal launch angle
Toroidal launch angle

## Slide 18
Based on ASDEX Upgrade profile shapes with peaked density
for frec = 0.4, need to drive 8.8 MA with 150 MW (gCD = 0.5) at hCD = 0.5
Tough constraint on overall efficiency hCDgCD, but in reach for NBCD/ECCD!
First studies on an ‘improved H-mode’ DEMO
G. Tardini (IPP)
R=8.5 m
a =2.84 m
B=5.75 T
Ip = 17.6 MA
q95=4
bN = 3,
Pfus=2.2 GW
fbs ~ 0.5

## Slide 19
Improved technology and physics (hCD=0.5, gCD=0.4,H=1.2, bN = 3.5)
* bN = 3.5
tpulse = 8 hrs
frec = 37%
Pel,net = 500 MW
Long pulses in reach, but achieving steady state challenging stability limits…
pulsed and steady state options to be studied in parallel (different A!)!
high efficiency of H&CD systems becomes crucial!
The ‘ITER’ case: R0=7.5 m, Bt=5.2 T, A=3.1
H. Zohm, Fus. Sci. Technology (2011)

## Slide 20
Area | Issues
Equilibrium | Shaping vs. A
MHD stability | Fast particle effects on bmax,th, stability of fast particle driven modes
Energy balance | Transport at high b, n/nGW and Prad, Te profile shape
Particle balance | Density profile shapes @ n/nGW, impurity transport
Power exhaust | Detachment physics, lpower in detached divertor, other divertor concepts, ELM mitigation
H&CD physics | Full optimisation NBCD localisation
Dynamical phases | Realistic times for recharge
Disruptions | Timescales
Color code
Sound physics base
Restricted applicability
Major progress needed
Conclusions
Target: agree on DEMO Physics Guidelines across parties