## Slide 1
This work was performed under the auspices of the U.S. DoE by LLNL under Contract DE-AC52-07NA27344 and is supported by the China NSF under Contract No.10721505, the National Magnetic Confinement Fusion Science Program of China under Contracts No. 2011GB107001. LLNL-PRES-587359
T. Y. Xia1,2, X. Q. Xu2, Z. X. Liu1, S. C. Liu1, B. Gui1,2, W. Meyer2, G. Q. Li1 and J. G. Li1
1Institute of Plasma Physics, Chinese Academy of Sciences, Hefei, China.
2Lawrence Livermore National Laboratory, Livermore, CA 94550, USA
X.Q.Xu1, P.W.Xi1,2, A.Dimits1, I.Joseph1, M.V.Umansky1, T.Y.Xia1,3, B.Gui1,3, S.S.Kim4,
G.Y.Park4, T.Rhee4, H.Jhang4, P.H.Diamond4,5, B.Dudson6, P.B.Snyder7
1LLNL,2PKU,3ASIPP,4NFRI,5UCSD,6U.York,7GA
24th IAEA Fusion Energy Conference,
8-13 Oct. 2012, San Diego, USA
Multi-field two-fluid and gyro-fluid simulations of Edge-Localized-Modes
Notes: 1

## Slide 2: Principal Results
Part one: two-fluid model
Fundamental model: 3-field 2-fluid model is a good enough model for P-B instability and ELM crashes.
Multi-field 2-fluid models are necessary to describe heat transport.
BOUT++ simulations show that bright stripes from visible camera on EAST match ELM filamentary structures.
Part two: gyro-fluid model
First order FLR corrections from “gyro-viscous cancellation” in two-fluid model are necessary to agree with gyro-fluid results for high ion temperature.
Higher ion temperature introduces more FLR stabilizing effects, thus reduces ELM size.

## Slide 3: BOUT++ code for modeling tokamak edge ELMs and turbulence*
Framework for writing fluid / plasma simulations in complex tokamak geometry
  Proximity of open+closed flux surface
  Presence of X-point
Written in C++, started from BOUT code, jointly developed by LLNL, Univ. York, other U.S. and international partners
Well benchmarked with ELITE, GATO and other codes
* X.Q. Xu and R.H. Cohen, Contrib. Plasma Phys. 38, 158 (1998)
Umansky, Xu, Dudson, et al., , Comp. Phys. Comm. V. 180 , 887-903 (2008).
Dudson, Umansky, Xu et al., Comp. Phys. Comm. V.180 (2009) 1467.
X.Q. Xu, B.D. Dudson, P.B. Snyder, M.V. Umansky,
H.R.Wilson and T. Casper, Nucl. Fusion 51 (2011) 103040
Linear Growth Rate (γ/ωA)
3-field model
Toroidal mode number n

## Slide 4
This work was performed under the auspices of the U.S. DoE by LLNL under Contract DE-AC52-07NA27344 and is supported by the China NSF under Contract No.10721505, the National Magnetic Confinement Fusion Science Program of China under Contracts No. 2011GB107001. LLNL-PROC-583395.
T. Y. Xia1,2, X. Q. Xu2, Z. X. Liu1, S. C. Liu1, B. Gui1,2, W. Meyer2, G. Q. Li1 and J. G. Li1
1Institute of Plasma Physics, Chinese Academy of Sciences, Hefei, China.
2Lawrence Livermore National Laboratory, Livermore, CA 94550, USA
24th IAEA Fusion Energy Conference,
8-13 Oct. 2012,San Diego, USA
Multi-field two-fluid Peeling-Ballooning modes simulation with BOUT++
TH/5-2Ra
Notes: 4

## Slide 5
Three-field (ϖ, P, A||): peeling-ballooning model.
Four-field (ϖ, P, A||, V||): include sound waves.
Five-field (ϖ, ni, Ti, Te, A||): parallel thermal conductivities
Six-field (ϖ, ni, Ti, Te, A||, V||): combine all the models together, based on Braginskii equations, the density, momentum and energy of ions and electrons are described in drift ordering[1].
[1]X. Q. Xu et al., Commun. Comput. Phys. 4, 949 (2008).
Multi-field two-fluid model in BOUT++

## Slide 6
ELM crash in BOUT++ simulations
ELM size
Density ni (1019 m-3)
Normalized Time (tA)
Major radius R (m)
Major radius R (m)
Pressure Perturbation
Major radius R (m)
Vertical Z(m)
Electron Temperature
perturbation (keV)

## Slide 7
Toroidal mode number n
growth rate (γ/ωA)
Five-field model: low density leads to larger stabilizing effects by diamagnetic drifts, and density gradient drives larger ELM size
Density quantity affects linear growth rate through
5-field
With fixed pressure profile, ion density gradient leads to larger ELM size.
Ion density (1019 m-3)
Major radius R (m)
3-field:
ELM size
Normalized Time (tA)
15
10
5
0
ELM size (%)

## Slide 8
Thermal conductivities suppress the energy transport at inner boundary
Thermal conductivities with flux limited expressions suppress the increase of ELM size:
Flux limited expression:
Electron temperature is most sensitive to κ||.
Electron temperature (eV)
Normalized flux y (radial direction)
Electron temperature (eV)
Normalized Time (tA)
Ion density (m-3)
Normalized flux y (radial direction)

## Slide 9
3-field 2-fluid model is good enough to simulate P-B stability and ELM crashes, additional physics from multi-field contributes less than 25% corrections
Power depositions on PFCs.
Turbulence and transport
Toroidal mode number n
Growth rate (γ/ωA)
ELM size
Normalized Time (tA)
15
10
5
0
ELM size (%)
Fundamental physics in ELMs:
  Peeling-Ballooning instability
  Ion diamagnetic stabilization
     kinetic effect
  Resistivity and hyper-resistivity
     reconnection
Additional physics:
  Ion acoustic waves
  Thermal conductivities
  Hall effect
  Compressibility
  Electron-ion friction
change the linear growth rate less than 25%

## Slide 10
EAST#41019@3034ms
Visible camera shows bright ELM structure$
BOUT++ simulation shows that the ELM stripe are filamentary structures*
BOUT++ simulations show that the stripes from visible camera match ELM filamentary structures
Z (m)
2 2.25
0
-0.5
Major radius
R (m)
$Taken by J. H. Yang
*Figure by W.H. Meyer
Pitch match!
Mode number match!

## Slide 11
EAST experiments verified BOUT++ predictions
that low-n modes become dominant at high Ip
BOUT++:
Higher current has lower n mode
Qualitatively consist
Z.X. Liu et al, Phys. Plasmas 19 102502 (2012).
Z.X. Liu et al, EX/p7-11, “Study of ELMy H-mode plasmas and BOUT++ simulation on EAST”
Experiment:
400kAn=25
300kAn=30
Linear Growth Rate (γ/ωA)
Toroidal mode number n

## Slide 12
This work was performed under the auspices of the U.S. DoE by LLNL under Contract DE-AC52-07NA27344 and is supported by the China NSF under Contract No.10721505, the National Magnetic Confinement Fusion Science Program of China under Contracts No. 2011GB107001. LLNL-PRES-587357.
X.Q.Xu1, P.W.Xi1,2, A.Dimits1, I.Joseph1, M.V.Umansky1, T.Y.Xia1,3, B.Gui1,3, S.S.Kim4, G.Y.Park4, T.Rhee4, H.Jhang4, P.H.Diamond4,5, B.Dudson6, P.B.Snyder7 (1LLNL,2PKU,3ASIPP,4NFRI,5UCSD,6U.York,7GA)
24th IAEA Fusion Energy Conference,
8-13 Oct. 2012,San Diego, USA
Theory and Gyro-fluid Simulations of Edge-Localized-Modes
TH/5-2Rb
Notes: 12

## Slide 13: An isothermal electromagnetic 3-field gyro-fluid model
We derived an isothermal electromagnetic 3-field gyro-fluid model with vorticity formulation generalized from Snyder-Hammett gyro-fluid model [1] for edge plasmas.
Utilizing the Padé approximation for the modified Bessel functions, this set of gyro-fluid equations is implemented in the BOUT++ framework with full ion FLR effects,
In long-wavelength limit, this set of gyro-fluid equations is reduced to previous 3-field two-fluid model with additional gyro-viscous terms resulting from the incomplete “gyro-viscous cancellation” in two-fluid model given by Xu et al [2].
Higher ion temperature introduces more FLR stabilizing effects, thus reduces ELM size.
[1] P. B. Snyder and G. W. Hammett, Phys. Plasmas 8, 3199 (2001).
[2] X. Q. Xu, R. H. Cohen, T. D. Rognlien, et.al., Phys. Plasma 7, 1951 (2000).

## Slide 14: In the presence of large density gradient, gyro-fluid and two-fluid model show qualitative difference when kρi is large
Two-fluid model: no stabilizing on high-n modes,
Gyro-fluid model: strong FLR stabilizing on high-n modes.
Simple ion diamagnetic effect in two-fluid model is not sufficient to represent FLR stabilizing if density gradient is large!
Consider the large density gradient at H-mode pedestal:
Normalized wavenumber (kqri)
Growth rate (γ/ωA)

## Slide 15: Gyroviscous terms are necessary to stabilize Ion-Density-Gradient modes, which appear in two-fluid model
Two-fluid dispersion relation:
At long wavelength limit, gyro-fluid goes back to two-fluid but with additional gyroviscous terms
Normalized flux y (radial direction)
Normalized wavenumber (kqri)

## Slide 16: Higher ion temperature introduces more FLR stabilizing effects, thus reduces ELM size
Hyper-resistivity is necessary to ELM crash, but ELM size is weakly sensitive to hyper-resistivity;
With fixed pressure profile, high ion temperature introduce stronger FLR effect and thus leads to smaller ELM size
ELM size %
Ion temperature (keV)
Definition of ELM size:
Pressure (104 Pa)
Major radius R (m)
Rout
Rin

## Slide 17
Ratio of fit to analytical operator vs. wavenumber
Accurate non-Fourier methods for Landau-fluid operators
Tokamak edge:
kinetic effects important -> need Landau-fluid (LF) operators
Large spatial inhomogeneities & complicated boundary
  need non-Fourier implementation
  Useful accurate approximation:
The new method has favorable Fourier-like computational scaling
The error is less than 1.5%.

## Slide 18: Principal Results
Part one: two-fluid model
Fundamental model: 3-field 2-fluid model is a good enough model for P-B instability and ELM crashes.
Multi-field 2-fluid models are necessary to describe heat transport.
BOUT++ simulations show that bright stripes from visible camera on EAST match ELM filamentary structures.
Part two: gyro-fluid model
First order FLR corrections from “gyro-viscous cancellation” in two-fluid model are necessary to agree with gyro-fluid results for high ion temperature.
Higher ion temperature introduces more FLR stabilizing effects, thus reduces ELM size.

## Slide 19
P. W. Xi, X. Q. Xu, X. G. Wang, and T. Y. Xia, Phys. Plasmas 19, 092503 (2012)
Equilibrium EXB shear flow can stabilize high-n ballooning modes and reduce ELM size, but introduces Kelvin-Helmholtz instability and leads to larger ELM when flow shear is too large.

## Slide 20
Theoretical Equations for ni, Ti, Te, ϖ and ψ
We will neglect the thermal conductivities first.
S=(μ0RVA)/η=108
Cross term
(density gradient length scale)

## Slide 21
Vorticity:
Density:
Ohm’s Law:
Compressible terms
Parallel velocity terms
Electron Hall
Thermal force
Gyro-viscosity
The parallel ion equation:
Theoretical Equations for 6-field 2-fluid model

## Slide 22
Compressible terms
Parallel velocity terms
Electron Hall
Thermal force
Gyro-viscosity
Energy exchange
Energy flux
Theoretical Equations for 6-field 2-fluid model (cont.)

## Slide 23
The new method has Fourier-like computational scaling
For small number of grid cells, direct matrix multiplication is as efficient as Fourier
Implementation is as a sum of results of Helmholtz solves