## Slide 1
Progress of
the JT-60SA Project
24th IAEA Fusion Energy Conference, San Diego, Oct. 2012
Y. Kamada, P. Barabaschi, S. Ishida,
The JT-60SA Team,
JT-60SA Research Plan Contributors
(392 persons,
15 JA institutes, 23 EU Institutes)
* BA Satellite Tokamak Project team,
*JA Home team (JAEA),
*EU Home team (F4E, CEA , CIEMAT , Consorzio RFX , ENEA , KIT , SCK.CEN/Mol )
*JA Contributors (CRIEPI, Hokkaido Univ ., Keio Univ., Kyoto Institute of Technology , Kyoto Univ .,
Kyushu Univ., Nagoya Univ ., NIFS, Osaka Univ., Shizuoka Univ ., Univ. of Tokyo, Tohoku Univ .,
Tokyo Institute of Technology ., Univ. of Tsukuba )
*EU Contributors (Aalto Univ., CCFE , CEA , CIEMAT , CNRS/ Univ. de Marseille, Consorzio RFX ,
CRPP /Lausanne , EFDA-CSU , ENEA , ENEA-CREATE , ERM , FOM , F4E, FZ /Jülich , IFP-CNR ,
IPP /Garching, JET-EFDA , KIT , National Technical University of Athen , Univ. of York)
OV4/1

## Slide 2
JT-60SA: Highly Shaped Large Superconducting Tokamak
JT-60SA: highly shaped (S=q95Ip/(aBt) ~7, A~2.5) large superconducting tokamak confining deuterium plasmas (Ip-max=5.5 MA) lasting for a duration (typically 100s) longer than the timescales characterizing the key plasma processes such as current diffusion time, with high heating power 41MW.
Contribute to ‘Success of ITER’ , ‘Decision of DEMO design’ ＆Foster next generation leading scientists.
Sustainment Time (s)
0
1
5
6
4
3
2
0
3000
400
JT-60SA Target
100
20
40
60
80
DEMO reactors
ITER
ITER
bN
Existing Tokamaks
JT-60U
Steady-state
Inductive
FB ideal MHD limit
representative scenarios
5.5MA
4.6MA

## Slide 3
2011
2012
Construction
Operation
Year
2007
2008
2009
2010
2013
2014
2015
2016
2017
Disassembly
Assembly
Commissioning
Preparation
2018
2019
2020
Experiment
Integrated
Commissioning
By 2012 Sep., 18 Procurement Arrangements (PAs) have been concluded
(JA: 10PAs, EU: 8PAs) = 75% of the total cost of BA Satellite Tokamak Program.
Tokamak assembly starts in Dec. 2012, First plasma in Mar. 2019
The first experience of disassembling a radio-activated large fusion device in Japan.
Cryostat Base
from EU
2010 Mar.
2012 Dec.
Careful treatment of the activated materials and safety work are being recorded as an important knowledge base for Fusion Development.
2012 Oct.
JT-60U Torus Disassembly completed => JT-60SA Assembly from Dec. 2012

## Slide 4
Manufacture of EF coils & CS: JAEA
manufacturing error (in-plane ellipticity) of the current center
= 0.6mm (x 10 better than requirement)
EF5&6 manufacture started in JAEA Naka
EF (NbTi) : 55%
CS (Nb3Sn): 25%
Conductors :under
mass production (Naka)
completed
CS (5.1K, 8.9T) conductor test,
The critical current Ic by 4,000 cycle excitation (JAEA/NIFS)
=> Confirmed ‘no degradation’
Conductor Manufacture building (Naka)
EF4 coil completed
4.4 m
Coil Manufacture building (Naka)
Manufacture of EF5 & EF6 started
12 m

## Slide 5
TF coil & test :F4E, ENEA,CEA,SCK CEN
TF Conductor (F4E)
under mass production.
TF coil test (at nominal current): Facility preparation started(CEA Saclay) .
Cryostat (SCK CEN) ) completed & delivered to Saclay.
NbTi
(25.7kA,5.65T, 4.9K)
Conductor Samples &
Joints were tested successfully at SULTAN
TF Coils (ENEA, CEA)
Manufacture started:
The first winding packs
~ early 2013.
6 double
pancakes
18 (+1 spare)
ENEA
CEA

## Slide 6
1st.
2nd
3rd
Vacuum Vessel
120deg. (40deg. X 3) completed
Vacuum Vessel and Divertor : JAEA
Welding procedure established
=>tolerances well within requirement +-5mm
FY2012=> another 120deg.
41 MWx100s =>15 MW/m2 : W-shaped + vertical target with V-corner at the outer target
& divertor pumping speed can be changed by 10 steps between 0 - 100 m3/s
Divertor
Manufacture of brazed CFC monoblock targets on going. .
The first three divertor cassettes:
accuracy of 1 mm
Divertor cassettes: with fully water-cooled plasma facing components & remote handlable
A. Sakasai, FTP/P7-20
double wall, SS316L low cobalt (<0.05%)

## Slide 7
Cryostat Base manufacture
almost finished
=> Delivery to Naka in the 1st week Jan.
Cryostat :CIEMAT
13.4mf ,250t
Cryostat Vessel Body Cylindrical Section: drawings completed,
all the material has been supplied by JAEA
Cryogenic Systems :CEA
Quench Protection Circuit (CNR-RFX)
Prototypes completed
Switching Network Units (ENEA)
Contract signed in Sep. 2012
Superconducting Magnet PS (CEA & ENEA)
contracts expected by Mar. 2013
The RWM control coil PS (CNR-RFX)
specification is in the final stage
Power Supplies :
CNR-RFX, ENEA, CEA
High Temperature Superconducting Current Leads :KIT
26 current leads based on W7-X
Material purchasing is progressing
Contract of manufacture is expected within 2012
All CEA contributions: A.Becoulet, OV/4-5
P. Bayetti, FTP/P1-29

## Slide 8
→200kV & 100s without breakdown was demonstrated with 70mm single gap.
(500 keV & 3A demonstrated in 2010)
High power long pulse gyrotron (110GHz)
1 MW x 70 s & 1.4 MW x 9 s
achieved with newly installed 60.3 mmf transmission line & improved mode convertor.
The first dual-frequency gyrotron
(110 & 138GHz) was successfully manufactured, oscillation confirmed.
Development of N-NB & ECRF for JT-60SA:JAEA
N-NB System
2011-: Using test stand, we found
V/G0.5 ~ S-0.13 & N-0.15
V: vacuum insulation voltage
( the first scaling of the multi-aperture grid)
ECRF System
Mock-up test of a novel linear-motion antenna showed preferable characteristics.
M.Hanada, FTP/P1-18
A. Isayama, FTP/P1-16
→ 500kV extraction is expected in JT-60SA’s 3-stage-acceleration (also contributes to ITER)
N: number of the apertures
S: grid area (m2)
G( grid length(mm))0.5
V ( insulation voltage) (kV)

## Slide 9
With the ITER- and DEMO-relevant plasma parameters and the DEMO-equivalent plasma shapes, JT-60SA contributes to all the main issues of ITER and DEMO.
=> ‘simultaneous & steady-state sustainment of the key performances for DEMO’.
JT-60SA: Research Goal
JT-60SA Research Plan Ver. 3.0 has been completed in Dec. 2011 with 332 co-authors (JA 145 + EU 182 + Project Team 5, from 38 institutes)
JT-60SA should decide the practically acceptable DEMO parameters,
and develop & demonstrate a practical set of DEMO plasma controls.
DEMO reference: ‘ economically attractive ( =compact) steady-state’
but we treat ‘the DEMO regime’ as a spectrum.

## Slide 10
JT-60SA allows study on self regulating plasma control
with ITER & DEMO-relevant non-dimensional parameters
Collisionality,
Gyroradius,
Beta,
Plasma shape,
First ion beta,
Fast ion speed,
Pedestal
Collisionality
Mutual Interaction

## Slide 11
41MW×100s high power heating with variety
Variety of heating/current-drive/momentum-input combinations
Positive-ion-source NB (85keV), 12units × 2MW=24MW,
CO:2u, CTR:2u, Perp:8u
NB: 34MW×100s
Negative-ion-source NB,
500keV, 10MW, Off-axis
EC
NNB
N-NB driven current
Torque input
138GHz2.3T
110GHz,1.7T
jECCD(MA/m2)
EC driven current
A. Isayama, FTP/P1-16
ECRF: 7MW×100s
110GHz+138GHz,
9 Gyrotrons,
4 Launchers
with movable mirror
>5kHz modulation

## Slide 12
Profile controllability for high-bN & high-bootstrap plasmas
lower N-NB
upper N-NB
1.5D transport code TOPICS (with the CDBM transport model) + F3D-OFMC
 Self consistent simulation for Scenario 5-1( Ip=2.3MA with ITB)
By changing from the upper N-NB to the lower N-NB
=> qmin increases above 1.5.
S. Ide, FTP/P7-22
r
Toroidal rotation velocity
(105 m/s)
co-P-NB + ctr-P-NB
+ N-NB
co-P-NB + N-NB
ctr-P-NB + N-NB
0.3% of VAlfven
By changing combinations of tangential
P-NBs (co, counter, and balanced) with N-NB, the toroidal rotation profile is changed significantly.  RWM-stabilizing rotation
M. Honda, TH/P2-14

## Slide 13
0
1
0.5
r
0
0
1
3
2
7
4
6
5
q
JT-60SA allows
* dominant electron heating,
(+ scan of electron heating fraction )
* high power with low central fueling
* high power with low external torque
(+ scan)
For all the representative scenarios:
tflat-top(100s) > 3 x current diffusion time tR
Modelling studies by METIS:
G. Giruzzi, TH/P2-03
Advanced inductive scenario (#4-2):
q(r) reaches steady-state before t=50s with q(0)>1.
ITER- & DEMO- relevant heating condition
& sufficiently long sustainment
Scenario 4-２
Bootstrap fraction=0.4
ITER Q=10
ITER S.S.

## Slide 14: MHD stability control
RWM Control coil: 18 coils. on the plasma side.
Fast Plasma Position Control coil
Error Field Correction (EFC) coil)
bN = 4.1 (Cb =0.8) with effects of conductor sheath, noise (2G), and latency (150 ms).
Stabilizing Wall
(=>RMP, 18 coils 30 kAT, ~9 G~4x10-4BT
RWM control
RMP
+ ECCD (NTM), rotation control

## Slide 15
Fuel & Impurity Particle Control for ITER & DEMO
Compatibility of the radiative divertor with impurity seeding and sufficiently high fuel purity in the core plasma should be demonstrated.
SOL/divertor simulation code suite SONIC
The separatrix density necessary to maintain the peak heat flux onto the outer divertor target <~10MW/m2
Divertor heat flux can be managed by controlling Ar gas puffing.
S. Ide, FTP/P7-22
2
2.5
3
-2.8
-2.4
-2
R (m)
Z (m)
nAr/ni
Ar puff
back-flow
10
%
8
6
4
2
0.75 pa m3/s
Dsep (m)
qheat (MWm2)
IMPMC
Detailed simulation by IMPMC illustrates dynamics of impurity:
Origin (puff and back-flow) and distribution of Ar illustrated.
2
Acceptable for #5-1:
Ip=2.3MA, 85% nGW ,
separatrix density
~ 1.6x1019m-3

## Slide 16: Summary
The JT-60SA device has been designed as a highly shaped large superconducting tokamak with variety of plasma control capabilities in order to satisfy the central research needs for ITER and DEMO.
  Manufacture of tokamak components is in progress on schedule
  by JA & the EU.
  JT-60 torus disassembly has been completed, and JT-60SA assembly will start in Dec.2012.
  JT-60SA Research Plan Ver. 3.0 was documented by >300 JA & EU researchers.
In the ITER- and DEMO-relevant plasma parameter regimes, heating conditions, pulse duration, etc., JT-60SA quantifies the operation limits, plasma responses and operational margins in terms of MHD stability, plasma transport, high energy particle behaviors, pedestal structures, SOL & divertor characteristics, and Fusion Engineering.
The project provides ‘simultaneous & steady-state sustainment of the key performances required for DEMO’ with integrated control scenario development.