## Slide 1: State-of-the-Art Neoclassical Tearing Mode Control in DIII-D Using Real-time Steerable Electron Cyclotron Current Drive Launchers
Egemen Kolemen1, A.S. Welander2, R.J. La Haye2, N.W. Eidietis2, D.A. Humphreys2, J. Lohr2, V. Noraky2, B.G. Penaflor2, R. Prater2, and F. Turco3
1) Princeton Plasma Physics Laboratory, Princeton, NJ, USA
2) General Atomics, San Diego, CA, USA
3) Columbia University, 116th St and Broadway, New York, NY 10027, USA
Presented at IAEA Meeting, October, 2012
Catch &
Subdue

## Slide 2
New fully automatic NTM control system at DIII-D integrates all the Real-Time (RT) components of mode detection, location, suppression.
New control strategy “Catch and Subdue” can reduce the EC power use; lead to higher Q and reduce disruption risk in ITER
Fully Automatic NTM Control Using Real-Time Mirror Steering Can Suppress the 2/1 Mode

## Slide 3: In ITER, without ECCD, 2/1 Islands Can Grow and Cause Disruptions
Loss of H-mode and disruption is expected after locking
Need robust and efficient NTM control strategies
DIII-D experiment
ITER Simulation
La Haye
IAEA 2008

## Slide 4: Accurate Alignment of ECCD to Resonant Surface Suppresses Neoclassical Tearing Mode
Steerable Launcher Mirror
5 Gyrotrons (~2.8 MW injected)
Align the Electron Cyclotron Current Drive deposition with the Neoclassical Tearing Mode (NTM) island for suppression
Mirrors steered to move the beam vertically along the EC resonance for best alignment

## Slide 5: Accurate Alignment of ECCD to Resonant Surface Suppresses Neoclassical Tearing Mode
Align the Electron Cyclotron Current Drive deposition with the Neoclassical Tearing Mode (NTM) island for suppression
Mirrors steered to move the beam vertically along the EC resonance for best alignment
Steerable Launcher Mirror
5 Gyrotrons (~2.8 MW injected)

## Slide 6: DIII-D NTM Control System Overview
Diagnostics  Detect NTM / Find Location
Mirror Control
System
Plasma Control
System (PCS)
Gyrotrons
Control System
rf beam
EC Launcher

## Slide 7: Real time MSE Equilibria Enable Precise Tracking of Resonant Surface
Real time MSE tracks q=3/2 or 2
Calculate intersection point of the q surface with 2fce
Move the mirrors to align the ECCD with NTM
Tracking performance with minimal overshoot and <1 cm error.
Calibration:
  ECCD deposition: with 100 Hz ECCD modulation
  NTM location: with ECE based calculation & Sweeps across NTM
  Mapping of angle in mirror to position in plasma: Ray tracing

Δz

## Slide 8
Application to the 3/2 NTM:
  Head room to develop the technique

## Slide 9: NTM Control Methods: Successful 3/2 NTM Suppression After Mode Saturation

## Slide 10: NTM Control Methods: Preemptive NTM Suppression Achieved
Without ECCD, 3/2 NTM develops
NTM Preemption with ECCD

## Slide 11: Minimize EC Use for Higher Q Operation
ITER strategies:
  Preemptive suppression: uses continuous power, decreases Q
  Suppression after saturation: requires large power and long time, risking disruptions
  Preferable to intercept mode while still small
Q
10
6
8
4
12
0
10
20
30
PEC (MW)
Q=10 operating point
Pre-emptive stabilization with 7 or 20MW
3/2 NTM
2/1 NTM
Modes drop performance
[Zohm, IAEA 2006]
Pre-emptive suppression

## Slide 12: New "Catch and Subdue" Technique is More Efficient
Detect
Example of 3/2 Catch&Subdue
ms
Continuous q-surface Following
  Constantly calculate q-surface
  Track w/ mirrors; be ready to suppress
Detect that island is forming (2/1 or 3/2)
  Real-time Fourier analysis of Mirnov diagnostics
Turn Gyrotrons ON when the mode is detected
Result: Catch the island before it saturates
  Island saturation for 2/1 mode ~100-150 ms, 3/2 mode ~200ms

## Slide 13: Catch and Subdue Technique Enables Much Faster Suppression and Reduced ECCD Power
150093: No ECCD
(Beam drops after 5 sec)
150100: Catch and Subdue
(Many more examples)
Control Start
Results:
  Less power needed: Suppression with 3 gyrotrons instead of 5 for fully saturated modes
  Faster suppression (~140 ms after the gyrotrons turn on)
  Avoids continuous power deposition of the preemptive approach

## Slide 14: Catch and Subdue Even Works Well Starting from a Misalignment of ECCD and q Surface
Experiment:
Intentional mirror misalignment ~4 cm
Result:
System rapidly corrects deposition location
Fast suppression: complete suppression takes ~40 ms longer than aligned case

## Slide 15: Saturated Mode Suppression of 3/2 NTM Requires Good Alignment & Jeccd>Jboot
Color=Mode amplitude (Gauss)
Jeccd~Jboot
EC Power (MW)
No mode
Power: Peak ECCD (Jeccd) > local bootstrap current density (Jboot)  To replace the missing current in the island.
Alignment: ECCD aligned with the 3/2 island within the half width of the ECCD profile
Alignment: (ρ3/2-ρeccd)/FWHMeccd
Contour plot of Mode Amplitude
Saturated
Suppression

## Slide 16: Catch and Subdue Needs Less Power
Color=Mode amplitude (Gauss)
Jeccd~Jboot
EC Power (MW)
No mode
Catch and Subdue needs less power compared to saturated mode suppression.
C&S+Saturated
Suppression
Alignment: (ρ3/2-ρeccd)/FWHMeccd
Contour plot of Mode Amplitude

## Slide 17: Preemptive ECCD Reduces Power Requirement for 3/2 Suppression by Over 50%
Jeccd~Jboot
Preemptive
EC Power (MW)
No mode
Preemption reduces the power threshold.
Color=Mode amplitude (Gauss)
Alignment: (ρ3/2-ρeccd)/FWHMeccd
Contour plot of Mode Amplitude

## Slide 18: Early Mode Detection is Key for Rapid NTM Suppression
Below the critical amplitude small island effect takes over which enable fast suppression
Above the critical amplitude the mode saturates and suppression takes more than a second or becomes unachievable
*All shots with same βN and ECCD is actively aligned with a power of 1.5±0.2 MW at the island location.
Critical amplitude (knee)
2 late “catch” shots
3 early “catch” shots

## Slide 19
Application to the 2/1 NTM:
  Most challenging and important case

## Slide 20: Successful 2/1 NTM Catch and Subdue Demonstrated
Peak mode amplitude is reduced; without ECCD, mode reaches ~40 G and locks with loss of H-mode
The mode is brought to full suppression
Time [ms]

## Slide 21: 2/1 Mode Suppression Requires Good Alignment & Jeccd>Jboot
No mode
EC Power (MW)
Jeccd~Jboot
at q=2
Alignment: (ρ2/1-ρeccd)/FWHMeccd
Catch and Subdue
Suppression
Catch & Subdue suppression of 2/1 pushes the limit of the available EC power
Color=Mode amplitude (Gauss)
Contour plot of Mode Amplitude

## Slide 22: Preemptive ECCD Reduces Power Requirement for 2/1 Suppression by 40%
EC Power (MW)
Jeccd~Jboot
at q=2
Alignment: (ρ2/1-ρeccd)/FWHMeccd
Preemption
Catch and Subdue + Preemption
No mode
Preemption reduces the power threshold.
Color=Mode amplitude (Gauss)
Contour plot of Mode Amplitude

## Slide 23: Faster Suppression Needs Early Mode Detection for “Catch and Subdue”
Islands caught bigger than the critical amplitude takes much longer to suppress
Noise from sawteeth and ELMs are hindrance for small island detection
  Also important for ITER
Detection below the critical amplitude would reduce the energy even even lower
Critical Amplitude (knee)
#150783, #150792

## Slide 24: Integration of NTM Control Elements Has Demonstrated the Ability to Efficiently Control NTMs in ITER
Advanced integrated control:
  Mode detection with Fourier analysis of the Mirnov diagnostics
  Real-time high accuracy equilibrium reconstruction with MSE
  Fast EC steerable mirrors
  Fully automatic control algorithm “catch and subdue” that fuses all the ingredients.
Provides an efficient approach for ITER
  Reduces power requirements for NTM control
  Reduces time to suppress modes
  Decreases adverse effects on confinement & disruption
  Enables higher Q in ITER
Catch &
Subdue