## Slide 1
Control of 3D edge radiation structure with RMP fields applied to stochastic layer and stabilization of radiative divertor plasma in LHD
M. Kobayashi1, S. Masuzaki1, I. Yamada1, Y. Narushima1, C. Suzuki1, N. Tamura1, B.J. Peterson1, S. Morita1, C.F. Dong1, N. Ohno2, S. Yoshimura1, Y. Feng3, M. Goto1, K. Sato1, T. Akiyama1, K. Tanaka1, and the LHD experimental group1
1 National Institute for Fusion Science, Toki 509-5292, Japan
2 Nagoya University, Nagoya 464-8603, Japan
3 Max-Planck-Institute fuer Plasmaphysik, D-17491 Greifswald, Germany
EX/4-4
24th IAEA Fusion Energy Conference – IAEA CN-197
San Diego, USA 8-13 Oct.

## Slide 2
Introduction : Control of enhanced radiation at divertor region
Necessity of divertor heat load reduction for future devices:
Divertor detachment, radiative divertor is prerequisite to meet the engineering limit of PFC heat load (< several MW/m2).
Control of enhanced radiation region in its location & intensity is one challenging issue.
Involved issues in the physics:
A/M processes with strong non-linearity in cold plasma
Energy transport in parallel/perpendicular to field lines
Impurity transport, plasma recycling with volume recombination, momentum loss process
3D magnetic field configuration:
Seeking divertor optimization in helical devices, RMP application to tokamaks
 Effects of three dimensionality/symmetry breaking on radiating edge plasma are not yet fully understood.
This paper reports recent experimental results of radiative divertor stabilization with RMP application to the edge stochastic layer of LHD.
Radiative Divertor stabilization with RMP
RD transition induced by RMP
Compatibility with main plasma confinement
Magnetic structure dependence of RD stabilization

## Slide 3
Magnetic field structure of LHD: RMP (m/n=1/1) application
 remnant island in stochastic region
Helical coils
Plasma shape
RMP coils
(m/n=1/1)
With RMP
Without RMP
Resonance value
Rotational transform i
2.5
3.0
3.5
4.0
4.5
5.0
-1.0
-0.5
0
0.5
1.0
R (m)
Z (m)
Without RMP
With RMP (m/n=1/1)
Stochastic region
Edge surface layers
Divertor legs
Magnetic island O-point
104
103
102
101
100
Connection length (m)
R = 3.9 m, a ~ 0.7 m, 10 field periods (toroidal)
Divertor : carbon, Fist wall : Stainless steel

## Slide 4
With RMP  Stable sustainment of radiative divertor operation (RMP assisted RD)
Without RMP  Radiation collapse due to thermal instability
Reduction of divertor power load by a factor of 3 ~ 10
Radiation increase by a factor of ~ 3
Stable operation around density limit
No significant degradation of main plasma confinement
Plasma shrinks at RD phase due to radiative energy loss and RMP penetration
No noticeable high Z impurity (Fe) emission at high density range.
RD (6.6x1019 m-3)
Attach
(ne = 2.0x1019 m-3)
Significant increase in carbon emission
Radiative divertor
CVI (a.u.)
CV (a.u.)
CIV (a.u.)
CIII (a.u.)
Radiative divertor
With RMP
S. Morita et al. EX/P5-18
Divertor power
load (MW/m2)
With RMP
Without RMP
Radiation
(a.u.)
Wp (kJ)

## Slide 5
Increased volume of low Te region (~10 eV) at remnant island with RMP leads to enhanced carbon radiation
Radiation collapse
Without RMP
With RMP
Radiation Power (a.u.)
ne dependence of radiation power (bolometer)
Without RMP
With RMP
Resonance layer
Te flattening at island
Te, ne profiles at outboard midplane
(Thomson scattering)
(Estimated with ncarbon=0.01ne
net = 1017 m-3 s)
Carbon radiation
RD
Radiation enhanced

## Slide 6
Modification of 3D edge radiation structure by RMP : 3D numerical simulation
R
Z
Without RMP
With RMP
Carbon radiation distribution by EMC3-EIRENE
Inboard
side
Outboard
side
2.0x100
2.0x10-1
2.0x10-2
2.0x10-3
MW/m3
Poloidal angle (deg.)
Toroidal angle (deg.)
Without RMP
With RMP
0
100
200
300
0
100
200
300
Poloidal angle (deg.)
0
100
200
300
Inboard
Outboard
Outboard
Radiation peak at inboard side
Localization around X-point of m/n=1/1 island
Without RMP  Radiation peak appears at inboard side.
With RMP  X-point of m/n=1/1 island is selectively cooled.
X-point of island
Inboard
Outboard
Outboard

## Slide 7
Radiation profile : Comparison between experiments & simulation
With RMP
X-point of island
Carbon radiation distribution by EMC3-EIRENE
Without RMP
Inboard side
LOS of
measurements
Ch1
Ch16
Experiments
Simulation
Intensity (mW/m2)
Channel
Intensity (a.u.)
Channel
Systematic downward shift of peak location by 2 channels in experiments.
Fine structure in simulation is not observed in experiments.
The qualitative change of profiles due to RMP application roughly agrees between experiments & simulation.
Results implies selective cooling at X-point of m/n=1/1 island in experiments.
The well-structured magnetic field “catches” the radiation and prevents it from penetrating inward?!

## Slide 8
RD transition can be induced by RMP ramp-up
 new control knob for divertor power load reduction
Density & NBI heating are kept constant before RD transition.
RMP strength is increased during discharges.
Radiation increase & divertor particle flux reduction occurs when RMP ( ) reaches 0.07~0.08%.
RMP is suppressed in attached phase
 Sudden penetration of RMP at RD transition
Time evolutions of RMP ramp-up experiment
(10-4 Wb)
Phase of
(p rad)
DF
plasma
r
DF
plasma
r
Growth
Healing
Compatibility with Ne seeding scheme is confirmed.

## Slide 9
Main plasma confinement : Recovery of energy confinement after RD transition ( ) due to pressure profile peaking
Without RMP
With RMP (attach)
With RMP
(radiative divertor)
t
E
exp
/ (fren )
t
E
ISS04
Confinement enhancement factor vs ne
RD transition
Increase of ne leads to confinement degradation without RMP.
Significant degradation in RMP attached phase  due to large magnetic island in the edge.
Energy confinement recovers after RD transition with RMP  due to pressure peaking.
The cause of the pressure peaking is under investigation.
With RMP
(radiative divertor)
With RMP
(attach)
Without RMP
pe profiles with & without RMP

## Slide 10
Realization of RMP assisted RD depends on RMP strength & radial location of island with respect to LCFS
Stable RD
Radiation collapse
No Te flattening due to plasma healing
LCFS
Clearance between island & LCFS is too small
Healing
0
Stable RD
Radiation collapse
(r X point – r LCFS ) vac ( m )
2.0x10-4
1.0x10-3
2.0x10-3
RD controllability in terms of magnetic field structure
Connection length (m)
6x104
6x103
6x102
6x101
Lower threshold of RMP strength depends also on MHD plasma response
Separation between radiation region (island) & confinement region is important factor for stable RD operation
Radial extension of radiation region ~ several cm
S. Sakakibara et al. EX/P4-30

## Slide 11
Summary
With RMP  stable sustainment of RD (RMP assisted RD)
Without RMP  radiation collapse due to rapid growth of thermal instability
The remnant island created by RMP modulates the radiation distribution
Increased volume of cold and dense plasma around island  enhanced radiation
Strong radiation condensation around island X-point  radiation profile measurements and 3D transport simulation
Selective cooling around the island is considered responsible for stabilization of RD operation
RD transition can be induced by RMP ramp-up  New control knob for divertor heat load reduction
RMP assisted RD is compatible with Ne seeding scheme
Good main plasma energy confinement factor ~ 0.96 during RMP assisted RD
Due to pressure peaking after RD transition
Operation space of RMP assisted RD investigated in terms of & distance between the island and main plasma
Lower threshold of is affected by MHD plasma response (healing of island)
Separation between island and main plasma should be large enough > radial extension of radiation region (~ several cm)
Effects of edge magnetic structure on RD plasma have been investigated with RMP (m/n=1/1) application to stochastic layer of LHD.
Further investigations
♠ Power balance : consistency between divertor heat load reduction and total radiated power
♠ Divertor heat load distribution : toroidal and poloidal direction
♠ Compatibility with medium – high Z impurity (Ar, Kr, Xe etc) seeding schemes
♠ Mechanism of the stabilization : transport in 3D magnetic field structure

## Slide 12
Backup materials

## Slide 13
Large Helical Device (LHD) and magnetic field structure
Helical coils
Plasma shape
Perturbation coils m/n=1/1
(a)
Field line trajectories in the edge of LHD
divertor leg field lines
divertor plate
Helical coils
R=3.90 m
a~0.70 m
(b)
Inside view of vacuum vessel
Major radius =3.90 m
Averaged plasma minor radius ~ 0.7 m
Plasma volume ~ 30 m3
RMP: m/n=1/1
Divertor: carbon
First wall: stainless steel
Bt ~ 3T
NBI heating ~ 23 MW
Major Specification

## Slide 14
Decrease of Divertor flux at strike point:
Factors of 1/6 @ inboard, 1/3 @ upper divertor
Flux broadening to private region (the pattern has n/m=1/1 mode structure)
Divertor probe measurements indicates non-uniformity of divertor power load in the RD phase (m/n=1/1?)  Toroidal distribution is under investigation
Upper divertor
Toroidal profile of private particle flux
1/6
Inboard divertor
1/3
Flux broadening

## Slide 15
Close correlation between radiation profile and magnetic field structure
With RMP, radiation penetration is “blocked” by island (?!)  RD stabilization
With RMP
Long flux tubes of m/n=1/1 remnant island
midplane
Without RMP
Confinement region
Radiation at midplane
(MW/m3)
101
100
10-1
10-2
1x104
1x103
1x102
1x101
1x100
Connection length (m)
Radiation penetration is “blocked” by remnant island (?!)
stabilization
Radiative divertor
R (m)
Radiation penetration to core
collapse
R (m)
ncarbon=0.01ne
net = 1017 m-3 s

## Slide 16
RMP assisted RD
Radiation enhanced with Ne seeding
Compatibility with Ne seeding scheme is confirmed.
Divertor particle flux (A)

## Slide 17
With RMP
Radiative divertor
Attach
Te, ne profiles at attach & RD phase with RMP

## Slide 18
(S. Konoshima JNM 2003)
Detachment onset
X-point MARFE
X-point

## Slide 19
Divertor power
load (MW/m2)
With RMP
Without RMP
Wp (kJ)
RMP assisted RD

## Slide 20
Line integrated radiation profiles (AXUVD)
Viewing lines
Ch.4
Ch.1
Ch.16
Upper
Lower
Channel number
Ch.4
radiative collapse
RMP assisted RD
Without RMP
With RMP
Viewing lines of radiation measurements
Impurity radiation distribution
With RMP
Without RMP
(MW/m3)
Island X-point
R (m)
R (m)
Z (m)
t~3.0 s
t~3.1 s
8.0x100
8.0x10-1
8.0x10-2
8.0x10-3
Radiation profile measurement & transport simulation indicate localized radiation around X-point of m/n=1/1 island
<Experiments>
<Simulation>