## Slide 1: Populating a National Nuclear Forensics Library (NNFL)
John F. Wacker
Pacific Northwest National Laboratory
Presented at the “International Conference on Advances in Nuclear Forensics:
Countering the Evolving Threat of Nuclear and Other Radioactive Material out of Regulatory Control”
IAEA, Vienna, Austria 07-10July2014
PNNL-SA-103748
Presentation Ref. Number: IAEA-CN-218-59
International Conference on Advances in Nuclear Forensics, Vienna, Austria; 7-10 July 2014

## Slide 2: Acknowledgements
Pacific Northwest National Laboratory
  Andy Luksic (retired)
US Department of Energy
  Marcia Brisson (Nuclear Materials Information Program (NMIP))
  Stephen LaMont (Nuclear Materials Information Program (NMIP))
  Heather Dion (National Nuclear Security Administration)
US Department of Homeland Security
  William Ulicny
Los Alamos National Laboratory
  David Olivas
  Joe Watts
Savannah River National Laboratory
  Donna Beals (retired)
PNNL-SA-103748

## Slide 3: United States NNFL
Goal: Ensure domestic material would be recognized if interdicted or used in a terrorist event
Approach: Develop a Library and necessary support structure
National Nuclear Forensics Library
National Nuclear Material Archive
Data Interpretation and Comparative Analysis
Laboratory Analysis and Process Modeling
Entire U.S. effort is part of the U.S. Nuclear Materials Information Program (NMIP)
PNNL-SA-103748

## Slide 4: U.S. NNFL: Implementation
National Nuclear Forensics Library
National Nuclear Material Archive
Data Interpretation and Comparative Analysis
Laboratory Analysis and Process Modeling
Data Dictionary: Published
Database: Under Development
DOE Laboratories
Los Alamos
Y-12
PNNL-SA-103748

## Slide 5: Developing an Inventory
If some nuclear material is found outside of administrative controls anywhere in the world, can each country answer the question:
  “Is it ours?”
Verifying inventory may confirm that material does not appear to be missing, but that may not be sufficient
PNNL-SA-103748

## Slide 6: Developing an Inventory
Fully characterizing the US inventory of nuclear materials is a challenging and complex task
The US has been producing nuclear materials for ~70 years
The US inventory includes a wide variety of uranium and plutonium
  Physically
  Chemically
  Isotopically
Any of these can be modified, though changing the isotopics is the most difficult
PNNL-SA-103748

## Slide 7: Searching for Nuclear Materials Data
Nuclear Materials Management & Safeguards System (NMMSS)
  U.S. government’s information system containing current and historic data on the possession, use, and shipment of nuclear materials.
  NMMSS contains some materials information, but does not contain sufficient details needed for nuclear forensics analysis
Production facilities
  Information is available on various materials, produced and recycled
  But, the data are often incomplete, e.g., data showing that specifications have been met
Thus, NMIP needed to develop a more detailed database of materials characteristics
  Nevertheless, information in NMMSS and other databases has proven to be valuable and is being utilized by NMIP
PNNL-SA-103748

## Slide 8: Finding the Data
NMMSS
Weapons Program
  Material Production
  Weapons Production
  Surveillance
  Disposition
Fuel Fabrication
Publications/Reports
  National Laboratories
  Scientific Journals
PNNL-SA-103748

## Slide 9: Mining Existing Data
Isotopic Composition (NMMSS)
  Uranium weight and U-235 content
  Plutonium weight and Pu-239 content
Initial characterization (but we require more!)
  Uranium: U-232, U-233, U-234, U-236
  Plutonium: Pu-238, Pu-240, Pu-241, Pu-242
Other sources have additional data, but is it useful?
PNNL-SA-103748

## Slide 10: Effect of Process Histories
Different processes impart different signatures.
Identifying signatures associated with processes we used, potentially allows us to include or exclude unknown material as being “ours.”
We need to identify those signatures and acquire the associated data on our material.
PNNL-SA-103748

## Slide 11: Data
Goal: Full Characterization of Nuclear Materials
  Relevant material characteristics includes:
    Isotopic composition
    Elemental composition
    Chemical form
    Physical form
    Processing age
    Morphology
This presentation will discuss the U.S. experience
PNNL-SA-103748

## Slide 12: Data
Detailed information on isotopic compositions is our initial priority
  Pu-238 U-233
  Pu-239 U-234
  Pu-240 U-235
  Pu-241 U-236
  Pu-242 U-238
First, acquire available information
Identify Gaps, and work to fill them
PNNL-SA-103748

## Slide 13: Data
NMMSS provides high-level characterization for most attributes
Types of historic data sets
  Facility Production Records
  Shipments from Production Site
  Rocky Flats measurements
  Integrated Surveillance Program (MOX program)
  R&D Measurements
Much of the U.S. data is hard copy
Much is no longer available
PNNL-SA-103748

## Slide 14: Data
Tens of thousands of records
  Numerous facilities
  Varying requirements
  Quality determined by requirements
    Accuracy may be goal of measurement
    Within specification may be sufficient
    Less than may be good enough
    Function of time (we got better as time progressed)
Measurements performed for production purposes are generally not sufficient for forensic purposes
PNNL-SA-103748

## Slide 15: Measurements
Characterization of plutonium changed significantly over time
  1940s-1950s neutrons/g-sec
  mid-1950s Pu-240
  late-1960s Pu-240, Pu-241
  mid-1970s Pu-240, Pu-241, Pu-242
  1980s Pu-240, Pu-241, Pu-242, Pu-238
Uranium data evolved to include U-236, U-234 and other minors
Recorded data changed with time
Recorded data changed with utilization
15
PNNL-SA-103748

## Slide 16: Measurements
DA
NDA
16
PNNL-SA-103748

## Slide 17: Measurements
Chart: Pu-240/Pu-239
| 0.00270812437311937 | 0.00754032258064517 | 0.0131712259371834 | 0.0189602446483181 | 0.024923076923077 | 0.0309597523219814 | 0.0368639667705088 | 0.0428422152560085 | 0.0486855941114616 | 0.0546031746031746 | 0.0604255319148937 | 0.0662740899357602 | 0.0719827586206897 | 0.0776814734561214 | 0.0835332606324975 | 0.0891447368421052 | 0.0949227373068432 | 0.100443951165372 | 0.106145251396648 | 0.111797752808989 | 0.117514124293785 | 0.122727272727273 | 0.128146453089245 | 0.13463751438435 | 0.140046296296297 | 0.145518044237486 | 0.151053864168618 | 0.156654888103651 | 0.162322274881517 | 0.166666666666667 | 0.172455089820359 | 0.178313253012048 | 0.184242424242425 | 0.188794153471377 | 0.194852941176471 | 0.199753390875463 | 0.205700123915737 | 0.21072319201995 | 0.216791979949875 | 0.221941992433796 | 0.228136882129278 | 0.233418367346939 | 0.238461538461539 | 0.243556701030928 | 0.25 | 0.255541069100391 | 0.2608125819135 | 0.266139657444005 | 0.271523178807948 | 0.276964047936085 | 0.282463186077644
CANDU | 3.2598e-08 | 3.7702e-07 | 1.5299e-06 | 4.0469e-06 | 8.4615e-06 | 1.5273e-05 | 2.513e-05 | 3.8245e-05 | 5.531e-05 | 7.6614e-05 | 0.00010255 | 0.00013383 | 0.00017026 | 0.00021235 | 0.00026063 | 0.00031579 | 0.00037748 | 0.00044617 | 0.00052179 | 0.00060562 | 0.00069605 | 0.00079545 | 0.00090389 | 0.0010196 | 0.0011447 | 0.0012806 | 0.0014169 | 0.0015665 | 0.0017299 | 0.0019048 | 0.0020838 | 0.0022771 | 0.0024727 | 0.0026797 | 0.0029044 | 0.0031443 | 0.0033829 | 0.0036409 | 0.0038972 | 0.004174 | 0.0044613 | 0.0047577 | 0.0050641 | 0.0053866 | 0.0057124 | 0.0060626 | 0.006422 | 0.0067852 | 0.0071656 | 0.0075632 | 0.0079652
NRX | 6.2651e-08 | 5.9394e-07 | 2.1218e-06 | 5.1531e-06 | 1.0174e-05 | 1.7629e-05 | 2.7979e-05 | 4.1502e-05 | 5.87e-05 | 7.9579e-05 | 0.00010476 | 0.00013404 | 0.00016898 | 0.00020753 | 0.00025189 | 0.00030185 | 0.00035699 | 0.00041822 | 0.00048401 | 0.00055654 | 0.00063474
PWR | 3.8338e-09 | 3.9318e-08 | 1.5377e-07 | 3.998e-07 | 8.3535e-07 | 1.5081e-06 | 2.4848e-06 | 3.8149e-06 | 5.5454e-06 | 7.7222e-06 | 1.0451e-05 | 2.7818e-05 | 6.6387e-05 | 0.00012818 | 0.00021842 | 0.00033911 | 0.00049288 | 0.00068217 | 0.00090929 | 0.0011765
BN-600 (UO2) | 5.3075e-08 | 4.7089e-07 | 1.6887e-06 | 4.2072e-06 | 8.5969e-06 | 1.5504e-05 | 2.5639e-05 | 3.9815e-05 | 5.8901e-05 | 8.3876e-05 | 0.00011574 | 0.00015573 | 0.00020486 | 0.00026442 | 0.00033589 | 0.00042042
Hanford 327°C | 3.0586e-07 | 3.0278e-06 | 1.0841e-05 | 2.6087e-05 | 5.0843e-05 | 8.7e-05 | 0.00013625 | 0.00020017 | 0.00028024 | 0.00037769 | 0.0011697 | 0.002562
Hanford 727°C | 6.2763e-07 | 6.0897e-06 | 2.1442e-05 | 5.0951e-05 | 9.8263e-05 | 0.0001667 | 0.0002591 | 0.0003783 | 0.00052667 | 0.00070679 | 0.0021574 | 0.0046914
NDA
PNNL-SA-103748
Notes: Hanford 327C = 600K

## Slide 18: Data Vetting: Verification and Validation
1
DATA for SUBMISSION to NNFL
2
DATA INPUT
Manual Entry or
Electronic Data from another Database
6
AUTHORIZE By
SME and Database Expert
&
Release Data To NNFL
3
REVIEW
INPUT DATA
5
DATA VALIDATION
By Subject Matter Expert
4
DATA VERIFICATION
By Database Expert
PNNL-SA-103748

## Slide 19: Issues for Data Vetting
Transcription errors
  Typos, improperly transferred characters, etc.
Field mismatches
  Truncating number strings, conversion amongst different numeric formats (for instance from integer to scientific notation)
  Text to numeric conversions
    e.g., parsing text information into numeric or alphanumeric fields
Less-than values, detection limits, non-reported data
  e.g., “<500 ppm” or “not detected”
      What should be entered when a numerical value is expected by the database?
Values with no quoted uncertainty
  Very common in older database
Unit conversions or mismatched units
PNNL-SA-103748

## Slide 20: Gaps and Prioritization
Acquiring data is a work in progress
Largest inventory categories first
  Isotopics is considered the primary characteristic
  Other data (elemental composition, trace elements, etc.) to be obtained as available
Conclusions to date
  All historic data is not be available
  All historic data is not suitable for forensic applications
    Different analytical techniques produce different results
  Modeled data may be required in the interim
  New measurements will be required
Planning and Prioritization is in progress
20
PNNL-SA-103748