## Slide 1: Summary in view of divertor concepts beyond ITER
32
  If Resonant Magnetic Perturbation fields will be applied beyond ITER, 3D boundary effects need to be considered.
  DIII-D and ASDEX Upgrade show different reaction of heat flux to magnetic perturbations.  Detailed survey of devices needed
  The RMP ELM suppressed ITER baseline will show us the impact in partially detached vertical target situation – at the moment it is almost impossible to achieve ITER-like detached scenarios with RMP ELM suppression. A task at ITPA-DSOL formed to address this question.
  Advanced divertor concepts were not studied so far in RMP ELM suppressed regimes experimentally, hence firm extrapolation is difficult
  Initial assessment with field line tracing and EMC3-EIRENE modeling shows higher fidelity effects – flux expansion “cures” some 3D effects
  Plasma response was not considered and no experimental basis exists to align with reality – that’s a glaring gap for research on divertor concepts beyond ITER

## Slide 2: Questions
Questions, which needs to be answered for ITER:
  Do we need rotation of RMP fields to protect divertor or is detachment and RMPs compatible with each other?
  How to approach detached discharges with RMPs? Are the results from DIII-D and ASDEX Upgrade concerning plasma response different?
  What about mitigated ELMs scenarios?
  How to determine the plasma response fields?
    Does this change between attached and detached states?
    Does this change from ELMy to ELM mitigates/suppressed states?
Questions beyond ITER
  How to approach RMP scenarios for DEMO?
    Plasma equilibrium defined by fully non-inductive plasma current?
    How to test RMP scenarios with X-divertor
    Is there a concept for ELM suppression with RMP coils for DEMO?