## Slide 1: 3s
Implementation of safety, security and safeguards in the Finnish Encapsulation plant and Geological repository project from the operator's perspective Mari Lahti and Sanna Mustonen, Posiva Oy

## Slide 2: Disposal facility complex
Encapsulation plant and other site buildings
Access tunnel
Shafts for ventilation, personnel entrance and disposal canister transfers
Repository (deposition tunnels)
Technical rooms, incl. disposal canister receiving station and buffer storage
Transfer from Olkiluoto NPP site (2 km)
Transport from Loviisa NPP site (350 km)
Above ground encapsulation plant and underground geological repository
2001
2025
PLANNED START OF OPERATION
SITE SELECTION
2015
CONSTRUCTION LICENSE
ONKALO EXCAVATIONS STARTED
2004
2019
CONSTRUCTION OF ENCAPSULATION PLANT
Access routes to underground
450 m

## Slide 3: Defining safeguards relevant design information
Safeguards implementation started in parallel with the excavations at the site
  documentation and reporting of progress of underground tunnels
  demonstrating absence of undeclared activities at the site
What safeguards relevant design information consists of regarding the geological repository
  geological features, underground openings, infrastructure?
2025
PLANNED START OF OPERATION
SITE SELECTION
2015
CONSTRUCTION LICENSE
ONKALO EXCAVATIONS STARTED
2004
2019
CONSTRUCTION OF ENCAPSULATION PLANT
2001

## Slide 4: Common use of operator data
Responsibility of the safety, physical protection and control of nuclear materials in the facility lies with the operator
Facilities will include systems to control the processes and monitor the repository site
    process cameras
    radiation monitoring
    seismic monitoring
    hydrogeological monitoring
These measures can be used to demonstrate that
    radioactive materials are transferred and stored only at their intended locations
    underground premises are constructed as declared
    any other works that could compromise the integrity of the geological containment are excluded
The possibilities to share process data by signal splitting and authentication could be further studied in cases that would benefit both the regulator and the operator
Information security questions to be considered

## Slide 5: Excavations detected by seismic monitoring

## Slide 6: Interaction in safeguards infrastructure planning
Development of the safeguards measures for the new type of facilities has benefited from interactive communication
  comprehending what is safeguards relevant design information
  communicating design changes
  understanding intended operation of the facilities
  influencing the choice of safeguards measures considering the operational perspective
Integration of the safeguards instrumentation into the facility structures in around 2023, when the commissioning tests are planned to commence
2025
PLANNED START OF OPERATION
SITE SELECTION
2015
CONSTRUCTION LICENSE
ONKALO EXCAVATIONS STARTED
2004
2019
CONSTRUCTION OF ENCAPSULATION PLANT
2001
INTEGRATION OF SAFEGUARDS EQUIPMENT
SAFEGUARDS BY DESIGN
REPORTING OF CONSTRUCTION ACTIVITIES

## Slide 7
Thank you