## Slide 1: New Safeguards Tools for Research Reactors
Mark W. Goodman,1 D Lockwood,2 J.S. Adams,1 B.D. Reid3
Presented at IAEA Safeguards Symposium
Vienna, 6 November 2018
1U.S. Department of State
2U.S. National Nuclear Security Administration
3Pacific Northwest National Laboratory

## Slide 2: Background
History of Misuse
  Research Reactors involved in every case of reported safeguards non-compliance: Iraq (1991), Romania (1992), DPRK (1993), Libya (2004), Iran (2006), Syria (2011)
  Small quantities of nuclear material involved
  Safeguards measures failed to deter misuse
Safeguards Relevant Characteristics
  Fuel Type: HEU, LEU, natural U
  Power and Cooling Capability: Capacity for Pu production
  Potential for Target Irradiation: Space and excess reactivity
  Transfers of Irradiated Nuclear Material
  Access to Hot Cells

## Slide 3: Safeguards Framework
Current Safeguards Approaches
  Two main objectives:
    Detecting diversion of 1 SQ of direct use material
    Detecting undeclared production within a single year of 1 SQ of direct use material
  Standard Suite of Safeguard Measures: Examine reports/records, Inventory verification (NDA/counting), DIV, C/S, Environmental sampling
Acquisition Path Analysis/Generic High-Priority Paths:
  Divert 1 SQ fresh HEU fuel, convert to metal
  Divert 1 SQ irradiated HEU fuel, recover in hot cell, convert
  Divert irradiated natural U fuel, recover 1 SQ Pu, convert
  Fabricate natural U targets, irradiate, recover 1 SQ Pu, convert
Relation to State’s fuel cycle capabilities

## Slide 4: Candidate Safeguards Measures: Hafnium coupons
Undeclared irradiation would affect the power level/profile and the neutron flux/profile
Hafnium isotopes function as neutron fluence “odometer”
  Hf “coupons” could be placed to monitor fluence profile across the core
  Needed quantity of Hf is very small

## Slide 5: Candidate SG Measures: Environmental/Waste Sampling
Undeclared reprocessing could leave signatures in multiple locations:
  Hot cells
  Analytical labs
  Waste tanks (rarely disposed)
Sampling waste is costly/intrusive
  Use selectively, to resolve other indicators
  Sampling from ventilation pipes can detect Pu-240 fission products and infer Pu mass

## Slide 6: Candidate Safeguards Measures: Mailbox Declarations
Purpose: Identify anomalous operations and movements of nuclear material (fuel/targets)
Concept: Regular declaration of relevant data:
  Reactor operations
  Isotope production
  Movement of fuel
  Movement of shielded containers
IAEA right to verify declared information
  IAEA may use machine learning to detect patterns of normal and abnormal operation

## Slide 7: QUESTIONS? COMMENTS DISCUSSION