## Slide 1
R&D on NDA Techniques for Nuclear Safeguards and Security within the JAEA-JRC Partnership in Ispra
K. ABBAS, J.M. Crochemore, T. Bogucarska, B. Pedersen, S. Nonneman
European Commission, Joint Research Centre, Directorate for Nuclear Safety and Security, Nuclear Security Unit, Via Enrico Fermi 2749, 21027 Ispra (VA), Italy
kamel.abbas@ec.europa.eu
D.C. RODRIGUEZ, F. ROSSI, T. Takahashi, M. Seya, M. Koizumi
Integrated Support Center for Nuclear Nonproliferation and Nuclear Security, Japan Atomic Energy Agency, Shirakata Shirane 2-4, Tokai, Naka, Ibaraki, Japan
Vienna, November 5-8, 2018

## Slide 2
Contents
  -
  -
R&D infrastructure and capabilities at the JRC Ispra site
Preliminary results on the development of an innovative NDA technique for nuclear safeguards and security under JAEA–JRC collaboration ()
  JAEA-JRC Collaboration
  JAEA Delayed Gamma Spectrometry experimental set-up being tested in PERLA
  Preliminary results
  Conclusion
see also the paper 153 of this symposium!

## Slide 3
DG Energy
DG Mobility and Transport
DG Agriculture and Rural Affairs
DG Climate Action
President Jean-Claude Juncker
27 Commission Members
Joint Research Centre (JRC)
DG Education and Culture
DG Environment
Commissioner Tibor Navracsics
Education, Culture, Youth and Sport
…
The JRC in the Commission
JRC Director-General
Vladimir Šucha
Notes: 3

## Slide 4
  PERLA Facilities
Neutron detection material alternative to 3He
Development and testing of neutron and gamma detector including the associated electronic
Development of method for characterization of fresh and spent fuel
Validation of instruments and methods for nuclear decommissioning and waste management (ND&WM)
Capacity building in imaging techniques such as gamma cameras
Building a pilot experiment for tomography of waste as a support to the JRC ND&WM programme
Calorimetry for safeguards
Support to EURATOM in terms of R&D such as development of a dedicated instrument for fresh MTR fuel verification.
  R&D in ESSOR Area
Part 1
  Infrastructure and capabilities in Ispra

## Slide 5
  PERLA Facilities
FIG. 1: View of a side of PERLA (Ispra, Iatly)

## Slide 6
6
A facility for Research in NDA methods and instrumentation For applications in nuclear safeguards and security
Nuclear Safeguards:
Mass determination of small quantities of fissile material
Method: Differential Die-Away technique with neutron correlation analysis
Applications: e.g. nuclear waste assay
Nuclear Security:
Detection of special nuclear material (SNM) in shielded containers.
Method: detection of fission signatures
Application: e.g. air cargo containers (ULDs)
Pulsed Neutron Interrogation Test Assembly - PUNITA

## Slide 7
Features
• sample cavity: 50 cm x 50 cm x 80 cm
• thick graphite linear on all six side
• fission neutron counters: He-3 in polyethylene
• low pressure, thermal flux monitors
• monitor for neutron generator output
• HPGe, LaBr3, scintillators in cavity
side view
top view
Pulsed Neutron Interrogation Test Assembly - PUNITA
14-MeV neutron generator: MF Physics Model A-211
neutron emission
2108 /s, 106/burst in 4π angle
sealed, D-T mixed beam
300-500 hours life
pulsing of ion source and acceleration voltage
no emission between bursts
neutron burst width: 10 µs
burst repetition rate: 1 – 150 s-1

## Slide 8
Development of standards for decommissioning and environmental remediation
Perform Research & Development for site characterisation in view of waste minimisation
Development of new characterisation methods of waste (NDA and imaging) Application of safeguards verification technologies & methodologies based on laser verification in nuclear decommissioning and waste management
Innovative Techniques/Technologies and Standardisation of Practices in Decommissioning (ITSP)

## Slide 9: NDADecomm
Tomography of waste drums in the characterisation/clearance stage

## Slide 10
Part 2
  JAEA-JRC Collaboration
JAEA ISCN Active Neutron Nondestructive Assay Program
in collaboration with EC JRC
(Neutron) Differential Die-away Analysis (DDA) | Neutron Resonance Transmission Analysis (NRTA) | Prompt Gamma-ray Analysis (PGA/NRCA) | Delayed Gamma-ray Spectroscopy (DGS)
239Pueff Fissile Mass | Nuclide Content | Matrix Materials | Fissile Nuclide Ratio
JRC-Ispra (PUNITA) | JRC-Geel (GELINA) | JRC-Geel (GELINA) | JRC-Ispra (PUNITA/PERLA)

## Slide 11
Part 2
  JAEA-JRC Collaboration
  Test of DGS technique in PERLA

## Slide 12
  JAEA DGS experimental set-up being tested in PERLA
  Application DGS technique
  Preliminary system using Cf-252 as a surrogate for a pulsed neutron generator
The remote operation of the system is considered

## Slide 13
  System installed in PERLA
Static measurement configuration: the sample remains fixed in front of the detector and the neutron irradiation position

## Slide 14
  Some fission products considered for DGS
Nuclide | Half-life (min) | Gamma-ray (keV) | Branching ratio (%)
89Kr | 3.2 | 3533 2866 1533 | 1.4 2 5
90Rb | 2.6 | 3383 4366 4646 | 7 8 2.2
90mRb | 4.3 | 3317 3503 1739 | 14.3 2.4 1;9
136I | 1.9 | 2869 2634 2289 | 4 6.7 10
99mNb | 2.5 | 2641 2851 2134 | 4 3 1
138Cs | 33.4 | 2639 2218 1436 | 7.6 15 76
91Rb | 1 | 2563 3600 1971 4265 | 12.6 10.4 6.7 1.4
Nuclide | Half-life (min) | Gamma-ray (keV) | Branching ratio (%)
106Tc | 0.6 | 2238 1968 2789 3186 3258 | 13.6 8.9 7.9 5 2.7
136Te | 0.3 | 2078 2569 3050 | 22.4 15.4 2.1
95Y | 10.3 | 2175 3575 2631 954 | 7 6.4 4.8 15.8
95Sr | 0.4 | 2718 2933 2248 | 4.6 4.1 3.8
90Kr | 0.5 | 1780 1538 1119 | 6.7 9.7 39
134Te | 42 | 2077 2569 3049 2497 | 22.4 14.4 2 4.9
138Xe | 14 | 1767 2016 2251 | 16.7 12.3 2.3

## Slide 15
  Gamma background measurement
  Preliminary Results
  Part 2
The DGS spectra with 50-MBq during irradiation (red) and during measurement (black).
A high gamma background from system activation and insufficient fission rate is preventing visibility of the gamma-ray peaks of interest!
Count
Prompt gammas from Fe-56 activation

## Slide 16: Investigation of a stand alone HDPE moderator to test improvements of the fission rate
Front view
NM sample
Overhead view
Cf-252 source

## Slide 17
Gamma ray spectrum of an enriched (4.5%) uranium sample (200 g total U mass) showing well resolved delayed gamma ray peaks (>2.5 MeV). The upper spectrum is of the 252Cf irradiated uranium sample while the lower is of the sample prior to its 252Cf irradiation.

## Slide 18
Energy range (3 – 3.8 MeV) of the gamma spectrum showing well resolved delayed gamma-ray peaks

## Slide 19
Gamma-ray spectra of a 4.5% enriched uranium sample irradiated
with 252Cf in PERLA
with a D-T generator in PUNITA (K
The gamma-ray peaks of interest are well resolved!

## Slide 20
Conclusion
  Preliminary Results on the Application of DGS as an NDA technique for the Characterisation on NM are promising!
      Fissions of LEU samples irradiated with a 252Cf source (10MBq) are observed
      Gamma ray peaks at high energy (>2.5 MeV) are well resolved despite a substantial background
      Improvement of the experimental set-up supported by MCNP modelling is ongoing
      The high energy resolution gamma detector requires to be strongly shielded to prevent detection of a variable background of the measurement environment
      The fine tuning of the 252Cf irradiator of the JAEA DGS system including its neutron moderator is on-going thanks to the extensive MNCP modelling input and the exploration of new neutron flux characterisation at key position of the DGS system
      Further experimentation with both U and Pu samples are planned

## Slide 21
Thank you for your attention!
  kamel.abbas@ec.europa.eu