## Slide 1
Algeria has fully supported the implementation of safeguards, as required
by its Comprehensive Safeguards Agreement (CSA) with the IAEA since
1996 INFCIRC 531 [1] . The Atomic Energy Commission (COMENA) is designated as the competent authority for the implementation of this agreement, indeed COMENA is responsible for Safety, Security and Safeguards. The control and the accountancy of nuclear material is part of the requirements of the CSA, COMENA periodically holds, through its State System of Accounting for and Control (SSAC) [2], an exhaustive inventory of its materials and record changes in that inventory between inventory periods. COMENA has established the Safeguards Laboratory (SGL) as a technical support structure, which provides technical capabilities to SSAC, through the put in place and application of non-destructive assay (NDA) techniques related to the activities of inspections, verification and control of nuclear materials.
ABSTRACT
For consolidation and updating the national inventory of nuclear materials used outside the fuel cycle, several campaigns of verification and control are undertaken throughout the national territory . Challenges and difficulties are encountered during field inspection for companies located in south of Algeria. More time to do a real physical inventory verification (PIV) for device with Depleted Uranium and radiological sources information, usually Illegible nameplate (mass of DU), absence of documents for old device and no record keeping, sometimes the weights of the DU declared by the users are wrong, a possible correction of the mass requires investigation by using international catalog of sealed radioactive sources (IAEA website and suppliers). Sometimes the measurement is difficult at the field, in this issue the item (device) will be transferred to the safeguards laboratory for advanced gamma spectrometry analyzes.
INSPECTIONS
Conducting inspections at level, nuclear facilities and location out facility (LOF) is different relative to, the size of facilities, type and status of the nuclear material and the activities. The conduct of national inspections is limited at the fresh fuel material balance areas for two research reactors, and at LOFs. Activities of inspections require the use of non-destructive assay technologies and inspection methods and plan. nuclear material covered by LOF is essentially depleted uranium used as shielding in gammagraphie equipments. Those equipment are used by the various operators (company), public and private socio-economic sector and in particular by those operating in the hydrocarbons sector for non-destructive testing activities and medical fields (hospitals).
Several companies are widespread on the national territory (North, South, East, and West) Fig. 1 and each of them present one key measurement point (KMP).
In order to perform material analysis, including identification, characterization and verification measurement of enrichment uranium 235U [3] at the field and at laboratory level, SGL staff and national inspectors use portable radiation detection system, using the NDA techniques which include low and high resolution gamma spectroscopy system, as Sodium Iodine detector (NaI), High Purity Germanium detector (Hp-Ge), Hand-held radiation detection systems (HM-5) and Cadmium Zinc Telluride detector (Cd-ZnTe).
These analyses are approved based on and on the methods of measurement and the use of certified reference materials SRM969 [4] .
EXPERIENCE, DIFICULTIES AND CHALLENGES
TFIG.2. Correction mass of location out facility (LOF)
The requirements for sustaining the durability of the system are, to increase the inspection frequency, strengthening the capabilities of the inspector in the field and improve detection performance in the field. Satisfactory results have been achieved following the efforts and investigations provided by the national inspectors with the help of the safeguard laboratory (SGL). Correction of seven percent of total mass initially declared is represented by false declaration of the users.
CONCLUSION
FIG. 1. KMPs distribution map trough the national territory
ID: 15
[1] Agreement between People’s Democratic Republic of Algeria and the International Atomic Energy Agency for the application of safeguards in connection with the treaty on the non-proliferation of nuclear weapons.
[2] The structure and content of agreements between the Agency and states required in connection with the Treaty on the Non-proliferation on nuclear weapons.
[3] ASTM c1514-02, Standard Test Method for Measurement of 235U Fraction using the Enrichment Meter Principle, 2007.
[4] National Bureau of Standards Certificate, Standard Reference Material 969, Uranium Isotopic reference material for gamma spectrometry measurements, Gaithersburg, MD 20899, October 1985.
REFERENCES
PURPOSE
KMPs/Companies
People's Democratic Republic of Algeria
Area: 2381741 km²
Algeria shares more than 6,385 km of land borders, with several countries
Several KMPs (companies) Different sectors: industry & health
DISCUSION
Most of the KMPs were checked during the years 2013-2014, where the frequency of inspection was maximum, many factors influence the activity of inspection like, the mobility of the equipment, the region climatic factor (temperature, sand wind ...), and the adequate logistic means to ensure an effective inspection.
The results of those inspections and verification of the equipment subject to safeguards gives the correction of 7% of the LOF balance initially declared (Fig.2).
STRENGTHENING SSAC CAPABILITIES THROUGH THE
ESTABLISHMENT OF A SAFEGUARDS LABORATORY (SGL)
Zaghouane Rabah, Benbouzid Sofiane, Bounatiro Saleha, Sehad Smail
Algerian Atomic Energy Commission (COMENA)
r.zaghouane@comena-dz.org
ID: 15