## Slide 1: Muography of spent fuel containers for safeguards purposes
A feasibility test in proximity of a CASTOR® container.
Muon radio/tomography is a technology candidate to verify the content of spent fuel containers without opening them
Detectors positioned around the container  Absorption, Transmission and multiple Coulomb scattering
Simulation Results

## Slide 2: A radioactive environment
How much does radioactivity emitted by nuclear material stored inside Canisters interfere with the detector response?
Is the (low) cosmic-ray intensity (~.1 mSv/h) compatible with the noise induced by radioactivity?
Purpose of the test is to prove that it is possible to record muon tracks and to measure the effects induced by radioactivity
A small prototype: 8 layers of 8 Al tubes:
50 mm diameter, 1.5 mm thickness, 2 m length, central 100 mm anode wire (+3000 V),
Ar-CO2 (85%-15%) gas mixture
realized by INFN Padova group
~0.60 m
~0.50 m
~2 m

## Slide 3: Field test in nuclear power station at Neckarwestheim
Two positions for data taking
Far (~no radioactivity)
Near CASTOR® ~14mSv/h g
Main result: it is possible to reconstruct muon tracks with very little additional background:
Probability for a tube to have a hit in coincidence with a muon <1%
Layout of the apparatus.
Display of reconstructed muon tracks.

## Slide 4: Field test in nuclear power station at Neckarwestheim
The test was not conceived to study the CASTOR® content but we can show the influence of the container to modify the muon flux
Azimuthal angle distribution, superimposed to the hall map sketch, for the far (blue) and near (red) data.
The flux reduction in correspondence of CASTOR® is evident.
Elevation angle distribution: effects of the geological environment and of CASTOR® presence. The blue area and the red curve are normalized to the total number of entries of the corresponding data-taking.

## Slide 5: Conclusions and future perspective
The technique works: it is possible to study CASTOR content using cosmic muons measured with a gas drift detector
Given the test positive results: next step is to realize a prototype covering a large fraction of a spent fuel container

## Slide 6: Backup slides

## Slide 7: The detector for a test
commissioning
construction
ready

## Slide 8: A possible detector
Drift tubes technique is adequate for industrial production
A charged particle crossing the tube ionizes the gas
(e.g. Ar 85% CO2 15%)
Electrons drift in presence of the electric field and in proximity of the wire (E~1/r) an avalanche process starts allowing signal detection
- - - -
++++
Typical drift time: ~1 ms for 2.5 cm
m+