## Slide 1
Feasibility Study of Advanced Solution Measurement
and Monitoring Technology for Reprocessing Facility
Based on IAEA R&D plan (STR-385), as a feasibility study, we developed a new detector to enable real–time flow monitoring of Pu in solutions with numerous fission products (FP) for entire reprocessing facilities as part of an advanced approach to effective and efficient safeguards.
There is a possibility to monitor the change of Pu amount in solution by combination of gamma-ray and neutron measurements. The results suggest the applicability and capability of Pu monitoring.
ABSTRACT
RADIATION MEASUREMENT AND MCNP MODEL
INTRODUCTION / METHOD
Pu monitoring capability
Possible to monitor the difference of Pu amount using neutron count rate and to estimate the Pu quantity with MCNP simulation in a static configuration where the Pu concentration and Pu/Cm are constant and only HALW volume changes. The measured neutron count rates increased linearly as a function of Pu mass decreasing for constant Pu/Cm ratio and Pu concentration. Neutron count rates are in proportion to a function of analytical value of Cm.
Operational status and sludge monitoring capability
The results using the IC showed the possibility of using this Pu monitoring capability to confirm the operational status including pulsation as well as sludge movements. These results can be used not only for Pu monitoring technology but also one of decommissioning technique.
RESULTS
Megumi Sekine1,* , Takuya Matsuki1, Satoshi Suzuki1,3 , Koichi Tsutagi1, Hirofumi Tomikawa1, Hironobu Nakamura1, Adrienne LaFleur2, Michael Browne2
1 Japan Atomic Energy Agency, 2 Los Alamos National Laboratory, 3 E&E Techno Service Co.,Ltd
* Email : sekine.megumi@jaea.go.jp
ID: 74
We would like to acknowledge MEXT of the Japanese government and the DOE/NNSA for supporting this work. We also would like to acknowledge the FRS at Nuclear science research institute, analysis section of TRP and CAD team at Nuclear Fuel Cycle Engineering Laboratories of JAEA.
ACKNOWLEDGEMENTS
The technology to monitor Pu in solution directly after a purification process were already developed.
To further improve the effectiveness of safeguards activities, a new detector to enable monitoring of Pu in solutions with numerous fission products (FPs) was developed.
Steps of this technology development
High Active Liquid Waste storage at Tokai Reprocessing Plant
Typical composition
Major nuclides and radiation of HALW
MOCK-UP TEST
CONCLUSION
MCNP
MODEL
Guide rail B
FRP rod
Inspection hole
IC holder
Before we performed radiation measurement at the actual HALW tank, we had mock-up test for safe measurement.
Mock-up test equipment
Rail and guide rings
Inside of guide tube
HALW tank
The good consistency among source, model and measurement in the MCNP model was confirmed.
Establishment of detailed MCNP model, and implementation of MCNP simulations changing liquid level and concentration.
Neutron count rate at the other tanks (V31, V33, V34) which have different HALW compositions.
Pu masses, 4 different tank levels and concentration were simulated in MCNP.
The pulsation operates every 6 mins. When we sset the IC the change of the gamma dose rate with timing of the pulsation was observed.