## Slide 1: Core Density Peaking Experiments in JET, DIII-D and C-Mod in Various Operational Scenarios  Driven by Fueling or Transport?
Tuomas Tala

## Slide 2: Core Density Peaking Experiments in JET, DIII-D and C-Mod in Various Operational Scenarios  Driven by Fuelling or Transport?
T. Tala1, S. Mordijck2, H. Nordman3, A. Salmi1, C. Bourdelle4, J. Citrin5, A. Czarnecka6, F. Eriksson3, E. Fransson3, C. Giroud7, J. Hillesheim7, A. Hubbard8, J.W. Hughes8, C. Maggi7, P. Mantica9, A. Marioni9, M. Maslov7, G. McKee10, L. Meneses11, S. Menmuir7, V. Naulin12, M. Oberparleiter3, C. Petty13, T. Rhodes14, G. Sips15, A. Skyman3, D. Tegnered3, M. Tsalas16, E. Tolman8, H. Weisen17 and JET contributors*
1VTT, P.O. Box 1000, FI-02044 VTT, Espoo, Finland
2The College of William and Mary, Williamsburg, 23187, USA
3Chalmers University of Technology, Göteborg, Sweden
4CEA, IRFM, F-13108 Saint-Paul-lez-Durance, France
5DIFFER, Eindhoven, Netherlands
6IPPLM, Warsaw, Poland
7CCFE, Culham Science Centre, Abingdon, OX14 3DB, UK
8MIT Plasma Science and Fusion Center, Cambridge, MA, USA
9Istituto di Fisica del Plasma, via Cozzi 53, Milano, Italy
10University of Wisconsin – Madison, Madison, USA
11Instituto de Plasmas e Fusão Nuclear, IST, Lisbon, Portugal
12Danish Technical University Physics, Lyngby, Denmark
13General Atomics, San Diego, USA
14University of California, Los Angeles, USA
15Commission, Brussels, Belgium
16ITER Organisation, Cadarache, France
17CRPP, Lausanne, Switzerland
*See the author list of X. Litaudon et al (2017), Nucl. Fusion 57 102001.

## Slide 3: Do We Understand Where Core Density Peaking is Coming from?
High density in the core is desirable for fusion
Previous works [1-5] have identified strong dependency between density peaking and collisionality υ* or υeff
  Multi-machine steady state databases
  Theory + GK modelling have identified mechanisms
In this talk, we will clarify what is still missing:
  Origin of the peaking (transport versus fueling)
    Linear regression limited to database averages
  Test of models against dedicated υ* scans
This is the first time when electron particle transport coefficients in H-mode have been measured in tokamaks with high resolution diagnostics yielding a unique dataset
Angioni, NF 2007
Dimensionless nu* scans
[1] H. Weisen, PPCF 2006
[2] C. Angioni, NF 2007
[3] M. Greenwald, NF 2007
[4] M. Valovic PPCF 2004
[5] L. Garzotti, NF 2006
ITER

## Slide 4: Gas Puff Modulation Experiment to Obtain Electron Particle Diffusivity D and Convection v
Gas puff modulation at 2-4Hz frequency at the top of the vessel
Both high resolution Thomson Scattering and density profile reflectometry diagnostics to follow the propagating density wave
Modulation amplitudes of the order of 1% in the core measured
Using perturbative approach, and linearization and some algebra, we will obtain the electron particle transport coefficients D and v
Core
Edge
Density

## Slide 5: The Experimental Set-up for the 3-point ʋ* Scans ̶ the DIII-D Scan Here as an Example
Collisionality scan is obtained by changing NBI power, torque and fueling
Dimensionless parameters matched typically to within 10% both in DIII-D and JET
Change in ʋ* in each scan a factor of 5-6
Excellent dataset for code validation
Time (s)
(low υ*) (middle υ*)
(high υ*)
Analysis window
Mach
β
ʋ*
ρ*

## Slide 6
Five Separate Dimensionless ʋ* Scans Performed in Total on JET and DIII-D ̶
Density Peaking Increases with Decreasing ʋ* in All H-mode Scenarios
Baseline ELMy H-mode
Hybrid-like scenario
L-mode plasma
(low υ*) (middle υ*)
(high υ*)
DIII-D
ELMy H-mode in Hydrogen
How does I-mode
on C-Mod compare?

## Slide 7
Inward Pinch Increases with Decreasing υ*
Particle transport coefficients are higher on DIII-D than on JET
Higher transport coefficients on DIII-D due to larger plasma volume and higher NBI power density and ECH consequences on the origin of the density peaking
Lowest υ* discharge on DIII-D jumps off the scan
Averaged over ρ=[0.5,0.8]
DIII-D:
JET:

## Slide 8: Beam Emission Spectroscopy (BES) Data Suggests an Increase in ITG at low υ* – Indicative of Increase in the Inward Thermo-Diffusion Pinch
Low-k fluctuations ) increase moderately with lower collisionality
[%]
Higher k fluctuations ) decrease moderately with lower υ*
Beam Emission Spectroscopy (BES), ITG range
Doppler Back Scattering (DBS)

## Slide 9
NBI Fueling Contributes around 50-70% to the Density Peaking in JET H-mode Plasmas
PF due to NBI source
PF due to inward pinch
The experimental D and V show that the contribution of NBI fueling to ne peaking is 50-70% in the ELMy H-mode scan in JET
This fraction is independent of υ*
In this parameter regime (3-point υ* scan) at q95=5, Ti/Te=1, βN=1.4, ρ∗=0.003 and υ*=[0.1,0.5], the NBI fueling is dominant
Core density peaking factor

## Slide 10
On DIII-D, Density Peaking from NBI is 15-30%
PF due to NBI source
The experimental D and V show that the fraction of NBI fueling is 15-30% on DIII-D
This fraction decreases with decreasing υ*
Clearly JET and DIII-D are different wrt density peaking. Why?
  NBI particle source – no, DIII-D source stronger
  Transport – yes, Trapped Electron modes (TEM) stronger than in JET, JET is deeply ITG dominated
  Diffusion larger on DIII-D than on JET, JET has larger confinement time, thus the source stays in the plasma way longer in JET
PF due to inward pinch
Core density peaking factor

## Slide 11
Model and Code Validation ….

## Slide 12: GENE Simulations Predict Zero Peaking in JET H-mode, but Peaked Profiles in DIII-D H-mode Plasma in Agreement with Experiments
GENE [1] predicts flat or even hollow (at high υ*) density profiles, implying that the NBI particle source dominates in contributing to density peaking.
JET
DIII-D
GENE in agreement with “transport versus fueling” contributions to the density peaking.
[1] F. Jenko, PoP 2000

## Slide 13: Non-linear GENE Simulation Predict Zero Peaking in JET H-mode – Stand-alone TGLF Runs in Good Agreement against the DIII-D υ* Scan
Non-linear GENE predicts also flat density profile in JET, suggesting that the NBI particle source dominates in contributing to density peaking.
JET
DIII-D
Stand-alone TGLF predicts the peaking factor in agreement with experimental density peaking
Particle flux

## Slide 14: TGLF Modelling of the JET υ* Scan in H-mode – NBI Source Contributes to Density Peaking at 50-90% Fraction
TGLF [1] peaking factor from NBI source using the JINTRAC transport code [2]:
  Low υ*: 47%
  High υ*: 90%
TGLF predicts similar results for Hybrid and ELMy H-mode in Hydrogen 3-point υ* scans
In L-mode, NBI source less important ~10%
TGLF performs well against JET discharges for each υ*
[1] G. Staebler, PoP 2005
[2] M. Romanelli, Plasma and Fusion Research 2014
Low υ*
Low υ*
High υ*
High υ*

## Slide 15: Predictive Capability of TGLF Is Good in DIII-D Provided That Ti Is Predicted Well
TGLF predictions for the high υ* case in agreement with experiment
TGLF does not predict the flat Ti profile at ρ=0.5-0.8 for the low υ* case
  Leads to an overestimation of NBI contribution
Predictive capability of TGLF is fairly good in JET and DIII-D υ* scans except for the low υ* case on DIII-D
Low υ*
Low υ*
High υ*
High υ*

## Slide 16
TGLF Simulations Reproduce the Experimental Peaking Factors When the Temperature Predictions Are in Agreement
TGLF simulations are in agreement with experimental peaking factors only when the predicted Ti and Te profiles are in agreement with experimental ones
This is also seen in stand-alone TGLF simulations
What happens at lower υ* in JET?
  Does NBI fueling lose its dominance to inward pinch?
TGLF with experimental Te and Ti
DIII-D TGLF
DIII-D Exp
Core density peaking factor
JET exp and TGLF

## Slide 17: Predictive Transport Modelling Can Reproduce the Lowest υ* JET Discharges
TGLF reproduces density peaking in low density JET hybrid plasma
Simulation without fueling suggests ~50% NBI contribution as in the H-mode υ* scan
Exp. TGLF
Ti
Te
Te
Ne
Ne
Ti
ICRH only
>20MW NBI
NBI source=0
TGLF captures density peaking with ICRH only
  Very low density + 8MW of ICRH
GENE also predicts density peaking correctly
Revisit database corners (no modulation)
ITER

## Slide 18: Density Peaking in non-Fuelled I-Mode Plasmas on C-Mod Are Similar with Respect to Core Density Peaking to Those of L-mode in JET and DIII-D
The C-Mod discharges do not have NBI fueling – relevant information on the role of NBI fueling and I-mode particle transport is a special case with no density pedestal
L-mode plasmas have different q-profile and Te/Ti ratio and thus, density peaking originating from different reasons
In line with the JET and DIII-D L-mode results, i.e. the I-mode core density peaking does not have any υ* dependence.
Gas puff modulation was also performed on C-Mod, but the modulated density data is too noisy to able to extract the particle transport coefficients.
low υ*
middle υ*
high υ*
Core density peaking factor

## Slide 19: Conclusions: Core Density Peaking – Driven by Fueling or Transport?
JET is NBI source dominant 50-70% and DIII-D transport dominant (only 15-30% from NBI)
  Trapped Electron modes (TEM) play a stronger role than in JET (JET is deeply ITG dominated)
  Lower υ*, higher magnetic shear, larger R/LTe and higher β in DIII-D than in JET
  JET has larger confinement time than DIII-D, thus the source stays in the plasma way longer in JET
Validation of TGLF and GENE against the unique experimental particle transport dataset:
  TGLF quite convincing against various experimental results provided that Ti predicted accurately enough
  GENE qualitatively agreeing well with various experimental trends, underestimates the pinch at Te/Ti~1
Density peaking (also in future devices) depends critically on the parameter regime, such as υ*, Te/Ti, LTe/LTi, β and q-profile
I-mode particle transport characteristics (core density peaking) are similar to those of L-mode in JET and DIII-D

## Slide 20: Particle balance transport coefficients from the experiment in 2 steps
Collisionality scan is also a density gradient scan thus providing . Integration yields [1]:
Use perturbative approach is to obtain absolute values for the transport (takes the code validation to the next level)
  Standard approach is to linearize using the ansatz:
Edge
Core
Steady state (1 eq 2 unknowns):
Inside rho<0.8
and from Fourier transformed
Step 1:
Step 2:

## Slide 21: Various Analysis Techniques Employed to Obtain the Particle Transport Coefficients
JET H-mode plasma shot #87420
Density evolution:
In steady state:
To disentangle transport from the source perturbative approach is needed
  Use ansatz:
  After some algebra [1]:
[1] H Takenaga et al 1998 PPCF 40 183
in JET
in DIII-D

## Slide 22
165303
165325
165318
Similar 3-Point υ* Scan Performed on DIII-D –
And Density Peaking Increases with Decreasing υ* as in JET

## Slide 25: C-Mod: Gas Puff Modulates Density in I-mode at 5.6T

## Slide 26: No Evidence on Time-Dependent Plasma Background from Fluctuations at 3Hz
No effect of gas puff modulation on fluctuation level from the correlation reflectometry
The assumption of the time independent background seems justified

## Slide 27: TGLF Simulation around the Operational Parameters of the JET ʋ* Scan