## Slide 1
Institute of Advanced Energy, Kyoto University
Sustainable Future Energy Scenarios and Possibility of Fusion
Oct.26, 2018
Mahatma Mandir Convention and Exhibition Center, Gujarat, India
27th IAEA Fusion Energy Conference
Satoshi Konishi： SEE/3-1Ra FUTURE POSSIBILITY OF CARBON SEQUESTRATION BY “Emission Credit” BIOMASS FUSION HYBRID SYSTEMS
Shutaro Takeda : SEE/3-1Rb ECONOMIC PERFORMANCE OF FUSION POWER PLANT ON “Future Electricity” FUTURE DEREGULATED ELECTRICITY MARKET
Nam Hoseok : SEE/3-1Rb TECHNO-ECONOMIC ANALYSIS OF DIESEL AND HYDROGEN “Synthetic Fuel” PRODUCTION VIA FUSION BIOMASS HYBRID MODEL

## Slide 2
What should fusion do in the future energy?
1. Electricity
- Electricity Market is rapidly changing.
Large fraction of renewables, smaller grids in developing countries,
dispersed system, increased vulnerability, and deregulated market require:
increased demand response, less impact and effect of stabilizing grids
2. Fuel, Heat, Industrial
- Fuels to substitute fossil with less (zero) CO2 emission (hydrogen?)
- freights, aviation and heavy transport, residential and industrial fuels
3. Global environment and climate change issues
- Competition with nuclear and renewables does not reduce emission.
- Carbon Capture and Sequestration (CCS) for fossil combustion needed.
- No technology other than Bio-CCS can reduce CO2 (Negative emission).
Introduction

## Slide 3
What CAN fusion do in the future energy market?
…we have to know the market and maximize the chance of fusion
1. Electricity SEE/3-1Rb Takeda The Economic Performance of Fusion Power Plant on
Future Deregulated Electricity Market
- Electricity price varies by bidding market.
- Fusion will sell in forward market and balancing market.
responding power highly evaluated/unplanned outage penalty
2. Fuel, Heat, Industrial SEE/3-1Rc Nam Techno-economic analysis of diesel and
hydrogen production via Fusion-Biomass Hybrid Model
- Fusion heat used for conversion of biomass to hydrogen or carbon-free diesel
- freights, aviation and heavy transport, residential and industrial fuels
3. Global environment and climate change SEE/3-1Ra Konishi
Future Possibility of Carbon Sequestration by Biomas-Fusion Hybrid Systems
- Charcoal production by fusion heat for carbon stabilization from atmosphere
- Emission credit can be sold as energy product, other than electricity or fuel
- Fusion as an ultimate energy-environment solution since the industrial revolution
Introduction-2

## Slide 4
  Future low carbon electricity
Battery
Large scale grid
generators
Local systems
Solar cell
Nuclear
(??)
Both large grid and local systems are needed.
Fire
(fade out)
Fusion
(to come)
PHV,EV
Local generators and
fuel cells Stabilizes fluctuation by renewables.
Grids are smaller
unstable
not responding demands
Solar cell
0
5
10
15
20
25
2000
2020
2040
2060
2080
Year (IPCC92)
Electricity
Solid Fuel
Liquid Fuel
Gaseous Fuel
Energy demand(GTOE)
Fuel cells
SOFC
Already clean
Small energy devices available and preferred
Fuel demand
larger
renewables
(dominates?)

## Slide 5
California Independent
System OperatorCAISO)
Value of the electricity (even clean base load) can be negative.
→Fusion Electricity may not recover investments!
Value of the electricity (California duck)
In the deregulated market,
Price of electricity varies.
Due to large share of renewable,
electricity market price drops in
day time.
Fig. Change of electricity demand in a sunny day
Instability of grid (frequency
change and outage) is
Serious when share of
Renewable increased.

## Slide 6
economic competitions in future electricity markets
Fig. 2 PJM Real Time Energy Market Historical Value.
Modeled fusion power plant, 1.2GW steady
The electricity is no longer sold for per kWh -
conventional economic metrics like Levelised Cost of Electricity (LCOE) are inapplicable on future electricity markets!
Fig. 1 PJM Deregulated Market Structure.
economic performance of fusion power plants on future deregulated electricity markets was evaluated with PJM market model.
System Parameter | Value
Operation Mode | Steady-state
Electricity Output (sending-end) | 1,200 GW
– Major Radius | 7.728 m
– Minor Radius | 2.208 m
– Beta Value | 4.274
– Fusion Output | 2,801 MW
Frequency of Unplanned Plant Outage | 0.001 – 0.00001 hour-1
Service Time before Plasma Restart | 10 days
Bidding Market | Real-time or Day-ahead or Year-Forward

## Slide 7
Revenue of fusion power plants had higher sensitivity to the unplanned outage frequency on deregulated electricity markets.
The unplanned plant outage (including plasma disruption) frequency target should be lowered to < 0.3 times/year on deregulated electricity markets.
Fig. Net Present Value of Fusion Power Plant on Deregulated Electricity Market vs. Conventional Market.
Disruptions have large impact on the total value of fusion as a generator of base load electricity
Fusion electricity is sold in the bidding market
Under a long-term contract as a steady source.
Fusion electricity in the future electricity markets
1. Electricity Selling Revenue
2. Frequency Regulation Revenue
3. Start-up Electricity Expense
4. Imbalance Fee

## Slide 8
Chemistry of biomass fusion hybrid
cellulose：（C6H10O5）n/6+ n/6H2O → nH2 + nCO – 136n [kJ]
Biomass
(1kg)
+
H2O
External Heat，900℃
H2,CO
2H2 + CO → -CH2- + H2O + 160 [kJ]
Fischer-Tropsch reaction
CO + H2O ⇔ H2 + CO2 + 32 [kJ]
Shift Reaction
hydrogen
Carbon Neutral
Plasma 8.2MJ
Chemical 15.6MJ
Hydrogen 24.2MJ
Chemical 16MJ
Heat 8.1MJ
for generation
diesel(hydrocarbon)
Carbon free oil 0.5 liter
Sold in the market
Biomass gasification
Waste
Garbage
Agriculture
byproducts
forestry
Fusion
Reactor
Chemical Reactor
Notes: こちらが、それぞれセルロース、リグニンの代表的な元素組成のCHO比から想定される水蒸気と反応した理想的なガス化を示す式です。
一方、このときに起こると考えられる代表的な平行反応には。これらの反応式が示すようにメタンを生成する反応や、一酸化炭素と水蒸気から水素と二酸化炭素を生成するシフト反応があります。簡略化のために炭素２個以上の反応は考慮していません。
こちらが本研究で用いる、パラメータである水素生成率、炭素分解率の定義式です。水素生成率は、全ての反応が理想的に上式で起こったときの水素生成量を100%とし、実際の生成量より求めます。炭素分解率は、バイオマスのもつ炭素原子数が一酸化炭素、二酸化炭素、メタンの炭素ガスにどれぐらい分解されたかを示します。
(0:55)

## Slide 9
Fusion Energy Balance
◯Large energy gain Q (>20) needed for DEMO because of poor generation efficiency.
Net plant energy output(fuel)
Driver
Energy
Pd
Fusion reactor ( Pf=3GWt)
Energy Multiplication
fusion energy
Pd
Blanket
Output
Generation
Efficiency
η ~0.33
Conversion
Efficiency
η 2.0~2.7
○If fusion plant can produce more energy output by fuel production,
required energy multiplication Q could be as low as 5.
1GWe
6~8GWt
Q =
Electricity generation
Biomass fuel production
Waste heat

## Slide 10
High Plasma Q not required
18
10
10
22
10
21
10
20
10
19
1
10
100
ｎt
Ｔ（ｋｅｖ）
Break-even
Ｑ＝１，η＝１
Electricity
generation
Ｑ＝20，
ηe＝0.33
biofuel
Ｑ＝５，
ηｆ＝２．７
-0.6
Negative power
ITER
DEMO
Driven and pulsed operation is acceptable
Target easier than ITER.
Particularly suitable for Small tokamaks.
High output temperature is required for gasification efficiency is required
Biomass –fusion Hybrid
-~6
Net power
-~8
Net power
Low neutron/ Heat flux
Small reactors <1GWt are preferred.
In Lawson’s criteria, generation efficiency of 1/3 is unavoidable.
With energy utilization factor of 2~2.7, break even is lower.
Notes: In order to satisfy these criteria, we proposed the non-nuclear hybrid of Fuel production from biomass with fusion energy.
Dr. Konishi presented this concept 2 days ago.
The feature of hybrid enables small DEMO reactor with a low plasma large Q.
Driven and pulsed operation is acceptable because it does not supply electricity to grid.
Fuel production from biomass requires high temperature blanket for biomass gasification.

## Slide 11
Fusion
core
Turbine
Local
Electricity
Gasification reactor
H2+CO
Liquid
Fuel
Grid
Electricity
Fuel Cell
Fischer Tropsch process
Biomass
“apparent”
energy multiplication
Fuel Cell
fusion-Biofuel energy system
Start-up and
driving
No generation plant needed
Consumers install
Fuel cells respond to the demand change
-preferred for grid stability
Demand response
Stabilized the grids

## Slide 12
8.2 MJ/kg of endothermic heat is calculated to be required for the complete conversion to syngas.
Energy output reaches 105 % for diesel 108 % or hydrogen comparing to the biomass.
Conversion of waste biomass into diesel or hydrogen can be economically competitive
LHV: Low Heat Value
Parameter |  | Value
Feedstock * |  | 0 $/ton
* Feedstock price can be negative as abandoned biomass is collected and transported to this system paid by government tax or waste producers. |  | 
Carbon Capture and Storage |  | 43 $/tCO2
Fusion heat cost * |  | 27 $/MWhth
Thermal efficiency |  | 33%
Fusion reactor load factor |  | 80 %
Reference Biomass Plant | Total Capital Investment (TCI) | 503 Million$
 | Operating and Maintenance | 6% of TCI
 | Capacity | 1,000 ton/day
 | Operating years | 30 years
 | Income tax | 30 %
 | Discount rate | 10 %
 | Overall efficiency | 85 %
 | Availability | 7,880 hours
 | Depreciation | MACRS with a 7-year recovery period
* DRAGOJLOVIC, Z et al., "An advanced computational algorithm for systems analysis of tokamak power plants," Fusion Engineering and Design, vol. 85, pp. 243-265, 2010.
Parameter for economic analysis
Economical analysis of Biofuel by fusion

## Slide 13
Carbon Budget (by IEA)
What we will run out is not fossil resource,
but carbon budget.
“Negative Carbon” will be
Most precious energy resource beyond 2050.
Oil and coal canot be sold not because of high price, but
High penalty.
Carbon budget of post-Paris agreement age will run out after 2040,
CCS resource is more critical than fossil fuels.
Fusion can provide alternative
CCS technology

## Slide 14
biomass conversion for Charcoal production
lignin: (CH1.4O0.3)n + 0.7nH2O → ０.4nH2 H2O+ nC –290n[kJ]
Biomass
(1kg)
+
H2O
Fusion Heat，300℃
H2O,C
Hydrogen to sell (as byproduct)
Carbon Sequestration
8.2MJ
There are insufficient CCS capacity in the world.
Only Fusion Charcoal can isolate the carbon from the environmental Carbon Cycle forever！
→Fusion has unlimited market chance of “negative carbon” by abundant energy.
100,000 unit-operation year of 3GW fusion plant market.(7.4 TtonCO2 to solidify)
Charcoal itself is the “proof of collected CO2 from air”.
Emission credit to be sold in the
rt
270℃
310℃
350℃
Notes: こちらが、それぞれセルロース、リグニンの代表的な元素組成のCHO比から想定される水蒸気と反応した理想的なガス化を示す式です。
一方、このときに起こると考えられる代表的な平行反応には。これらの反応式が示すようにメタンを生成する反応や、一酸化炭素と水蒸気から水素と二酸化炭素を生成するシフト反応があります。簡略化のために炭素２個以上の反応は考慮していません。
こちらが本研究で用いる、パラメータである水素生成率、炭素分解率の定義式です。水素生成率は、全ての反応が理想的に上式で起こったときの水素生成量を100%とし、実際の生成量より求めます。炭素分解率は、バイオマスのもつ炭素原子数が一酸化炭素、二酸化炭素、メタンの炭素ガスにどれぐらい分解されたかを示します。
(0:55)

## Slide 15
Biomass
C, H2O, H2
Hydrogen fuel
1 GW electricity equivalent
2.5Mt/ycarbon=9.3MtCO2/y
Emission reduction credit
450M$/y assuming 50$/tonCO2
Charcoal
photosynthesis
Solar energy
CO2 stored as solid charcoal at ambient temperature and pressure
Fusion
3GW heat
440M$/y assuming
5 cent/kwh
Sold as emission credits in the emission trade market
Fusion charcoal can be made at the break even
Price of 50$/ton CO2.
Fusion can choose
electricity,
fuel, and
emission credit
As energy products.
Charcoal production As energy application
CO2
32PJ/y electricity
Notes: こちらが、それぞれセルロース、リグニンの代表的な元素組成のCHO比から想定される水蒸気と反応した理想的なガス化を示す式です。
一方、このときに起こると考えられる代表的な平行反応には。これらの反応式が示すようにメタンを生成する反応や、一酸化炭素と水蒸気から水素と二酸化炭素を生成するシフト反応があります。簡略化のために炭素２個以上の反応は考慮していません。
こちらが本研究で用いる、パラメータである水素生成率、炭素分解率の定義式です。水素生成率は、全ての反応が理想的に上式で起こったときの水素生成量を100%とし、実際の生成量より求めます。炭素分解率は、バイオマスのもつ炭素原子数が一酸化炭素、二酸化炭素、メタンの炭素ガスにどれぐらい分解されたかを示します。
(0:55)

## Slide 16
Sustainable energy system with fusion-biomass
熱
biomass
(CxHyOz)n
heat
heat
Desalination of
Sea water
irrigation
charcoal
Woody biomass
farm
forests
Bio-fuels
Electricity
In future grid
Fusion plant
waste
waste：
FC
PV
gasification
CO2
absorption
Carbon sequestration
Atmosphere CO2
Capture and reduction
Grid parity
Electricity
And
stabilization
Restoration of
Environment,
Forest and
farmland
Returning the carbon from air to coal mines.
Notes: 以上のセルロース、リグニンの吸熱分解実験の結果を用いて、産業廃棄物である木くずの年間排出量596万トンを処理することを目的に、熱交換型反応器の概要設計を行いました。木くずはセルロース７０％、リグニン３０％でなるものとしました。
設計時に用いるガス化パラメータとして、吸熱量と反応時間がありますが、これらについて本研究のデータを用いました。
コチラの図は、実験で得られたパラメータをもとに必要な物質収支、熱供給量、反応時間を満たすように設計した装置の概念です。
バイオマスは細かく粉砕して反応器上部より投入し、水蒸気も同じ流路を上から下に流通します。
一方、伝熱管に反応器下部から上部へと熱媒体を向流で流し、バイオマスへと熱伝達を行い、ガス化を行います。高温ガス炉、または高温の核融合炉を想定して熱媒体はヘリウムと仮定し、伝熱管材料はSiC複合材としました。
こちらが反応器断面の一部になります。このように内径１７ｍｍ、外径２０ｍｍの伝熱管が密に配置され全長は１０ｍ、総本数は29500本となっています。反応熱による吸熱量が大きいために設計上は熱供給が一番厳しい条件になりました。

## Slide 17
Summary of future energy system study
Future Energy Systems analyzed to reconsider fusion target.
1.Base load electricity may not make expected return of investment.
Levelized Cost of Electricity (LCOE) is not suitable for economical evaluation,
Electricity will be sold by bidding ;price is determined by the market mechanism.
- as a base load electricity, outage frequency has strong impact.
More conservative design required
2.Biomass-fuel by fusion is economically viable to replace fossil (diesel) and hydrogen.
Required Q is <5, easier for near future reactor target.
Estimated break-even cost is competitive for diesel/H2.
3.Carbon Sequestration by Fusion-Charcoal
Can be sold as CO2 credit in emission trade market.
Alternative CCS technology with unlimited capacity has large possibility.
Results suggest new possibility of fusion and Requirements for R&D target.

## Slide 18
If the final target of the fusion development is the pursuit of the
“sustainable development” of humankind, Generating electricity is not sufficient.
we have to develop and design fusion to meet the future requirements (not past).
The entire scope of the fusion deployment may be
・to achieve best grid compatibility in the clean electricity supply mix, to adopt to future grids
・Clean Fuel (gas and liquid) production from waste biomass to provide fossil substitute, and
・to provide technology to capture and decrease CO2 from atmosphere, by charcoal
production for negative carbon cycle
・Future market study provides better chance for fusion to identify the moving target.
- R&D and design of fusion should reflect the updated requirements.
Conclusion

## Slide 20
FCs
Oil
Turbine
FT plant case, PCD is supplied by 100 mills/kWh
  Fusion electricity by fuel cells