Impurity Screening in High Density Aditya Tokamak Plasmas (EX/P4-6)

R. Manchanda et al

- Impurity behaviour in the Aditya tokamak high density plasmas were studied.

- Impurities emissions monitored in Visible and VUV ranges using PMT based and VUV spectrometer based spectroscopic diagnostics, respectively.

- Impurity emissions decrease very much with the increase in ne. Similar observation was visible in the Prad and visible continuum signal.

- Thius indicates the better plasma properties in Aditya tokamak with increasing densities.

- This observation was corroborated with estimation of energy confinement time, which show increasing trend with ne.