## Slide 1: STUDY OF IRON IMPURITY BEHAVIOUR USING VUV SPECTROSCOPY IN ADITYA AND ADITYA-U TOKAMAK S. PATEL et al. (EX/P4-3)
VUV spectral lines at 28.41 nm (3p6 3s2 1S0 - 3s 3p 1P1) from Fe XV, 33.54 nm (2p6 3s2 2S1/2 - 2p6 3p 2P3/2) and 36.08 nm (2p6 3s2 2S1/2 - 2p6 3p 2P1/2) from Fe XVI are measured from Aditya and Aditya-U tokamak ohmic discharge.
Ratio of spectral line emission, and from two different plasma discharges, one with plasma density equal to and other with relatively high electron density is modelled using one dimensional impurity transport code.
Diffusion coefficient in the edge region is found to be 10 , while in the plasma core it is 0.1 . This values are compared with the Ion Temperature Gradient (ITG) driven anomalous transport, considering radially localized and density of independent resonant helical modes, and neo-classical transport in Pfirsch-Schluter regime respectively.