## Slide 1: PROGRESS IN THE ITER INTEGRATED MODELLING PROGRAMME AND THE ITER SCENARIO DATABASE
Creation of ITER Scenario Database containing scenarios representing all stages of ITER Research Plan
  Robust point of traceable access to ITER simulations
  Destined to become single point of access for all ITER scenario data
IMAS workflow based around DINA and JINTRAC codes couples core + edge + SOL transport to assess, for first time, complete ITER 15 MA / 5.3 T Q=10 DT baseline scenario from early ramp-up (X-point formation) to late ramp-down (X-point to limiter transition) respecting PF engineering limitations and divertor power fluxes [ EX/P7-25]
ITER Integrated Modelling & Analysis Suite (IMAS) continues to mature and strengthen its capabilities through collaboration with developers within the ITER Members
  Data Dictionary extended as required to address new Use Cases
S.D. Pinches et al.
TH/P6-7