## Slide 1: Summary slide for OV/P-6, “Fusion Energy Development Applications Utilizing the Spherical Tokamak and Associated Research Needs and Tools” by J.E. Menard, et al.
International ST research and facility representatives have identified research goals and performance targets for a range of fusion energy development applications ranging from plasma-material-interface science facilities to power reactors
Team is also surveying present/near-term ST facility capabilities to support long-term fusion application development, and identifying key gaps between present/planned capabilities and next-steps
Potential gaps assessed include:
  Non-inductive current start-up/ramp-up and sustainment
  Core and edge stability
  Transport / energy confinement
  Core-edge integration
  Plasma-wall interactions and power exhaust
  Long-pulse actuators for heating, current drive and control
See next slide for additional detail

## Slide 2: OV/P-6: Summary of research needs to support next-step STs
MHD stability, access to low n* covered by near-term STs
NSTX-U plans access to high fBS and full non-inductive
  Need to extend to 70-95% bootstrap fraction for reactor-relevant scenarios
Near-term STs limited to 1/ri* ≤  50-120
  Need to extend to 200-300 with new facility (?) and/or leverage tokamak results
Full performance ST-40 could test ST lq scaling to high BP
Very high q|| in next-steps requires divertor innovation
  MAST-U Super-X capability and/or liquid metals (LTX-b, long-term NSTX-U)
Very compact ST reactors (R=3-4m) generate high neutron wall loading and require innovations in blankets and first-wall