## Slide 1: MARS-Q modeling of DIII-D reveals that resonant NTV can cause large density pumpout during ELM suppression
Example:
  DIII-D 157376: B0=1.9 T, Ip=1.6 MA, q95=3.8
  5 kA I-coils in n=3 even parity  ~40% density pump out in experiments
  Modeling  ~25% pumpout
~100 ms
MARS-Q
modeling
Externally applied 3D magnetic fields often pump out plasma density in tokamak experiments, e.g. during ELM control
MARS-Q full toroidal, initial value simulations reveal that NTV particle flux plays significant role in particle radial transport  density pumpout
Drift kinetic resonance between 3D perturbation and toroidal precession of trapped thermal particles substantially enhances NTV flux
N(t)/Neqaxis