## Slide 1
Full stable power-detachment achieved in W7-X divertor
Heat flux derived from IR camera data
Heat flux essentially disappears from target for t>2 s, persisting until end of plasma heating at t=4 s
tE~100 ms rather constant for over 1 s
Heat flux patterns generally in good agreement with expectations
Heat fluxes are not problematic at medium to high plasma density, even at high power
P=2.8 MW, density ramped to 4-5x1019 m-3
Complete detachment
for t> 2 s on all 10 divertors (one shown)