## Slide 1: EX/P8-6/From RFX-mod to RFX-mod2
RFX-mod2 Reversed Field Pinch (RFP) will resume operations in 2020 after upgrades at present being implemented
RFX-mod2 mission: extend the RFX-mod plasma scenarios and the RFP scaling laws in condition of reduced magnetic stochasticity and improved boundary:
  Lower edge deformation: milder Plasma Wall Interaction
  Lower Tearing Modes amplitude: reduced transport
  Higher current threshold for mode wall locking: improved startup
Tearing Modes amplitude
RFX-mod
RFX-mod2
Edge Deformation
Notes: RFX-mod2 will investigate RFP nonlinear MHD dynamics in an unexplored parameter space, characterized by lowest shell proximity, highest shell conductivity, highest plasma current.
Expected outcome of RFX-mod2 experiments
investigate active control of non linear self-organized MHD behavior in RFP
  Assess MHD behavior in the high current boundary optimized regime with active control
  interplay of Quasi Helical states and relaxation/reconnection/dynamo events
  Challenging R&D is ongoing (R.Cavazzana, this conference)