## Slide 1
Fig. 1: M3D-C1 screened RMP field with KAM surfaces
RMP-driven density pump-out without enhanced χeeff in the pedestal seen in coupled neoclassical-gyrokinetic & MHD simulation (TH/P5-9)
R. Hager et al. (PPPL)
Long standing issue: density pump-out without loss of Te pedestal
RMP penetration is computed in M3D-C1, and read in by the gyrokinetic neoclassical code XGCa for transport calculation
Even though the M3D-C1-produced RMPs have well defined KAM surfaces (Fig. 1), XGCa shows (Fig. 2) that they enhance the outward neoclassical particle transport in the pedestal to the level required for density pump-out (Deff ∼𝓞(0.1) m2/s)
  Collisional neoclassical 3D effect
However, χeeff is negative with RMPs in the steep pedestal slope, except at pedestal top and foot (Fig. 3, orange solid line).
  Cancellation between inward heat-pinch and outward convection
Linear ramp-up of RMP field
Fig. 2
Fig. 3
θ/π
electron thermal pinch