## Slide 1: From Tore Supra to WEST: Evolution of the CODAC infrastructure
12th IAEA Technical Meeting on Control, Data Acquisition, and Remote Participation for Fusion Research
A. Berne, B. Santraine, N. Ravenel, J. Colnel, G. Caulier , F. Leroux, A. Barbuti, B. Vincent, Y. Moudden and the WEST Team
IAEA TM 2019

## Slide 2: Summary
Introduction
  WEST Project and Timeline
  Tore Supra CODAC system
Evolution of WEST CODAC system
  Motivations and solutions
  Selection and development
  WEST CODAC infrastructure
Results obtained
Conclusion and plan forward
| PAGE 2
IAEA TM 2019

## Slide 3: WEST Project
WEST (W [tungsten] Environment in Steady-state Tokamak)
Tokamak for long pulse operation
Testing and qualifying ITER-like tungsten divertor
Refurbishment of Tore Supra
International platform
In kind procurement with partners
Divertor coils
Tore Supra:
Limiter configuration
Carbon PFCs
WEST:
Divertor configuration; Tungsten PFCs
| PAGE 3
IAEA TM 2019

## Slide 4
Ip/10 (MA)
PLHCD (MW)
nlDiv (1019m-3)
nl (1019m-3)
| PAGE 4
IAEA TM 2019
WEST Timeline
Tore Supra [1988 – 2012]: superconducting tokamak for long pulse operation
2013
2014
2015
2016
2017
2018
2019
2020
First plasma
First X-point
configuration
>30 seconds
discharge
= Construction
= Commissioning
= Experiments
= Study

## Slide 5: Tore Supra CODAC - Infrastructure
Ethernet Network
Real-Time Network
Timing System Network
| PAGE 5
IAEA TM 2019
VME Acquisition Units
PC Acquisition Units
VME Compiler
Database
Control Room
VME Server
1995 – 2011
2004 – 2012
INTEL acquisition unit: one unit remaining

## Slide 6: Tore Supra CODAC – Acquisition unitS
| PAGE 6
IAEA TM 2019
 | VME | Industrial Computer
Operating System | LynxOS Diskless system | Windows XP Local hard drive
Processing Unit | 1 or 2 CPU board | Single processor (possibly multiple cores)
Acquisition boards | VME board | PCI/PCIe board Ethernet boards
Timing System | Home made board | PCIe boards from NI
Real Time (reflective memory) | ScramNet | No support
Number of unit | 26 | 22
Advantages | Centralized system Real Time OS Easy bus analysis | Cheap components (<1k€)
Issues | Obsolescence issue Limited performance Cost (>5k€) | Lack of RT data Hard maintenance No Real Time No bus analyzer available in house

## Slide 7: Evolution of the WEST CODAC System - Motivations and solutions - Acquisition Units - Acquisition boards - Real-time Network - Timing System Network - Timeline

## Slide 8: Evolution – Why ?
  Motivations for an upgrade:
        Make maintenance easier
        Improve performances (acquisition and computation)
        Reduce cost
        Manage obsolescence
  Solutions:
        Centralized management for acquisition units
        Define a “WEST acquisition unit” reference and upgrade old units
        Change the “Real Time Network”
        Suppliers selection
        Choose “Off-the-shelf” components
| PAGE 8
IAEA TM 2019

## Slide 9: Acquisition Unit – CentrAlized
| PAGE 9
IAEA TM 2019
Production Server
  PXE (Preboot eXecution Environment):
        The server can host several “Operating System”
        The client recovers the OS at startup and runs it from internal RAM
        Configuration files are used to manage all units:
        PHY Address  IP Address  OS Version  User data
DHCP = Dynamic Host Configuration Protocol / TFTP = Trivial File Transfer Protocol
NFS = Network File System
LAN Network
PXE Booting Clients
Backup Server
Easier maintenance (configuration, update and replacement)
High risk on server – Higher network traffic
Local disk required for high data throughput

## Slide 10: Acquisition Boards
| PAGE 10
IAEA TM 2019
  Supplier selection:
        Performance (number of channel, sampling frequency …)
        Cost
        Linux / Windows support
        Multiple format (PXIe, PCIe, Ethernet)
        Reconfigurable (FPGA)
         National Instruments tm
  Additionnal suppliers:
        Scientific instruments
        Specific needs
        Collaborations
PCI/PCIe cRIO PXI/PXIe
Requirements for WEST
acquisition

## Slide 11: Real-Time Network
| PAGE 11
IAEA TM 2019
  Supplier selection:
        Performance / Cost / Multiplatform
         Dolphin Interconnect Solutions
  Features:
        Extended star topology
        Flexible network (remove / add nodes)
        1 master  multiple nodes
        Remote monitoring
        Copper (40 Gbps – 5m) or optic link (20 Gbps – 300m)
        High “theoretical” performances

## Slide 12: Timing System Network
| PAGE 12
IAEA TM 2019
  Main functionalities:
        Distribution of 1 MHz time-stamping clock
        Distribution of events (shot scheduling, data sampling, trigger, safety …)
        Star topology
        Simplex mode
  Types of boards:
        PXIe: FPGA (VHDL) board from “Marvin Test Solution”
        PCIe: FPGA (LabView) board from “NI”
        PCIe: FPGA (VHDL) board from “Techway”
         To maintain a single code (VHDL)
No modification
New format needed

## Slide 13: WEST CODAC
Ethernet Acquisition Network
Real Time Network
Timing System Network
CEA
Network
Firewall
Database
Linux Boot
Servers
Control Room
VME Units
Win XP
VME Boot
Server
Plasma
Control
System
RS232
LAN
PCIe/PXIe
PCIe/VME
GPIO

## Slide 14: WEST CODAC
| PAGE 14
IAEA TM 2019
  Results:
        WEST preferred solution:
        Linux centralized Operating System
        CentOS 7.5
        All drivers installed: NI, Dolphin, Marvel, Spectrum, CAEN, …
        Wide supported hardware: PCIe/PXIe/VME, GPU, Ethernet, single/dual processor, single module computer …
        Reduction of VME and Win XP units
        Still open for other types of systems (collaboration)
Tore Supra
Units
WEST
Units

## Slide 15: WEST CODAC TIMELINE
  Creation of the first centralized OS
| PAGE 15
IAEA TM 2019
2013
2014
2015
2016
2017
2018
2019
2020
  Acquisition Units specifications
  Suppliers selection
  In Kind Procurement from IPR
  On site collaborators from 2013 to 2018
  Prototyping acquisition unit
  Test selected solutions
  Installation and commissioning
  Scientific Operation
  CODAC upgrade and maintenance
  Acquisition units development and improvement
  ≈ 3 new units per year (full upgrade, new diagnostic)

## Slide 16: Example of acquisition unit - standard acquisition unit: Magnetics - HYBRID acquisition unit: Fueling - Continuous acquisition unit: Calorimetry

## Slide 17: Example - Standard acquisition unit
  Magnetics  Full upgrade :
    PC Linux + PXIe + cRIO
    112 channels @ 1kHz
    96 channels @ 250 kHz
    2 ms time cycle
    Data on Real-Time network for Plasma Control System
    OpenMP computation (plasma boundary reconstruction)
    MHD  Full upgrade :
    PC Linux + PXIe
    More channels (38  51)
    Higher sample clock (100kHz  2MHz)
    Trigger on plasma events
Time evolution of the main plasma
parameters used for the plasma control
0
2
4
6
8
Temps (s)
1
2
3
4
5
6
7
8
9
10
Fréquence (kHz)
Time evolution of the MHD frequency
| PAGE 17
IAEA TM 2019

## Slide 18: Example - HYBRID acquisition unit
  Fueling  Hybrid upgrade :
    PC Linux + VME
    Keeping VME crate and boards
    Bridge PCIe/VME
    Same channels
    Data on Real-Time network
    Managing CPU obsolescence
  Timing System  Hybrid upgrade :
    PC Linux + VME
    Keeping VME crate and boards
    Time cycle improved (1ms  500µs)
    Read data on Real-Time network
    Managing CPU obsolescence
| PAGE 18
IAEA TM 2019

## Slide 19: Example - CONTINUOUS acquisition unit
  Calorimetry  Full upgrade :
    PC Linux + 7 x cRIO
    Continuous acquisition of 250+ sensors (T°C + Flow)
    Data on Real-Time network for PCS
    Variable cycle time during day and night
| PAGE 19
IAEA TM 2019

## Slide 20: Conclusion and plan forward
        4000+ experiments
        Almost 24/7 operation
        High availability of the CODAC infrastructure
        Easier maintenance (troubleshooting during experiments, Operating System, driver installation, X-compiler)
        Pursue standardization
        Offer advance support (computing with GPU, synchronization with PTP, etc.)
        Improvements (network, middleware, parallel computing)
        Improve Real Time performances (soft patch)
| PAGE 20
IAEA TM 2019

## Slide 21: DRF IRFM STEP
Commissariat à l’énergie atomique et aux énergies alternatives
Centre de Cadarache | 13108 Saint Paul Lez Durance Cedex
T. +33 (0)4 42 25 62 25 | F. +33 (0)4 42 25 26 61
  Etablissement public à caractère industriel et commercial | RCS Paris B 775 685 019
Thank you for your attention