## Slide 1: Sustaining the Security of Radioactive Sources Through Compliance with Regulatory Requirements
By
Javed Iqbal
Pakistan Atomic Energy Commission

## Slide 2: Outlines
Application of Sealed radioactive Sources (SRS) in Pakistan
Basis for Implementation of Security of Radioactive Sources
Accountability and Control Program for SRS
  Categorization System and Security Levels for SRS
  SRS Database
  Corporate Oversight and Sustainability
  Physical Inventory Verification and Assessment of Physical Protection Measures
Management of Disused SRS
Conclusion

## Slide 3: Application of Sealed Radioactive Sources (SRS) in Pakistan
SRS Applications
Medical
Industry
Agriculture
Research/Education

## Slide 4: Commonly used Sealed Radioactive Sources (SRS) in Pakistan
Co-60, Ir-192, Cs-137
Activity Range: few KBq – TBq
Co-60 is used for radiotherapy
Ir-192 is used for Brachytherapy, radiography
Around 31% sources are being used in Industry (for Gamma Radiography, well-logging, level gauges, moisture gauges etc.)
Co-60 Teletherapy Machine
Notes: On the basis of Categorization 7.8% SRS fall in Category-1, 1.7% in Category-2,
1.9% category-3 while 88.4% fall in category-4 & Category-5

## Slide 5: Basis for Implementation of Security Measures for Radioactive Sources
IAEA code of Conduct – INFCIRC/663
IAEA nuclear Security Recommendations (NSS14)
IAEA Nuclear Security Implementing Guide (NSS-11)
PNRA Regulations on “Security of Radioactive Source(s)-PAK/926”

## Slide 6: Accountability and Control Program for SRS
Accountability and Control Program
SRS Database
Inspection:
Safety and Physical Protection Measures
Physical Inventory Verification
Management of DSRS

## Slide 7: Categorization and Security Level for SRS
Overriding priority for the categorization of radioactive sources shall be given to their use in a certain practice.
In case of radioactive sources is not listed in column 2 of the above table, then A/D ratio shall be used for their categorization
For the radioactive sources during manufacture and storage, their A/D value shall only be considered for categorization
Reference: PAK/926

## Slide 8: Periodic SRS Inventory Status
Periodic SRS data is acquired by Corporate level
  Quarterly for Category 1
  Bi-annually for remaining categories of SRS
  Approved SRS Accountability form (SRS-1 Form)
  Part-A of SRS-1 Form
  Summary of inventory of SRS
  Detail of each SRS
  Status and application of SRS
  SRS transfer information
  Custodian

## Slide 9: Periodic SRS Inventory Status Cont…
  Part-B of SRS-1 Form
  Questionnaire about onsite measures for secure handling of SRS
  Administrative physical protection measures
  SRS handling procedures
  Record keeping

## Slide 10: SRS Database
Information Extracted from SRS-1 Form
  SRS ID
  SRS Name
  Half Life
  Number of SRS
  Activity
  Category of SRS
  Physical Form
  Application
  Remarks
    In-use
    Dis-used

## Slide 11: Corporate Oversight and Sustainability
Physical Inventory Verification (PIV)
Technical Security Measures
  Detection
  Delay
  Access Control
  Administrative Security Measures
Sustainability
  Maintenance and testing program
  Adopting emerging technologies to enhance effectiveness of PPS
  Policies and procedures

## Slide 12: Physical Inventory Verification
  Inventory and records
  SRS receipt and transfer record
  SRS use/movement log
  Periodic Inventory Verification by the custodian
  SRS transportation and disposal record
  SRS certificate and relevant documentation provided by the manufacturer

## Slide 13: Technical Security Measures
Physical Protection System
  Intrusion detection System
  Assessment of Detection (CCTV)
  Automatic Access Control System
  Physical Barriers (Robust doors, Secure containers and enclosures, Locks for doors)
  Strong room for sources storage
  Locked Shielded Containers

## Slide 14: Security Measures for Source(s)
Security Function | Security Measures |  | 
 | Category-1 (Security Level A) | Category-2 (Security Level B) | Category-3 (Security Level C)
Goal | To prevent unauthorized removal | To Minimize likelihood of unauthorized removal | To reduce likelihood of unauthorized removal
Detection | IDS and/or continuous surveillance | IDS and/or continuous surveillance | -
 | Electronic Temper detection | Temper detection or periodic checks by operating personnel | Temper detection or daily checks by operating personnel
 | Immediate assessment of detection: CCTV or by operating personnel | Immediate assessment of detection: CCTV or by operating personnel | Immediate Assessment by operating personnel
 | Physical Verification: Fortnightly | Physical Verification: Fortnightly | Physical Verification: Monthly
Reference: PAK/926

## Slide 15: Security Measures for Source(s)
Security Function | Security Measures |  | 
 | Category-1 (Security Level A) | Category-2 (Security Level B) | Category-3 (Security Level C)
Delay | Two Layers of Delay Barriers (at least) | Two Layers of Delay Barriers (at least) | Single Barrier or surveillance by security personnel
Access Control | Provision of identification and verification | Identification measure | Identification measure
Response | Rapid, dependable and diverse means of communication; | Rapid and reliable means of communication | Appropriate actions in accordance with Physical Protection Plan
 | Interrupt and neutralize adversary as per Physical Protection Plan | Interrupt and neutralize adversary as per Physical Protection Plan | Appropriate response actions in accordance with Physical Protection Plan

## Slide 16: Administrative Security Measures
  Physical Protection Plan
  Security Event Reporting
  Reliability and Trustworthiness of Personnel
  Operating Procedures
    Access Control Procedures
    SRS handling and storage procedure
    Key control procedures
    Alarm assessment and response procedures
    SRS disposal procedures
  Training of Personnel
  Security Culture

## Slide 17: Event Reporting Mechanism
Required Actions | Timeline
Remedial measures and inform local law enforcement agencies | Immediate
Notify to Authority | 24 Hours
Submit a preliminary report to the Authority | 72 Hours
Submit to the Authority a detailed report on the causes of the event, its circumstances and consequences, and on the corrective actions taken or to be taken. | 60 Days
Reference: PAK/926
Notes: Event: unauthorized access/intrusion, loss of control over SRS

## Slide 18: Management of Disused SRS
Return to manufacturer
Regulatory requirement as per PAK/915
Applicable to SRS with initial activity > 100 GBq and Half-life > 1 year
SRS shall be returned to country of origin as part of contract with supplier
Mandatory condition for “NO Objection Certificate” from PNRA
Interim Storage
PPRWMF (PINSTECH Predisposal Radioactive Waste Management Facility) Islamabad
  Covers two provinces (i.e. Punjab, KPK) and Capital territory
RAWSA (Radioactive Waste Storage Area) KANUPP, Karachi
  Covers Provinces Sindh and Balochistan

## Slide 19: Conclusion
Sealed Radioactive Sources are being used in Medicine, Agriculture, Industry, Research and Education in Pakistan
Relevant Regulations for Safety and Security of SRS are in place for Safe and Secure use/ handling, storage and transport of radioactive sources
All radioactive sources and under strict regulatory control from cradle to grave