## Slide 1
Prepared by Michal Botha, Nuclear Security Section Australian Safeguards and Non-Proliferation Office
Making THE Australian Nuclear Security Regime Fit for Purpose
D20/73251
International Conference on Nuclear Security
11 FEBRUARY 2020

## Slide 2: Regulated Nuclear Industry and Facilities
  UOC Industry
    3 operating uranium mines
    14 Road, Rail and Sea transport
  ~ 100 Universities, Hospitals, Radiographers, etc. holding nuclear material
  ANSTO
    OPAL Research Reactor (LEU Fuel - Category II)
    nuclear material stores
    production of 99Mo and other medical isotopes
  Technology holders
    e.g. Silex Systems Ltd enrichment research

## Slide 3: Permit holder distribution by industry type
Chart: 
| L | R | U | P | T | S
Sales | 35 | 32 | 21 | 6 | 3 | 3
~ 150 Permit Holders

## Slide 4: INTERNATIONAL and NATIONAL Nuclear Security regimeS
International
National
Treaties
Less-than-treaty
Instruments
Laws, Regulation & Competent Authorities
Facility Operator Security Systems
Orgs
Amended CPPNM
Nuclear Non-Proliferation (Safeguards) Act 1987
Permits
Nuclear Security Series
Nuclear Terrorism Convention
Australian Radiation Protection and Nuclear Safety Act 1998
Licences
Code of Conduct
“Guns, Guards and Gates”
Security Plans and Arrangements
ASNO
ARPANSA
UNSCR 1540
ASIO
ACSC
AFP
AGs
IAEA
GICNT
United Nations
INTERPOL
WINS
Regulations
Regulations

## Slide 5: PERMITS HOLDER SECURITY CATGORISATION
Chart: 
| Prudent Managemnet Practice | Category II + III Nuclear Material | National Information Security
 | 126 | 2 | 11

## Slide 6: Australian Categorisation of Nuclear Material
IAEA Categorisation According to NSS-13 (INFCIRC/225/Rev.5) (CPPNM Annex II) |  |  |  |  |  | 
Material |  |  |  | Category |  | 
 | Form |  |  | I | II | III
Special Fissionable Material | Unirradiated | Pu |  | ≥2kg | >500g <2kg | >15g ≤500g
 |  | U235 | ≥ 20% U235 | ≥5kg | >1kg <5kg | >15g ≤1kg
 |  |  | > 10% U235 < 20% U235 |  | ≥10kg | >1kg <10kg
 |  |  | < 10% U235 |  |  | ≥10kg
 |  | U233 |  | ≥2kg | >500g <2kg | >15g ≤500g
 | Irradiated Fuel |  |  |  | DU, NU, Th or LEF <10% fissile content | 

## Slide 7: Australian Categorisation of Nuclear Material
IAEA Categorisation According to NSS-13 (INFCIRC/225/Rev.5) (CPPNM Annex II) |  |  |  |  |  |  |  |  |  |  | 
Material |  |  |  |  | Category |  |  |  |  |  | 
 | Form |  |  |  | I | II | III |  |  |  | LOF
Special Fissionable Material | Unirradiated | Pu |  |  | ≥2kg | >500g <2kg | >15g ≤500g |  |  |  | ≤10g
 |  | U235 | ≥ 20% U235 |  | ≥5kg | >1kg <5kg | >15g ≤1kg |  |  |  | ≤10g Total U235
 |  |  | > 10% U235 < 20% U235 |  |  | ≥10kg | >1kg <10kg |  |  |  | 
 |  |  | < 10% U235 |  |  |  | ≥10kg |  |  |  | 
 |  | U233 |  |  | ≥2kg | >500g <2kg | >15g ≤500g |  |  |  | ≤ 10g
 | Irradiated Fuel |  |  |  |  | DU, NU, Th or LEF <10% fissile content |  |  |  |  | 
Source Material | Unirradiated | Natural Uranium |  |  |  |  |  |  |  |  | Unlimited
 |  | Depleted Uranium |  |  |  |  |  |  |  |  | ≤5000kg
 |  | Thorium |  |  |  |  |  |  |  |  | ≤5000kg

## Slide 8: Australian Categorisation of Nuclear Material
IAEA Categorisation According to NSS-13 (INFCIRC/225/Rev.5) (CPPNM Annex II) |  |  |  |  |  |  |  |  | ASNO Categorisation Prudent Management Practice |  |  |  |  |  |  |  | 
Material |  |  |  |  | Category |  |  |  | Category |  | Location Outside Facility (LOF) |  |  | UOC |  | Radiographers | 
 | Form |  |  |  | I | II | III |  | IV |  | L3 | L2 | L1 | U1 | U2 | R2 | R1
Special Fissionable Material | Unirradiated | Pu |  |  | ≥2kg | >500g <2kg | >15g ≤500g |  | >10g ≤15g |  | ≤10g | ≤5g | ≤1g |  |  |  | 
 |  | U235 | ≥ 20% U235 |  | ≥5kg | >1kg <5kg | >15g ≤1kg |  | >10g ≤15g Total U235 |  | ≤10g Total U235 | ≤5g Total U235 | ≤1g Total U235 |  |  |  | 
 |  |  | > 10% U235 < 20% U235 |  |  | ≥10kg | >1kg <10kg |  | >10g ≤1kg Total U235 |  |  |  |  |  |  |  | 
 |  |  | < 10% U235 |  |  |  | ≥10kg |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | >10g <10kg Total U235 |  |  |  |  |  |  |  | 
 |  | U233 |  |  | ≥2kg | >500g <2kg | >15g ≤500g |  | >10g ≤15g |  | ≤ 10g | ≤ 5g | ≤1g |  |  |  | 
 | Irradiated Fuel |  |  |  |  | DU, NU, Th or LEF <10% fissile content |  |  |  |  |  |  |  |  |  |  | 
Source Material | Unirradiated | Natural Uranium |  |  |  |  |  |  | ≤5000kg |  | ≤5000kg | ≤500kg | ≤10kg | Unlimited | 1x106kg |  | 
 |  | Depleted Uranium |  |  |  |  |  |  | ≤5000kg |  | ≤5000kg | ≤500kg | ≤10kg |  |  | ≤5000kg | ≤500kg
 |  | Thorium |  |  |  |  |  |  | ≤5000kg |  | ≤5000kg | ≤500kg | ≤10kg |  |  |  | 

## Slide 9: ASSOCIATED ITEMS
ASSOCIATED ITEMS
ASSOCIATED MATERIAL (AM)
Material specially suited for use in nuclear activities
ASSOCIATED EQUIPMENT (AE)
Equipment or plant specially for use in nuclear activities
ASSOCIATED TECHNOLOGY (AT)
Information applicable primarily for enrichment, reprocessing or heavy water production
Photograph, model or other thing from which such information may be obtained or deduced
Electronic Media (e.g. CDs, USB, Hard-drive, Smart Device, Networks)
Equipment or plant (AE) from which information (AT) can be obtained or deduced
Nuclear Grade Graphite
Heavy Water
Reactors
Centrifuge Design
Heavy Water Plant
Enrichment, reprocessing or heavy water plant and equipment
Reactor internals, pressure vessels etc.
Computer or physical model
Document containing information

## Slide 10: PERMITS AND AUTHORITIES
Permit to Decommission Facility
Permit to Establish Facility
Authority to Communicate Information
S1 - Facilities
S2 - Research Associated Technology
S3 - Research Nuclear Material
S4 - Waste Repository
L1 - Very Low Quantity
L2 - Low Quantity
L3 - Moderate Quantity
L4 - Category IV
U1 - UOC Concentration Plant
U2 - UOC Transport Road/Rail
U3 - UOC Transport Sea
U4 - UOC Stevedores /Ports
U6 - UOC Laboratory
U5 - UOC Broker / Trader
U7 - Establish UOC Plant
U8 – Decommission UOC Plant
R1 - Radiographer Small Quantity
R2 - Radiographer Medium Quantity
T1 - NM General
T2 – NM Air transport
T9 - NM Single Transport
Section 18
Section 13
Section 16
P1 - Patent Attorneys
P2 – Government Archives
Permit to Transport Nuclear Material
Section 16A
Section 16B
Permit to Possess Nuclear Material

## Slide 11: Permit Content - UOC
PERMIT
HOLDER
PARTICULARS
EXECUTIVE LEVEL
PERMIT PRICIPLES
MAXIMUM
NUCLEAR
MATERIAL
HOLDINGS
INSPECTION REQUIREMENTS ASNO / IAEA
PERMIT SECTION
SECURITY PLAN
RISK ASSESSMENT
GOVERNANCE
APPLICATIONS
NOTIFICATIONS
REPORTING
ACCOUNTANCY REQUIREMENTS
NUCLEAR SECURITY REQUIREMENTS
COMPLIANCE CODE
CONTROL REQUIREMENTS
SCALABLE THREAT MODEL

## Slide 12: Permit Content – UOC TRANSPORT
PERMIT
HOLDER
PARTICULARS
EXECUTIVE LEVEL
PERMIT PRICIPLES
MAXIMUM
MATERIAL
TRANSPORT
LIMIT
INSPECTION REQUIREMENTS ASNO / IAEA
PERMIT SECTION
TRANSPORT PLAN
RISK ASSESSMENT
GOVERNANCE
SCALABLE THREAT MODEL
EMERGENCY PROCEDURES
DURING TRANSPORT
STORAGE INCIDENTAL TO TRANSPORT
COMPLIANCE CODE
PRE- TRANSPORT

## Slide 13: L1, L2, L3 PRUDENT MANAGEMENT PRACTICE – GRADED APPROACH
The Permit Holder shall maintain security measures for preventing the theft, loss or unauthorised handling of nuclear material including:
  [L1] restricting access to nuclear material to persons who need to access such material;
  [L1] securing the inventory in a lockable room or container; and
  [L1] maintaining documentary records associated with the Permit conditions (access list, log in/out sheet)
  [L2] maintaining written procedures for access, use and storage
  [L3] maintaining adequate levels of appropriately qualified staff to ensure systems of physical protection and security are fully implemented and operational

## Slide 14: NEXT STEPS
  Glossary
  Harmonisation
  New Permit Classes
  Production of Guidance Documents
  Model Security Plans

## Slide 16
Additional Slides

## Slide 17: Permit Functional Format
Pre – Transport
Container / Seal Inspection
Transport Briefing
Communications Operational Test
During Transport
Convoy Communication
Predetermined stops
Security and Situational Awareness
Interim Storage
Interim Security Arrangements
Approved Secure Compounds
Container storage to be door-to-door
Emergency Response
Restoring Communications
Maintaining Security
Training
Escalated Threat
Route

## Slide 18: Scalable Threat Model for the Transport of UOC
ASNO utilizes a threat scale based on the Australian National Terrorism Threat Advisory System3
3www.nationalsecurity.gov.au
4International Ship and Port Facility Security Code 2003
CERTAIN
EXPECTED
PROBABLE
POSSIBLE
NOT EXPECTED
Mining Industry
MARSEC 3
MARSEC 2
MARSEC 1
Australian Maritime Transport and Offshore Facilities Security Act 2003 in keeping with ISPS4 requires the application of maritime security levels
Attack/activities is imminent or occurring
Movements of UOC are to cease
Baseline nuclear security measures to be applied for the transport of UOC
Attack/activities is feasible and could occur
Attack/activities is assessed as likely
Normal business operations
Heightened risk of a security incident
Security incident is probable or imminent

## Slide 19: Australian Nuclear Security Regime
Australian Legislation
Administered by ASNO
Weapons of Mass Destruction (Prevention of Proliferation) Act 1995
NPT
Australian / IAEA Comprehensive Safeguards Agreement – 10 July 1974
Associated
Equipment
Associated
Technology
Patents Act 1990
- Article 147
Customs (Prohibited Exports) Regulations 1958 - Reg 13E
Nuclear & Associated Material
Customs (Prohibited Exports) Regulations 1958 - Reg 9
Amended Convention on the Physical Protection of Nuclear Materials
International Convention for the Suppression of Acts of Nuclear Terrorism
Nuclear Non-Proliferation
(Safeguards) Act 1987
Additional Protocol to the Comprehensive Safeguards Agreement – 12 December 1997
ARPANS Act 1998 Regulations 1999 – Part 3

## Slide 20: Australian Security LANDSCAPE
Radioactive Material
Nuclear Material
Associated
Material
Equipment
Technology
Other Sensitive Government Information/Assets
Nuclear Security-Related
Information
ASNO (Safeguards Act) - [Physical Security]
ICSANT
ARPANSA + State Authorities
Protective Security Policy Framework
IAEA NSS 20 – Nuclear Security
IAEA NSS 14
[Nuclear Security]
IAEA NSS 13 [Physical Protection]
Physical Security
Information/Cyber Security
Personal Security
Amended CPPNM

## Slide 21: CATEGORISATION OF NUCLEAR MATERIAL – INFCIRC/225
Australia has
- 1 research reactor facility that has Class III and Class II nuclear material in storage.
Approximately 140 operators that have nuclear material requiring prudent management practice
99% of Australian Operators are required to have prudent management practice