## Slide 1
Integrated no-ELM scenario in AUG:
EDA H-mode extended to high power by controlled Ar seeding
power to divertor controlled via Ar seeding
quite narrow power window in Psep for L- EDA - ELMy
very good performance: H98>1,
n/nGW=0.9, N = 2,
integration with detachment shown with Ar+N
completely ELM-free
low tungsten concentration < 10-5
quasi-coherent mode
EDA H  L-mode due to radiation event
QCM @ 20-30 kHz provides full ELM suppression
via MHD-stable pedestal