## Slide 1
Hybrid deep learning architecture for general disruption prediction across tokamaks
J. Zhu1
with, C. Rea1, K. J. Montes1, R.S. Granetz1, R. Sweeney1, R.A. Tinguely1
IAEA TM on Plasma Disruptions & Mitigation, July 20-23, 2020
Supported by US DOE grant DE-SC0014264-MFE
1MIT Plasma Science and Fusion Center
Cambridge, MA, USA

## Slide 2
New disruption predictor shows progress toward ITER requirements
Motivation: ITER cannot withstand many unmitigated disruption [1].
Any predictor for ITER must rely on few disruptive shots from test machine.
Our predictor learns device-independent knowledge from disruptive data, while non-disruptive data is machine-specific.
Few "unseen" device disruptive discharges still needed to reach best performances
[1] De Vries P. C. et al. 2016 Fus. Sci. Technol. 69, 471–484
Notes: Omit this due to time constraints (backup)

## Slide 3
Disruption warning databases
Table 1: The dataset composition of the three disruption warning databases
 | Number of training shots | Number of test shots | Number of validation shots
C-Mod | 3343 (692 disruptive) | 651 | 463
DIII-D | 5286 (732 disruptive) | 1085 | 734
EAST | 8296 (2301 disruptive) | 1674 | 1137
label imbalanced datasets
Table 2: Signals considered in the development of the predictive models
lock-mode-proxy | Greenwald-fraction | lower-gap | z-error-proxy
radiated-fraction | Rotating-mode-proxy | v-loop | q95
ip-error-fraction | betap | kappa | li
Notes: Omit this due to time constraints (backup)

## Slide 4
Hybrid Deep Learning (HDL) Predictor: a fast, powerful and general predictive model for disruption
The prediction framework consists:
  An advanced deep neural network converts an input plasma sequence to a predicted label.
  A shot by shot testing scheme to simulate alarms triggered in the Plasma Control System (PCS).
HDL features:
  Impressive performance on different machines with limited hyperparameter tuning
  Suitable for cross-machine study and ITER disruption prediction research.
  Short evaluation time (<1ms using an 8-core CPU), real-time deployment potential.
Notes: Omit this due to time constraints (backup)

## Slide 5
Cross-machine study: explore data-efficient disruption prediction on new devices.
Setup: two machines as ‘existing machines’, with the third one chosen as a ‘new device’.
Performance metric: ROC curves and AUC values [2] at 50ms before the current quench.
All following qualitative conclusions are machine-independent (only show the EAST case).
[2] Bradley A. P. 1997 Pattern Recognition, 30, 1145–1159
Notes: Omit this due to time constraints (backup)

## Slide 6
Best prediction recipe using 20 disruptive training shots from the target new device
Best prediction recipe on new device: using a few disruptive shots and many non-disruptive shots from the new device plus many disruptive data from existing devices.
Best scenario with limited disruptive
Chart: Training Set Composition
| Existing | New
Disruptive | 1978 | 20
Non-Disruptive | 0 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 7
Remove all disruptive training shots from the new device, worse
Best prediction recipe on new device: using a few disruptive shots and many non-disruptive shots from the new device plus many disruptive data from existing devices.
Chart: Training Set Composition
| Existing | New
Disruptive | 1978 | 0
Non-Disruptive | 0 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 8
Remove 50% of new device non-disruptive shots, worse
Best prediction recipe on new device: using a few disruptive shots and many non-disruptive shots from the new device plus many disruptive data from existing devices.
Chart: Training Set Composition
| Existing | New
Disruptive | 1978 | 20
Non-Disruptive | 0 | 2997
Notes: Omit this due to time constraints (backup)

## Slide 9
Trained only on selected new device data, baseline case, much worse
Best prediction recipe on new device: using a few disruptive shots and many non-disruptive shots from the new device plus many disruptive data from existing devices.
Chart: Training Set Composition
| Existing | New
Disruptive | 0 | 20
Non-Disruptive | 0 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 10
Go back to the baseline case
Best prediction recipe on new device: using a few disruptive shots and many non-disruptive shots from the new device plus many disruptive data from existing devices.
Baseline case with limited disruptive
Chart: Training Set Composition
| Existing | New
Disruptive | 0 | 20
Non-Disruptive | 0 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 11
Add disruptive data from existing machines, much better
Best prediction recipe on new device: using a few disruptive shots and many non-disruptive shots from the new device plus many disruptive data from existing devices.
Chart: Training Set Composition
| Existing | New
Disruptive | 1978 | 20
Non-Disruptive | 0 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 12
Continually add non-disruptive data from existing machines, drop back
Best prediction recipe on new device: using a few disruptive shots and many non-disruptive shots from the new device plus many disruptive data from existing devices.
Non-disruptive data from existing devices is harmful while disruptive data is beneficial to the predictive power, might from the label imbalance of each training set.
Chart: Training Set Composition
| Existing | New
Disruptive | 1978 | 20
Non-Disruptive | 7205 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 13
Cross-machine experiments using all disruptive training shots from the target new device
Best scenario with all disruptive
Chart: Training Set Composition
| Existing | New
Disruptive | 1978 | 2301
Non-Disruptive | 0 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 14
add non-disruptive data from existing machines, worse
Chart: Training Set Composition
| Existing | New
Disruptive | 1978 | 2301
Non-Disruptive | 7205 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 15
Trained only on new device data, baseline case, worse
Disruptive data from existing machines is still beneficial, while non-disruptive data is still harmful even with abundant new device disruptive data.
Chart: Training Set Composition
| Existing | New
Disruptive | 0 | 2301
Non-Disruptive | 0 | 5995
Notes: Omit this due to time constraints (backup)

## Slide 16
Remove 2/3 of EAST non-disruptive training shots, an inversely imbalanced dataset
Disruptive data from existing machines is still beneficial, while non-disruptive data is still harmful even with abundant new device disruptive data.
Baseline case with reduced non-disruptive
Chart: Training Set Composition
| Existing | New
Disruptive | 0 | 2301
Non-Disruptive | 0 | 1998
Notes: Omit this due to time constraints (backup)

## Slide 17
add disruptive data from existing machines, better
Disruptive data from existing machines is still beneficial, while non-disruptive data is still harmful even with abundant new device disruptive data.
Chart: Training Set Composition
| Existing | New
Disruptive | 1978 | 2301
Non-Disruptive | 0 | 1998
Notes: Omit this due to time constraints (backup)

## Slide 18
add non-disruptive data from existing machines, worse
Disruptive data from existing machines is still beneficial, while non-disruptive data is still harmful even with abundant new device disruptive data.
The effects of disruptive data (positive) and non-disruptive data (negative) do not result from the class imbalance of the dataset. Non-disruptive data is machine-specific, while disruptive data contains general knowledge about disruptions.
Chart: Training Set Composition
| Existing | New
Disruptive | 0 | 2301
Non-Disruptive | 1978 | 1998
Notes: Omit this due to time constraints (backup)

## Slide 19
Distributions of non-disruptive signals are clear different across devices
Univariate distributions imply different devices tend to have disjoint operational regimes.
Notes: Omit this due to time constraints (backup)

## Slide 20
Different devices show similar behaviors when a disruption is imminent
Univariate distributions imply different devices tend to have disjoint operational regimes.
Similar behaviors in disrupt data across machines are general knowledge hidden beneath disruptive shots.
Notes: Omit this due to time constraints (backup)

## Slide 21
Summary and Conclusions
HDL framework: a powerful general solutions for disruption prediction.
Relatively good prediction performances on target devices can be achieved using a small set of disruptive shots while thousands of non-disruptive shots from themselves, plus hundreds of disruptive discharges from other devices.
Non-disruptive data is machine-specific, and the disruptive data contains general knowledge about disruptions.
Future work:
  Fine hyperparameter tuning
  Incorporate device features to the HDL framework
  Extend analysis to other tokamaks (JET, KSTAR… )
Summary

## Slide 22
Summary and Conclusions
See J.X. Zhu, C. Rea et al. Hybrid deep learning architecture for general disruption prediction across tokamaks, submitted to Phys. Rev. Lett., 2020 https://arxiv.org/abs/2007.01401
For more information…