## Slide 1
MHD modeling of dispersive shell-pellet injection (DSP) for disruption-mitigation in DIII-D
V.A. Izzo, Fiat Lux
IAEA Technical Meeting on Plasma Disruptions and their Mitigation
20-23 July 2020
Acknowledgements: E. M. Hollmann, P. B. Parks, D. Shiraki, N. Alexander, N.W. Eidietis, C. J. Lasnier, R. A. Moyer, C.C. Kim, E. Nardon

## Slide 2: The DSP Concept for Disruption Mitigation*
Thin low-Z shell (diamond)
Dispersive payload (boron dust)
Pre-Thermal Quench
Thermal Quench
r/a
r/a
Te
Te
shell ablates in edge
Payload disperses in core
*P. B. Parks, “METHODS AND APPARATUS FOR DISRUPTION MITIGATION IN FUSION DEVICES,” U.S. Patent Application Attorney Docket No.: 074915-8030.US00
(don’t perturb edge flux surfaces, reduce conduction to divertor)
(inward heat flux, high radiation fraction, assimilation)

## Slide 3: Overview of NIMROD MHD+Radiation+RE Model
Single fluid MHD: Single temperature (one energy equation, instantaneous dilution cooling due to added impurities) Single velocity (one momentum equation, all species are advected together) | Free boundary, ideal wall simulation: Simulations boundary is outside the separatrix, open flux region is included Simulation boundary is perfectly conducting
Multiple ion species/charge states: Deuterium ions plus two impurity ion species: C and Be with all charge states of each impurity tracked separately (1+7+5 = 13 continuity equations). Electron density from quasi-neutrality. Ionization, recombination and radiation calculated for each species | Drift orbits calculated for RE test particles: Three equations in real space plus two in velocity space, includes E-field acceleration, slowing due to small angle collisions, synchrotron, and bremmstrahlung radiation Test particles have no feedback on the MHD equations

## Slide 4: Overview of NIMROD MHD+Radiation+RE Model
Single fluid MHD: Single temperature (one energy equation, instantaneous dilution cooling due to added impurities) Single velocity (one momentum equation, all species are advected together) | Free boundary, ideal wall simulation: Simulations boundary is outside the separatrix, open flux region is included Simulation boundary is perfectly conducting
Multiple ion species/charge states: Deuterium ions plus two impurity ion species: C and Be with all charge states of each impurity tracked separately (1+7+5 = 13 continuity equations). Electron density from quasi-neutrality. Ionization, recombination and radiation calculated for each species | Drift orbits calculated for RE test particles: Three equations in real space plus two in velocity space, includes E-field acceleration, slowing due to small angle collisions, synchrotron, and bremmstrahlung radiation Test particles have no feedback on the MHD equations

## Slide 5: Overview of NIMROD MHD+Radiation+RE Model
Single fluid MHD: Single temperature (one energy equation, instantaneous dilution cooling due to added impurities) Single velocity (one momentum equation, all species are advected together) | Free boundary, ideal wall simulation: Simulations boundary is outside the separatrix, open flux region is included Simulation boundary is perfectly conducting
Multiple ion species/charge states: Deuterium ions plus two impurity ion species: C and Be with all charge states of each impurity tracked separately (1+7+5 = 13 continuity equations). Electron density from quasi-neutrality. Ionization, recombination and radiation calculated for each species | Drift orbits calculated for RE test particles: Three equations in real space plus two in velocity space, includes E-field acceleration, slowing due to small angle collisions, synchrotron, and bremmstrahlung radiation Test particles have no feedback on the MHD equations

## Slide 6: Overview of NIMROD MHD+Radiation+RE Model
Single fluid MHD: Single temperature (one energy equation, instantaneous dilution cooling due to added impurities) Single velocity (one momentum equation, all species are advected together) | Free boundary, ideal wall simulation: Simulations boundary is outside the separatrix, open flux region is included Simulation boundary is perfectly conducting
Multiple ion species/charge states: Deuterium ions plus two impurity ion species: C and Be with all charge states of each impurity tracked separately (1+7+5 = 13 continuity equations). Electron density from quasi-neutrality. Ionization, recombination and radiation calculated for each species | Drift orbits calculated for RE test particles: Three equations in real space plus two in velocity space, includes E-field acceleration, slowing due to small angle collisions, synchrotron, and bremmstrahlung radiation Test particles have no feedback on the MHD equations

## Slide 7: Outline
Part I: Phenomenology of an inside out TQ
 Simulation results with constant shell ablation rate, near-axis payload delivery
Part II: Results with plasma parameter dependent ablation rates
 Single and dual shell pellet injection simulations

## Slide 8: Constant source rate model for shell & payload
Npayload = 1.17x1021 atoms Be
(= 100% DIII-D B payload quantity)
time
r/a
1.0
0.2
0.0
Toroidally and poloidally localized source of neutral impurities propagates along outer midplane from edge to core
C Shell delivery rate (1/s) = Nshellvpellet/(0.8a)
Nshell = 7.525x1019 atoms C
(= 25% of DIII-D nominal quantity)
Be Payload delivery rate (1/s) = Npayloadvpellet/(0.2a)

## Slide 9: Constant shell ablation simulations: phenomenology of an inside-out TQ
0.72 ms
0.96 ms
1.40 ms
4.75 ms
WTh [MJ]
B/B

## Slide 10: Current profile evolution during Ip spike
Current spike is associated with disappearance of reversed current regions after “flux trapping” in still warm plasma
*“Negative voltage spike in tokamak disruptions”
J.A. Wesson et al (1990) Nucl. Fusion 30 1011

## Slide 11: RE confinement time drops to ~μs
Fastest rate of RE losses is just prior to current spike
N (eq)
RE test particle losses vs. time
~ms confinement (at speed of light)
~μs confinement (at speed of light)

## Slide 12: 100% RE loss is not typical for DIII-D rapid shutdown simulations
Simulations with uniform or edge-localized impurity delivery in DIII-D typically retain some fraction of RE test particles after flux surfaces re-heal at end of TQ

## Slide 13: Summary of Part I
Inside out TQ characterized by rapid loss of core thermal energy followed by slow drop in edge Te
Ring of reversed current forms outside of current channel and expands outward
Destabilization and loss of reversed current ring at end of TQ produces current spike, large magnetic fluctuations, and very rapid loss of remaining RE population

## Slide 14: Outline
Part I: Phenomenology of an inside out TQ
 Simulation results with constant shell ablation rate, near-axis payload delivery
Part II: Preliminary results with plasma parameter dependent ablation rates
 Dual shell pellet injection simulations

## Slide 15: Shell pellet ablation model
Temperature and density dependent shell ablation given as:
dN/dt (atoms/s) = Cabl T5/3 n1/3 *
rp (pellet radius) dependence neglected due to thin shell, payload delivery triggered by total ablated quantity threshold
Coefficient is presently a free parameter: With T in eV, n in cm-3, Cabl=1.2x1013 chosen for payload delivery near axis @ 200 m/s
NGS* (H pellet) with Mi=12, rp=0.36cm gives Cabl=1.25x1015
*P. B. Parks, and R. J. Turnbull, The Physics of Fluids 21, 1735 (1978); doi: 10.1063/1.862088

## Slide 16
Two simultaneous shell pellets separated by 180 are launched with 5% difference in velocity
Q. Will payload release of the faster pellet prevent payload release of the slower pellet?
 | Pellet 1 | Pellet 2
 (deg) | 0 | 180
V (m/s) | 420 | 400
Nshell | 50% | 50%
Npayload | 50% | 50%

## Slide 17
Two simultaneous shell pellets separated by 180 are launched with 5% difference in velocity
Q. Will payload release of the faster pellet prevent payload release of the slower pellet?
A. The slower pellet released its payload first!
 | Pellet 1 | Pellet 2
 (deg) | 0 | 180
V (m/s) | 400 | 420
Nshell | 50% | 50%
Npayload | 50% | 50%
tpayload (ms) | 1.09 | 1.21

## Slide 18: Sudden increase of slow pellet ablation rate corresponding to growth of unstable MHD
Slower Pellet
Faster Pellet
Total ablated material from each pellet (# atoms)
Time [ms]

## Slide 19: Increase of slow pellet ablation rate corresponding to growth of unstable MHD
B/B

## Slide 20: Unstable modes distort/shift hot core away from faster pellet toward slower pellet
Slower Pellet
Faster Pellet
n=3
Temperature (eV)
Time = 0.95 ms
=180
=0

## Slide 21: Consistent with observations of 1/1 phase in MGI simulations
From IAEA 2014 presentation on MGI simulations
General finding from MGI simulations with NIMROD was that core modes triggered by gas jets tend to be phased such that they push hot core away from injected gas

## Slide 22: Summary of Part II & Conclusion
In dual DSP simulation, both payloads are delivered
Interaction between two simultaneous shell pellets could be mediated by MHD triggered by shell material
DSP simulations show : radiation of core thermal energy while maintaining edge confinement , fast loss of REs at end of TQ, potential for multiple DSPs