## Slide 1
S.A. Sabbagh1, J.W. Berkery1, Y.S. Park1, J.H. Ahn1, J.D. Riquezes1, J. Butt1, J.M. Bialek1, Y. Jiang1, J.G. Bak2, S.H. Hahn2, J. Kim2, J. Ko2, W.H. Ko2, J.H. Lee3, S.W. Yoon3, C. Ham3, A. Kirk3, L. Kogan3, D. Ryan3, A. Thornton2, M.D. Boyer4, K. Erickson4, Z.R. Wang4
V1.5
1Department of Applied Physics, Columbia University, New York, NY
2Culham Centre for Fusion Energy, UKAEA, Abingdon, UK
3National Fusion Research Institute, Daejeon, Republic of Korea
4Princeton Plasma Physics Laboratory, Princeton, NJ
Progress on Tokamak Disruption Event Characterization and Forecasting Research and Expansion to Real-Time Application
IAEA Technical Meeting on Plasma Disruptions and their Mitigation
20-23 July 2020
St. Paul-lez-Durance, France

## Slide 2: A broadened disruption prediction and avoidance analysis is progressing for ITER and future tokamaks
Motivation: Disruption prediction/avoidance is a critical need
  Why? A disruption stops plasma operation, might cause device damage
  A highest priority DOE FES (Tier 1) initiative - present “grand challenge” in tokamak stability research:
    Can be done! (JET: < 4% disruptions with carbon wall)
    ITER disruption allowance: < 1 - 2% (energy + E&M loads); << 1% (runaways)
Outline
  Disruption Event Characterization and Forecasting (DECAF) approach
  Overview of DECAF results, disruption event chains, early forecasting
  Initial multiple-device, large database analysis, forecasting performance
  Physics support research: i.e. KSTAR high bN, D’, ~100% non-inductive CD
  Recent focus on real-time design and implementation on KSTAR

## Slide 3: DECAF is a logical, physics-based paradigm that meets all disruption predictor requirement metrics
Disruption predictor must
  Predict SPECIFIC pre-disruptive phenomena  link to control
  Provide CONTINUOUS variable quantifying proximity (& can GENERATE triggers)
  Provide SUFFICIENT LEAD TIME for mitigation or avoidance
  Be EXTRAPOLABLE to new device (e.g. ITER) prior to operation
  Be REAL-TIME calculable
D. Humphreys, et al., PoP 22 (2015) 021806
DECAF in disruption prediction / avoidance framework
DECAF

## Slide 4
DECAF follows disruption event framework (de Vries) to provide understanding of disruption chains  automates it
P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018
JET disruption event chains
Related disruption event statistics
JET disruption event chain analysis performed by hand, desire to automate
General code DECAF: automates event chain process, provides disruption warning signals, being validated against databases from multiple devices

## Slide 5: DECAF is structured to ease parallel development of disruption characterization, event criteria, and forecasting
Physical event modules encapsulate disruption chain events
  Development focused on improving these modules
  Structure eases parallel development incl. real-time
Physical events are objects in physics modules
  e.g. VDE, LOQ, RWM are objects in “Stability”
  Python “objects” having attributes and methods
  Carry metadata, event forecasting criteria, event linkages, etc.
Main data structure
Code control workbooks
Density Limits
Confinement
Stability
Tokamak dynamics
Power/current handling
Technical issues
Physical event modules
Output processing
Tokamak databases
DECAF database

## Slide 6: DECAF is structured to ease parallel development of disruption characterization, event criteria, and forecasting
Physical event modules encapsulate disruption chain events. Examples:
Main data structure
Code control workbooks
Density Limits
Confinement
Stability
Tokamak dynamics
Power/current handling
Technical issues
Physical event modules
Output processing
Tokamak databases
DECAF database
VDE
DIS
IPR
HLB
GWL
IPB
LON
PRP
LTM
RWM
RKM
MHD
BIF
LOQ
WPC
Greenwald limit
Island power balance
Low density
H-L back-transition
MHD
Bifurcation
Locked mode
VDE
Pressure peaking
Low q
RWM and
Kinetic RWM
forecasting
Not at requested Ip
Wall proximity control
Disruption

## Slide 7: DECAF connected to databases from multiple machines, expanding analysis
Analysis
  Density limits
  Ideal, kinetic, resistive MHD stability
  Rotating MHD, etc.
DECAF database started
  Presently ~50 TB stored
Device / Capability | KSTAR | MAST | NSTX | DIII-D | AUG, TCV
Full database access (required!) | Yes (MDSplus) | Yes (UDA) | Yes (MDSplus) | Yes (MDSplus) | Yes (MDSplus)
Database analysis | continuing | continuing | continuing |  | 
Equilibrium analysis | Magnetic, Kinetic + MSE | Magnetic, Kinetic + MSE | Magnetic, Kinetic + MSE | available | 
Stability | Ideal, Resistive Kinetic MHD | Ideal (so far) | Ideal, kinetic MHD (resistive) | Ideal, kinetic MHD | 
shot*seconds (for kinetic analysis) | ~ 3,880 (2016-2018) | 2,667 (est) (M5 - M9 runs) | 2,000 / year (est) |  | 
Now, full access interface to AUG database; expanding to others
  100 shot LTM disruption database by V. Klevarova analyzed for
AUG

## Slide 8: DECAF now connected to databases from multiple machines, expanding analysis
Analysis
  Density limits
  Ideal, kinetic, resistive MHD stability
  Rotating MHD, etc.
DECAF database started
  Presently ~50 TB stored
Device / Capability | KSTAR | MAST | NSTX | DIII-D | AUG, TCV
Full database access (required!) | Yes (MDSplus) | Yes (UDA) | Yes (MDSplus) | Yes (MDSplus) | Yes (MDSplus)
Database analysis | continuing | continuing | continuing |  | 
Equilibrium analysis | Magnetic, Kinetic + MSE | Magnetic, Kinetic + MSE | Magnetic, Kinetic + MSE | available | 
Stability | Ideal, Resistive Kinetic MHD | Ideal (so far) | Ideal, kinetic MHD (resistive) | Ideal, kinetic MHD | 
shot*seconds (for kinetic analysis) | ~ 3,880 (2016-2018) | 2,667 (est) (M5 - M9 runs) | 2,000 / year (est) |  | 
Now, full access interface to AUG database; expanding to others
  100 shot LTM disruption database by V. Klevarova analyzed for
AUG
(100 shot LTM database)

## Slide 9: DECAF MHD events utilize history of 15 criteria to define time evolving disruption warning level
MHD-n1
MHD-n3
MHD-n2
DECAF automated MHD objects
LTM-n1
LTM-n2
BIF-n1
BIF-n2
DECAF “heat map” (for MHD)
“quasi-steady
state (O)”
Very low f mode 
f below bifurcation 
 High amplitude 
Decreasing plasma rotation 
 Core plasma rotation < 6 kHz 
Locked mode > 25G 
Key notables of MHD warning
  “Safe”/“unsafe” MHD periods found
  Early, slow warning level evolution
    Locked mode amplitude important, but warning comes in very late
  Mode frequency below bifurcation, decreasing plasma rotation key
DECAF MHD warning level
Safe

## Slide 10: DECAF provides an early disruption forecast - on transport timescales – giving potential for disruption avoidance
DECAF event chain reveals physics
  Rotating MHD slows, bifurcates, and locks
126962
Disruption forecast level
DECAF MHD events
MHD-n1
PRP
DIS
IPR
WPC
VDE
(0.490s)
BIF-n1
LTM-n1
(+.068s)
(+.073s)
(+.073s)
(+.077s)
(+.080s)
(+.005s)
(+.045s)
DECAF event chain
  Then, plasma has an H-L back-transition (pressure peaking warning PRP) before DIS
  Important: Early warning occurs in apparently SAFE region of operating space!
NSTX
Safe
n
1
2
3

## Slide 11: Example: DECAF shows plasma parameters of VDE event can occur far from those of DIS event
Largest portion of detected VDE events appear at (li,k) with very small portion of DIS events detected
NSTX

## Slide 12: DECAF MHD events also produce early disruption warnings for KSTAR
DECAF automated MHD objects
DECAF “heat map” (for MHD)
Mode locking at reduced plasma rotation
Key notables of MHD warning
  “Safe”/“unsafe” MHD periods
  Early disruption warning (300 ms)  on transport timescale
MHD warning level
Safe
KSTAR
16299
MHD-n1
MHD-n2
Very low frequency mode 
Plasma rotation profile
and dynamics
High amplitude mode 
}
Decreasing bN 
condition
time (s)
frequency (kHz)
warning level
n
1
2
3

## Slide 13: New “reduced” locked tearing mode event being created, aimed for real-time use / comparison
Using pickup coils and partial saddle loops
Compare to full FFT approach
Warning level criteria
  Pickup coil amplitude > 5 T/s
  Low zero-crossing measured frequency < 5 kHz
  High mode identified saddle loops amplitude > 20 G
NSTX 127733
DECAF “heat map” (for LTM v2)
Pickup loop > 5 T/s
Frequency < 5 kHz
LTM
(version 2)
t (s)
n = 1 saddle loop > 20 G
n = 2 saddle loop > 20 G
n = 3 saddle loop > 20 G
Warning level
0.
warning critera

## Slide 14: New DECAF edge localized mode event created to start examining correlations to other MHD
DECAF ELM event
  Presently determines ELM triggering times, along with frequency and relative amplitude
Near-term-goals
  Determine greater understanding between ELM triggering and more deleterious MHD excitation
Compatible with real-time use
ELM

## Slide 15: A density limit model has been examined in DECAF based on power balance in an island
Power density balance:
D. Gates et al., Phys. Rev. Lett. 108 165004 (2012)
Local island power balance limit
  Power balance in island between Ohmic heating and radiated power loss
  If radiated power at the island exceeds the input power (Ploss > Pinput), island grows
NSTX
134020

## Slide 16: Initial assessment of density limit model shows correlation with MHD events
DECAF automated MHD events
MHD-n1
MHD-n3
MHD-n2
Magnetic spectrogram
(toroidal array)
GWL
IPB
0.9
NSTX
Greenwald limit
  Near 0.9 when mode starts (range 0.75 – 1.05)
Rad. island power balance
  Near 1.0 when mode starts (range 0.60 – 1.50)  next step: reduce range

## Slide 17: Limited event chain analysis of large databases evolves initial performance of disruption prediction
First test on large, general database
Analysis with only 5 DECAF events tested for 10,094 discharges with disruptions (NSTX)
  Events used: VDE, GWL, LOQ, IPR, DIS
Performance (Model 3)
  91.2% true positives (warning occurs)
  8.7% false negatives (no warning)
    Somewhat high number of false negatives expected: only 5 DECAF events are used in this large database analysis
In 5,909 shots, vertical instability is part of the disruption chain
DECAF Disruption Forecasting Performance Evolution
greater realism
ITER need
~10 events, ~102 shots*s
(initial event validation)
~10 events, ~102 shots*s
(earlier forecasting)
5 events
~104 shots*s
(general database)
VDE

## Slide 18: DECAF is fueled by coordinated research that continues to validate/develop physics models, e.g.:
Resistive MHD
  Detection / forecasting: available magnetic diagnostics, plasma rotation
  Forecasting: starting examination of MRE  start with D’ evaluation
Density limits
  Detection: rad. power, global empirical limit
  Forecasting: starting examination of rad. island power balance model
Global MHD
  Detection: available magnetic diagnostics, plasma rotation, equilibrium
  Forecasting: Kinetic MHD model has high success in NSTX, DIII-D
Physics analysis / experiments to build DECAF models
  Interpretive and “predict-first” TRANSP analysis of KSTAR long-pulse, high beta plasmas with high non-inductive fraction

## Slide 19: Tearing mode classical D’ stability examined in KSTAR plasmas (supports future DECAF models)
16325
Classical tearing stability index, D′, computed at q = 2 surface using outer layer solutions
At higher q95, D′ is mostly positive predicting unstable classical tearing mode
  Indicates neoclassical effects, additional physics needed to reproduce XP
  KEY POINT: Conclusions regarding D’ evolution can be made!
    Recent paper with MRE evaluation  Y.S. Park, et al., NF 60 (2020) 056007
Experimentally
2/1 stable
*Resistive DCON
bN ~ 2
Ideal DCON dW
bN ~ 2
16325
*A.H. Glasser PoP (2016)

## Slide 20: A database of high-non-inductive fraction plasmas is important for disruption forecasting ; NICF ~ 75% in KSTAR
18492
16498
18476
16325
16295
TRANSP analysis of experimental plasmas
Non-inductive fraction
  Beam-driven
  Bootstrap
Non-inductive fraction is key for stable high beta steady state operation
Volume average electron density (m-3)

## Slide 21: “Predict-first” KSTAR TRANSP analysis shows expected high performance plasmas at > 80% NICF
High non-inductive current fraction predicted for 6.5, 7.5, 8.5 MW NBI
  The bN ranges from 3.0 – 3.5; based on KSTAR plasmas with NICF ~70%
Aim to generate a significant database of long pulse, high NICF plasmas in 2020-2021 KSTAR runs for disruption prediction studies
Predicted high non-inductive current fraction (NICF) current profiles
81.5% NICF
93% NICF
101% NICF

## Slide 22: Machine learning approaches are now coupling to DECAF to compute sub-elements of computations
Determination of ideal MHD no-wall stability limit by DL NN
(2019 Marseille conference)
Determination of ideal MHD stability function by non-linear random forest regression
(2019 IAEA ML conference)
Collaboration with CCFE / UCL (A. Piccone (UCL));  A. Piccone, et al, Nucl. Fusion 60 (2020) 046033
FES/ACSR Advancing Fusion with Machine Learning - Research Needs Workshop (May 2019)

## Slide 23: Disruption prediction and avoidance research on KSTAR moving to real-time application
Disruption forecasting physics analysis expansion
Implementation of real-time diagnostic capabilities
Real-time implementation of DECAF analysis and sensor input
  Plasma control system (PCS) code specifications written for 10 DECAF events – process continues
Real-time control leveraging real-time DECAF analysis and sensors
  Initial specification for model-based control in the PCS is written; interfaces to DECAF events being made
Next slides

## Slide 24: KSTAR DPA grant research “fills in” the desired real-time (r/t) diagnostic capability for r/t DECAF
Real-time measurement of rotating / locking MHD
  < 300 kHz; Data collected during Jan/Feb 2020 run
Real-time and offline Motional Stark Effect - IN FINAL DESIGN
  “offline” MSE background polychrometer system, Zeff profile
  Real-time implementation of MSE; includes dB profile measurement
Real-time plasma rotation profile – 1st system shipped to NFRI
  Completely new for KSTAR: 8 channels; 1 – 2 kHz time resolution
Real-time electron temperature profile – IN PROCUREMENT
  Implement real-time acquisition of heterodyne radiometer system
Real-time Te fluctuation profile – IN PROCUREMENT
  Implement real-time acquisition to 2-D ECE imaging system

## Slide 25: Overall setup for KSTAR real-time diagnostic integration and DECAF analysis for the PCS
All software development under GIT version control
Main Diagnostics Room
PCS Room
KSTAR Test Cell / ECE Screen Room
A-to-D (192 ch)
Expansion box connected to main ECEI r/t computer
r/t ECEI and r/t DECAF development computer
rtDECAF
Optical isolation
(Dolphin)
1G to KSTAR imaging data server & MDSPlus
r/t MHD computer
rtDECAF
r/t ECE computer (includes Te(R) calibrations 73 ch)
r/t Vf computer (includes profile calibration 8 ch)
r/t MSE computer (includes profile calibration 25 ch)
KSTAR PCS
RFM
Dolphin
r/t DECAF development computer
rtDECAF
1G to MDSPlus
RFM
Dolphin
RFM
Dolphin
1G to MDSPlus
v1.0s
RFM
RFM
RFM
Dolphin
Dolphin
Dolphin
1G to MDSPlus
1G to MDSPlus
1G to MDSPlus

## Slide 26: Disruption prediction and avoidance research on KSTAR moving to real-time application
Real-time MHD analysis computer installed at NFRI
  Designed for connection to plasma control system (PCS)
  Interface to MHD probes built
Real-time magnetic probe data acquired
(14 toroidal probes: n = 1 rotating field applied)
Offline DECAF analysis of real-time signals
0.05 kHz
0.10 kHz
0.20 kHz
n
1
2
3
DECAF spectrogram
0.05 kHz
0.10 kHz
0.20 kHz
DECAF mode decomposition
t(s)
0.05kHz
0.10 kHz
0.20 kHz
n
1
2
3

## Slide 27: KSTAR real-time MHD computer acquired data for 2019 campaign – data quality as good as offline
Frequency (kHz)
Amplitude (G)
Offline data, native code analysis
Frequency (kHz)
Frequency (kHz)
Real-time data, DECAF analysis (offline)
n
1
2
3
n
1
2
3
Spectrogram
DECAF object decomposition
~ 2 G
amplitude

## Slide 28: Analysis of KSTAR real-time MHD computer data compared to simulated FPGA* r/t analysis (I)
DECAF analysis using various inputs
Δt = 3.06 ms , Δf = 0.31 kHz (offline analysis set to match FPGA)
From simulated FPGA FFTs
From offline FFTs
*FPGA: field-programmable gate array

## Slide 29: DECAF object decompoition of r/t MHD computer data works well on simulated FPGA analysis
DECAF object decomposition
From simulated FPGA FFTs
From offline FFTs
n
1
2
3
n
1
2
3

## Slide 30: New real-time velocity diagnostic for KSTAR expands design of NSTX-U system (operated in 2016)
post-discharge
real-time
R~112cm
NSTX-U: demonstrated RT analysis for vf, Ti (for Ti>150eV)
  4 radial channels, active + backgrd, 5 kHz
KSTAR: plan for 8 radial channels, ~1kHz sampling rate
  Assess requirements in FY20 to optimize design & analysis software
  Re-locate NSTX-U system, interface w/ KSTAR
Status / plan
  NSTX-U system shipped to KSTAR (arrival this Wed July 22nd evening)
  Use data from initial system for final design of new KSTAR system
  Install new KSTAR system 2021
M. Podesta (PPPL)

## Slide 31: Expanding DECAF approach provides a new paradigm for disruption avoidance research
Multi-device, integrated approach to disruption prediction and avoidance that meets disruption predictor requirement metrics
  Physics-based “event chain” yields key understanding of evolution toward disruptions needed for confident extrapolation of forecasting, control
  Present performance on large (104) databases: 91.2% w/ only 5 Events
  Full multi-machine databases used (full databases needed!)
  Innovative use of machine learning started (event analysis, pred. models)
  Physics analysis, experiments run to understand, create, validate models
DECAF producing early warning disruption forecasts
  On transport timescales:  guide disruption avoidance by profile control
Continuing development
  Improve DECAF forecasting performance run on large database analysis
  Continue / expand disruption forecasting performance analysis ( ITER)
  Implement DECAF disruption forecasting models in real-time ( KSTAR)

## Slide 32: Supporting slides follow

## Slide 33: Simple island rotation dynamics model presently being constructed to forecast the bifurcation point
Start with cylindrical, rigid body model
Possible model of drag for both a “slip” and a “no slip” condition:
At very low angular speed mode reaches a stable steady state,  investigating this in KSTAR
Collaborating with UW Madison theoreticians to add explicit effect of island size on viscosity, toroidal effects, etc.
R. Fitzpatrick et al., Nucl. Fusion 33 (1993) 1049
Bifurcation

## Slide 34: Predictive TRANSP analysis shows KSTAR design target ~5 can be approached with ~100%
<TRANSP>
bN = 3.4
fNI = 96%
PNBI = 6.5 MW
Up to 75% NICF already reached in similar plasmas
NBI  6.5 MW in 2018
By altering and values, , up to KSTAR design target 5 can be achieved with 100% NICF
n=1 no-wall limit
n=1 with-wall limit
/=6
/=5
=1.5T
Predicted
=2.0T
=1.7T
Interpretive
“Predict-first” analysis used to design high-β , 100% non-inductive current fraction (NICF) experiments for present KSTAR run campaign
See J-H Ahn CO6.00005

## Slide 35: DECAF reduced kinetic MHD model provides early forecast of instability boundary to global MHD modes
Favorable characteristics
  Stability contours CHANGE for each time point
  Model allows real-time stability and mode growth rate prediction
ideal
Ideal + kinetic
unstable
stable
Norm. growth rate vs. time
gtw
139514
disruption
predicted instability
J.W. Berkery, S.A. Sabbagh, R. Bell, et al., Phys. Plasmas 24 (2017) 056103
Disruption forecasting
Global kinetic MHD mode growth
gtw
Increasing time
Collisionality (kHz)
Rotation
Predicted instability statistics
84% of shots are predicted unstable (stringent evaluation)
44% predicted unstable < 320 ms (approx. 60tw) before current quench
33% predicted unstable within 100ms of a minor disruption
NSTX

## Slide 36: DECAF analysis of large databases further supports published results that disruptivity doesn’t increase with βN
DECAF analysis of event
  Shots analyzed at 10 ms intervals
Analysis during Ip flat-top
  MAST: 8,902 plasmas analyzed
  NSTX: 10,432 plasmas analyzed
  KSTAR: 1,309 plasmas analyzed
DIS
MAST
NSTX
KSTAR

## Slide 37: Initial analysis of large databases further supports published result that disruptivity doesn’t increase with plasma β
DECAF analysis of event
  Similar to a “standard” disruptivity analysis
  Shots analyzed at 10 ms intervals
Analysis during Ip flat-top
  MAST: 8,902 plasmas analyzed
  NSTX: 10,432 plasmas analyzed
  KSTAR: 1,309 plasmas analyzed
MAST
NSTX
KSTAR
DIS

## Slide 38: Global MHD modes can also be “slow” and allow early warnings for disruptions, potentially allowing avoidance
123856
DECAF rotating MHD warning level
IPR
DIS
PRP
VDE
RWM
LOQ
(0.629s)
(+.010s)
(+.012s)
(+.058s)
(+.101s)
(+.101s)
(+.107s)
MHD-n1
LTM-n1
WPC
(+.106s)
(+.101s)
DECAF event chain
Global MHD (RWM) can also be “slow”
  Rotating MHD warning level decreases after 0.46s  DANGEROUS for RWM onset!
  H – L back transition (PRP) drags out time to disruption (> 100 ms – transport timescale)
NSTX
DECAF MHD events
n
1
2
3
Safe

## Slide 39: New 2nd NBI system installed in KSTAR, may be available for 2020 run campaign
90°
Geometry of 2nd NBI system is included in TRANSP model
  Available power
  1.5MW/source
  (conservative)

## Slide 40: Clear pressure profile distinction between Internal Transport Barrier and H-mode phases
Broad pedestal pressure reconstructed in H-mode is not observed in earlier ITB phase
ITB
H-mode
L-mode
2.5
4.8
Xp by Jinil Chung
Safty factor q
1.8 1.9 2.0 2.1 2.2 2.3
R (m)
Total Pressure (105Pa)
0.0 0.2 0.4 0.6 0.8 1.0
yN
15
10
5
0
1.8 1.9 2.0 2.1 2.2 2.3
R (m)
1.2
1.0
0.8
0.6
0.4
2
0.0
-0.2
16498
0.0 0.2 0.4 0.6 0.8 1.0
yN
15
10
5
0
Safety factor
t = 2.5s
Safety factor
t = 4.8s
Total Pressure
t = 2.5s
Total Pressure
t = 4.8s
1.2
1.0
0.8
0.6
0.4
2
0.0
-0.2
△ data
— fitted
△ data
— fitted
t = 2.5s
t = 4.8s
ITB phase
H-mode phase