## Slide 1: Characterization of helical tomotherapy plans complexity
Tania Santos1,2, Tiago Ventura2, Josefina Mateus2, Miguel Capela2
1 Physics Department, University of Coimbra, Portugal
2 Medical Physics Department, IPOCFG, E.P.E., Portugal
ICARO-3
16-19 February, 2021
# INDICO 16

## Slide 2: Conflict of interest statement
The authors have no conflict of interest to declare.

## Slide 3: Objectives
The aim of this work was to evaluate the complexity of helical tomotherapy (HT) plans using some metrics recently published and assess their potential to predict the plan deliverability.

## Slide 4: What is a complex treatment plan?
H Rocha, et al., 2010, Towards efficient transition from optimized to delivery fluence maps in inverse planning of radiotherapy design, ISSN: 1645-2631
Fluence variability
Weiliang Du, et al. Quantification of beam complexity in intensity-modulated radiation therapy treatment plans, 2014, Med. Phys. 41 (2)
Small, narrow, irregularly shaped and off-axis apertures

## Slide 5
Other technologies such as Tomotherapy?
What is a complex treatment plan?

## Slide 6
Methods
6 complexity metrics were calculated from the planned sinogram of 100 head and neck HT plans
the modulation factor (MF) =
%LOT < 100 ms
indices to assess the leaf open time variations in the sinogram, adapted for HT1:
LOTV: Leaf Open Time Variability
PSTV: Plan Time Sinogram Variation
MI: Modulation Index
%LOT > pT-20 ms
1 Santos T, et al. On the complexity of helical tomotherapy treatment plans. J. Appl. Clin. Med. Phys. 21:7 (2020) 107-118
Notes: The computed parameters included the actual modulation factor (MF). The MF is defined as the ratio between the maximum leaf open time and the mean of all
non-zero leaf opening times. A higher MF allows a larger range of beamlet intensities 6.
The percentage of open leaves with an opening time below 100 ms (%LOT < 100 ms), and the percentage of leaves with an opening time close to the projection duration (%LOT > pT-20 ms) were calculated to characterize the leaf open times distribution. As reported the linear model assumed for the MLC leaf latency is violated for small leaf open times and LOTs approaching the projection duration, which may compromise plan deliverability. Therefore, plans with a higher percentage of leaves with a short LOT and/or approaching the projection time were considered more complex.
To evaluate the modulation of the entire planned sinogram, i.e., the differences in leaf open times, three metrics are proposed. These are extensions to HT of indices previously defined for conventional IMRT techniques. The leaf open time variability (LOTV) that evaluates the variations in leaf open times along the treatment. The Plan Time Sinogram Variation (PSTV), an adaptation of the plan intensity map modulation score proposed by Coselmon et al.11, is computed for a given control point by summing the LOT differences in two directions.
The Modulation Index (MI) 10 was here modified to quantify the leaf open time variations in the planned sinogram in the directions defined by the MLC leaves (𝑥), the projections/control points (𝑦) and the corresponding diagonals (𝑥𝑦, 𝑦𝑥). The number of LOT changes (Δt) between adjacent elements in the four directions that exceed a certain fraction (𝑓) of the standard deviation (𝜎) of the entire planned sinogram.

## Slide 7: Methods
Dosimetry Check software (Math Resolutions, USA) in pre-treatment mode was used to reconstruct the measured dose distribution from the detector signal.
The correlation between the complexity metrics and the pre-treatment verification results was investigated using the Spearman’s rank correlation coefficients rs.
3D global gamma analysis was performed with a 3%/3 mm and 10% threshold (TH) criteria, for a passing rate acceptance limit of 95%. More stringent criteria were also adopted:
  - 3%/2 mm 10% TH
  - 2%/2 mm 10% TH
  - 2%/1 mm 10% TH
Notes: .

## Slide 8
Results
MF=2.096 ± 0.175
%LOT< 100 ms=27.792 ± 3.571
%LOT > pT-20 ms=8.658 ± 3.746
LOTV=0.931 ± 0.010
MI=10.726 ± 0.895
PSTV=5.406 ± 0.729

## Slide 9
Table 1 – Correlation coefficients between the γ passing and the complexity indicators for the HT plans.
 | 3%/3 mm 10%TH |  | 3%/2 mm 10%TH |  | 2%/2 mm 10%TH |  | 2%/1 mm 10%TH | 
 | rs | p-val | rs | p-val | rs | p-val | rs | p-val
MF | 0.102 | 0.312 | 0.059 | 0.562 | -0.072 | 0.474 | -0.111 | 0.271
%LOT < 100 ms | -0.193 | 0.054 | -0.193 | 0.055 | -0.003 | 0.973 | -0.022 | 0.831
%LOT > pT-20 ms | -0.272 | 0.006 | -0.245 | 0.014 | -0.075 | 0.459 | -0.044 | 0.661
LOTV | 0.366 | 0.000 | 0.346 | 0.000 | 0.178 | 0.076 | 0.154 | 0.125
PSTV | -0.347 | 0.000 | -0.337 | 0.001 | -0.139 | 0.169 | -0.128 | 0.206
MI | -0.157 | 0.119 | -0.162 | 0.108 | -0.070 | 0.487 | -0.103 | 0.306
The lack of correlations may be explained by the homogeneity of the considered set of plans, which led to a limited variation of both the complexity indicators and the deliverability results.
Results
All plans were considered clinically deliverable, with an average passing rate of 98.6 ± 1.0 % (3%/3 mm, 10% TH) for the entire group. The use of more stringent criteria for gamma analysis, resulted in a wider spread in the passing rates, as expected.

## Slide 10
Results
1 Santos T, et al. On the complexity of helical tomotherapy treatment plans. J. Appl. Clin. Med. Phys. 21:7 (2020) 107-118
2 Santos T, et al. Evaluation of the complexity of treatment plans from a national IMRT/VMAT audit – Towards a plan complexity score. Phys. Med. 70 (2020) 75-84

## Slide 11: Conclusions
Despite the reported lack of correlations, the complexity indicators values (mean ± standard deviation) can be taken as reference in our clinic to evaluate future plans, given that the pre-treatment QA results of the entire set were all clinically acceptable. This is in line with AAPM recommendations on the need to quantify plans complexity 1,2.
1 Ezzell, G.A., et al. IMRT commissioning: Multiple institution planning and dosimetry comparisons, a report from AAPM Task Group 119. Med. Phys. 36 (2009) 5359-5373
2 Miften, M., et al. Tolerance limits and methodologies for IMRT measurement‐based verification QA: Recommendations of AAPM Task Group No. 218. Med. Phys. 45 (2018) 53-83
Treatment plans with a complexity out of these limits for any of the computed metrics should be further evaluated and eventually be subjected to a more rigorous QA.

## Slide 12
Thank you for your attention!
This work was supported by the Portuguese Foundation for Science and Technology through a PhD grant, SFRH/BD/118929/2016.
UNIÃO EUROPEIA
Fundo Social Europeu