## Slide 1
Review and main outcomes From the experimental program carried on the PLATEAU facility
27/09/2022
David GUENADOU
P. AUBERT, J-P. DESCAMPS, L. CACHON, G. CHIARA, T. GILARDI, M. SADEK, U. BIEDER, H. BHATIA

## Slide 2: ISSUES OF THE ASTRID PROTOTYPE STUDIED ON THE PLATEAU LOOP
Hot Plenum:
Gas entrainment, temperature and velocity fields, stability of the outlet core jet
Sodium Gas Heat Exchanger:
Maldistribution of the flow
Pipes:
Leak, sodium fire
Pump-diagrid pipe:
Cavitation
Experimentations
Studying the new design choices
Validating the code calculations
Experimentations with sodium are very complex
r(Na), m(Na)  r(H2O), m(H2O)
Experimentations with water
MICAS
CALIMEREAU
DANAH
JETSER
4 mock-ups

## Slide 3: WATER/SODIUM SIMILITUDE
Similitude
Equivalence in phenomenology
Froude for the free surface studies
Richardson for the thermal influence
Distortion of the other dimensionless numbers.
Reynolds for the hydraulic aspects
Difficulty to fit the experimental conditions in order to observe all the dimensionless numbers.

## Slide 4: THE PLATEAU LOOP
Mock-up
TA01
TA02
EX01
HEAT01
P01
P02
P03
MCM
TIC
CSC
HSC
1
2
3
3 modes
Hydraulic (T1=T2=T3(°C))
Transitory (T1  or , T2=T3(°C))
Thermohydr. (T1≠T2=T3(°C))
Qmax=400m3/h
T(°C)<60°C
T(°C)=10°C

## Slide 5: MICAS MODEL – HOT PLENUM
Pump pit
IHX
Core
ACS
ACS
IHX1
P03
IHX4
IHX3
IHX2
P01
P02
Core
ACS: Above Core Structure
IHX: Intermediate Heat Exchanger
P0x: Pump n°x
Sector : 360° ; Scale : 1/6
3 flow distribution zones in the MICAS core: fission zone, reflector and internal assembly storage.
Built in transparent polymer (PMMA) for optical measurements
External vessel made of 12 plane walls to enhance the optical access
External vessel
Fission
Reflector
Int. Stor.

## Slide 6: VELOCITY MEASUREMENT - EXPERIMENTAL SETUP
Particle Image Velocity
Average velocities (10 s at 15 Hz)
Laser
Camera
Laser sheet
External pool
Plug
Cask
IHX4
ACS
Core
CD camera (4 Mpix)
Double pulse laser
External pool
0°
90°
270°
IHX1
IHX2
IHX3
P01
P02
P03
The external pool reduces the optical deformations
Optical access lessened by obstacles (immerged components…)

## Slide 7: CODE VALIDATION
Computations proceed with TrioCFD prior the experimental campaign in order to avoid any influence
Slight differences, but rather good accordance in terms on flow direction and magnitude
Experimental
Numerical

## Slide 8: GAS ENTRAINEMENT
Gas accumulation in the diagrid may lead to safety problems if a gas pocket is released into the core (positive reactivity effect)
One of the origins of gas due to vortices created at the free surface in the upper plenum
CFD codes do not handle vortex in complex structures because of the multiphase flow aspect
Development of a simple model based on the Burger vortex model
Gas entrainment when the vortex length Lgc reaches the outlet depth h
Need of a and G

## Slide 9: GAS ENTRAINEMENT
Chart: Radius (mm)
Model | 0.12856 | 0.13223 | 0.13612 | 0.14025 | 0.14463 | 0.14929 | 0.15426 | 0.15957 | 0.16524 | 0.17133 | 0.17785 | 0.18485 | 0.19235 | 0.2004 | 0.20899 | 0.21813 | 0.22778 | 0.23785 | 0.24823 | 0.25871 | 0.269 | 0.27873 | 0.28741 | 0.29447 | 0.29924 | 0.301 | 0.299 | 0.29251 | 0.28091 | 0.2637 | 0.24062 | 0.21167 | 0.17714 | 0.13767
Derivative null at the maximum velocity
a, G
No gas entrainment for a.G2<4.5
Theoretical value a.G2<228
Vortex center

## Slide 10: FLOW BEHAVIOR VS OPERATING CONDITIONS
Flow fluctuations in the upper plenum induce thermal oscillations in the immerged components that lead to thermal fatigue and reactor lifetime decrease
Jet outgoing the core subject to oscillation when it rises to the surface
Experiments carried out on the MICAS mock-up to investigate the range of the operating conditions for which it occurs
Study based on the Richardson number and PIV measurements
Ri’=1
Ri’=25
a
a

## Slide 11: FLOW BEHAVIOR VS OPERATING CONDITIONS
Chart: Ri'
| 27.467261003121919 | 12.609162194664043 | 7.00886126540051 | 4.5279288306350569 | 3.0784644249779101 | 2.2589271953942802 | 1.7230796802361861 | 1.3847542686123162 | 1.0946324918269859 | 12.609162194664043 | 1.0946324918269859
Jet - Max | -0.31187 | 0.18698 | 0.26155 | 0.28942 | 0.24875 | 0.24791 | 0.3064 | 0.27287 | 0.23641 | 0.11545 | 0.26577
Jet - Mean | -0.32983 | 0.19076 | 0.24253 | 0.2749 | 0.31313 | 0.29124 | 0.29519 | 0.26344 | 0.2288 | 0.1348 | 0.27072
Transition to a rising jet for a value between 13<Ri’<27
Ongoing studies to identify if this result can be transposed to higher scales

## Slide 12: SODIUM GAS EXCHANGER
Gas turbine (Brayton cycle) to avoid Na/water issues
Gas pumping power has a first order impact on the Brayton cycle efficiency
Optimisation of the sodium/gas heat exchanger
Maldistribution of the sodium flow rate in the Na channels
72 Na channels layers intercalated with 72 gas channel layers
3 x 6 mm2 Na cross section
2.2m
Decrease of the global efficiency of the exchanger
Optimization of the geometry of the Na header using CFD (ANSYS-Fluent)
Needs of experimental validations

## Slide 13: DANAH MOCK-UP
Scale 1 the inlet header
Half of the channels bundle with a representative pressure loss
Possibility to change the header geometry
Built in PMMA
Velocity measured by both PIV and LDV technics
Header
Channels
Inlet
Outlet
DP

## Slide 14: SIMULATION VS EXPERIMENT
Experiment
Simulation
Header
Outlet
Good agreement
Optimizing the geometry of the SGE with CFD
Maldistribution
25%2%

## Slide 15: SODIUM LEAKAGE
Sodium jet may burn in contact with air in respect of the flow behavior
The intensity of the fire depends mainly on the degree of fragmentation, which impacts on the surface of contact with air
First step: experiment with water in JET-SER (Na at IGCAR)
Jet
Lighting device
Hydrophobic windows for visualisation of the jet
Shadowscopy device to measure the shape of the jet and the droplets size in the whole mock-up volume
Influence of the angle of the jet, the nozzle diameter and the flow rate

## Slide 16: JET BREAK-UP

## Slide 17: JET BREAK-UP
Nozzle outlet
Growth of the amount and the size of droplets along the jet.
An increase of the velocity at the nozzle exit enhances the fragmentation by generating smaller and more numerous droplets that leads to higher surface of exchange.
Correlation of the model developed by Wu with a slight adjustment parameters for downward jets
For horizontal and upward jets when the gravity takes place, the Wu model only valid near the nozzle exit (gravity induces smaller fragmentation)
Good agreement with the experimental results in terms of droplet diameter with preliminary calculations proceeded with NEPTUNE_CFD

## Slide 18: CAVITATION IN THE PUMP-DIAGRID PIPES
ASTRID pump-diagrid pipe ram shaped design (to spare space)
Cavitation in the elbows prohibited because of the erosion by gas bubbles
Onset of the cavitation?
Record of the noise induced when the cavitation occurs by fast pressure sensors and accelerometers
Fast pressure sensors
Cavitation
Pump
Diagrid
Diagrid
(Actual design property of Framatome)

## Slide 19: CAVITATION IN THE PUMP-DIAGRID PIPES
Cavitation number (Thoma):
Saturation pressure
Chart: sc
| 4.1552182911205202 | 4.2419434315561197 | 4.3397063171380701 | 4.61082093229526 | 4.52488420222726 | 5.0023652311027904 | 4.9597910712525799 | 5.0895831280181296 | 5.6081600473046196 | 5.4792549522026199 | 5.6951808416280603 | 6.3861239775302998 | 6.1709864984724501 | 6.5594757071055501 | 7.2076475805656797 | 7.5530698728688197 | 8.2008475411451602 | 8.7622942741696992 | 10.790972701291 | 11.6975460727308 | 13.035281363949901 | 14.200748989849201 | 17.222627377550001 | 17.351729575243901 | 18.9487533261062 | 26.330738149206599 | 29.050261160934198 | 29.136197891002201
Acc. 1 leg | 2581.0502 | 2549.0868 | 1622.1461 | 639.2694 | 607.3059 | 391.5525 | 343.6073 | 319.6347 | 271.6895 | 223.7443 | 215.7534 | 191.7808 | 135.8447 | 135.8447 | 79.9087 | 71.9178 | 47.9452 | 23.9726 | 31.9635 | 23.9726 | 55.9361 | 55.9361 | 31.9635 | 63.9269 | 71.9178 | 15.9817 | 7.9909 | 39.9543
Acc. 2 legs | 103.8813 | 55.9361 | 63.9269 | 47.9452 | 63.9269 | 55.9361
Pressure | 18.0822 | 15.2055 | 14.3379 | 11.2329 | 10.7306 | 10.274 | 8.5388 | 8.1735 | 6.9863 | 6.9863 | 6.5297 | 5.7078 | 4.8858 | 5.2055 | 3.6073 | 4.9315 | 3.9269 | 3.4703 | 2.968 | 2.5114 | 1.6438
2 geometries tested: 1 or 2 legs
Onset of the cavitation for a value around 7 for the one leg configuration
Cavitation not reached for 2 legs (flow limit of the pump)
Transposition to the Na case to be studied

## Slide 20: CONCLUSION
Hot plenum (MICAS mock-up): Experimental vs numerical  code validation; Model to forecast the gas entrainment
Sodium gas exchanger optimization: Validations from the experiments of the CFD calculations
Pipe leakage in the framework of sodium fire: Study of the droplet sizes and velocities during the jet break-up; Good correlation with a model from the literature; Implementation of this model in a CFD code
Cavitation in pump diagrid pipe: investigation with accelerometer and pressure sensors; Cavitation for s=7
Transposition of these results to higher scale (?)
PLATEAU loop applicant in the framework of EU program to welcome new experiment or mock-up from EU labs.

## Slide 21: Thank you for your attention

## Slide 22
22
22

## Slide 23: DANAH CFD Calculations
Mass flow inlet (25 kg/s)
Symmetry
Non slipping walls
Porous media
(30 mm  DP=5000 Pa)
Pressure outlet
(0 Pa)
Chart: Axial distance (mm)

## Slide 24: Break-up calculations
NEPTUNE_CFD code
Implentation of the Wu model to calculate the droplet diameter
Chart: Y (m)
| -0.161042342076824 | -0.43819137439826999 | -0.64170350722074798 | -0.87431476569407596
Experimental | 1.2586 | 2.0517 | 2.3793 | 2.8448
CDF | 1.2363 | 2.0717 | 2.4936 | 2.9976 | 3.1518
Wu model | 0.015806 | 1.047 | 1.2721 | 1.7221 | 2.2016 | 2.6712 | 2.8669 | 2.9647 | 3.5224 | 3.9236