## Slide 1
Akihiro Uchibori1, Joji Sogabe1, Yasushi Okano1, Takashi Takata2,
Norihiro Doda1, Masaaki Tanaka1, Yasuhiro Enuma1, Takashi Wakai1,
Tai Asayama1, Hiroyuki Ohshima1
1Japan Atomic Energy Agency
2The University of Tokyo
Development of Plant Lifecycle Optimization Method,
ARKADIA for Advanced Reactors
Technical Meeting on State-of-the-art Thermal Hydraulics of Fast Reactors
C. R. ENEA, Camugnano, Italy and Virtual, September 26-30, 2022.

## Slide 2: Contents
Development of ARKADIA
  Development motivation
  Evaluation flow and system structure
  ARKADIA-Design and -Safety
Simulation technologies of ARKADIA-Design
  Module structure
  Validation analyses
Simulation technologies of ARKADIA-Safety
  Development motivation
  Numerical models
  Functional test analysis
Summary

## Slide 3
Development of ARKADIA
  Development motivation
  Evaluation flow and system structure
  ARKADIA-Design and -Safety
Simulation technologies of ARKADIA-Design
  Module structure
  Validation analyses
Simulation technologies of ARKADIA-Safety
  Development motivation
  Numerical models
  Functional test analysis
Summary

## Slide 4: What is ARKADIA ?
Knowledge base that stores insights from past nuclear reactor development projects and R&D
State-of-the-art computational methods linked with the knowledge base and AI*
Advanced Reactor Knowledge- and AI-aided Design Integration Approach through the whole plant lifecycle
Automatic optimization of plant design including safety measures from various perspectives such as safety and economics
* Artificial Intelligence

## Slide 5: Development motivation
Support evaluation of various innovative reactor concepts represented by SFRs*
Optimize plant lifecycle of advanced reactors automatically by using state-of-the-art simulation technologies and knowledge
Keep and transfer technology bases including knowledge
Develop human resources
* Sodium-cooled fast reactors

## Slide 6: Evaluation flow and system structure
AI-aided platform
Start
(1) Set objective
(2) Obtain related information and select evaluation condition
(3) Evaluate
Finish
Change condition
(4) Confirm
achievement
of objective
Apply to actual plant
KMS
New design, improve safety, etc.
EAS
(Enhanced and AI-aided
optimization System)
KMS
(Knowledge
Management
System)
VLS
(Virtual plant
Life System)
Generalized evaluation flowchart
Three systems that comprises ARKADIA
Steps (1), (2), (4)
Step (3)

## Slide 7: ARKADIA-Design and -Safety
Individual development in the first phase
Integration into a single system in the second phase
ARKADIA-Design
ARKADIA-Safety
optimizes core design, plant structure design, and maintenance program
provides design satisfying requirements of
safety and economics from SA* simulation
Example coupled simulation by VLS
(Neutronics, thermal hydraulics, structure)
Example SA simulation by VLS
(hypothetical condition)
Pipe break
[C]
[¢/cm3]
Core temperature
Core reactivity
Coolant and atmosphere temperature
during loss of reactor level event
* Severe accidents

## Slide 8
Development of ARKADIA
  Development motivation
  Evaluation flow and system structure
  ARKADIA-Design and -Safety
Simulation technologies of ARKADIA-Design
  Module structure
  Validation analyses
Simulation technologies of ARKADIA-Safety
  Development motivation
  Numerical models
  Functional test analysis
Summary

## Slide 9: Module structure of ARKADIA-Design
Implementation mainly in conceptual design stage within design base events
Support of design optimization in the fields of core, structure, maintenance
Composed by PSSP for controller, EAS for evaluation, VLS for virtual plant, and KMS for knowledge base
Virtual Plant in VLS
Multi-level & multi-physics approaches
“multi-code connection (MCC)” methodology with modules(codes) for various scales and physics
A coupling methodology

## Slide 10: Core deformation reactivity analysis (1/2)
Evaluate reactivity feedback due to core deformation in abnormal transient conditions or a significant temperature rise of the core in accidents.
Time-marching procedure
The three codes run sequentially
Data exchange as boundary conditions of each analysis

## Slide 11: Core deformation reactivity analysis (2/2)
10
Whole core temperature and core deformation
Fuel region
Magnified displacements (x20)
Magnified displacements (x20)
(Fuel)
(Structural material)
Core deformation reactivity distribution
Fuel region
Fuel region
Coupled analysis of EBR-II SHRT-45R test
Subassembly bows toward the
colder side
4th-row subassemblies: inward
6th-row subassemblies: outward
Negative reactivity contribution due to outward displacements of reflector SAs as well as fuel SAs

## Slide 12: 1D-CFD analysis model (SHRT-17 in EBR-II)
Outline of SHRT-17 test in EBR-II
Pressure-velocity coupling scheme |  | Coupled
Turbulence model |  | Realizable k-ε (Buoyancy effect: ON)
Wall function |  | Standard wall function
Discretization scheme | advection term | 2nd-order upwind
 | diffusion term | 2nd-order central-difference
Time scheme |  | 1st-order implicit
Time step |  | 0.1 s
: pressure difference
: mass flow rate
: temperature
Trip
Coupling method (sequential 2-way method)
Flow network model for
plant dynamics analysis code (1D)
3D detailed model for CFD code
Outline of CFD analysis conditions
CFD code: ANSYS Fluent
Total cell number: 5 million
(Tetra formed meshes)

## Slide 13: 1D-CFD analysis results (SHRT-17 in EBR-II)
Temperatures on TC tree in UP was traced measured data except in initial 50 s in forced circulation condition.
IHX outlet temperature was captured well by 1D-CFD coupling analysis. Behavior of sodium flow discharged from IHX was not captured by 1D analysis.
TC tree location in UP
Temperature distribution in CP
:TC
IHX outlet temperature
Temperature distribution in UP+Z
[UP: Upper Plenum, Z: Z-pipe, CP: Cold Pool, TC: Thermocouple]
Results on TC tree
Measured TC1 and TC3 are very close.

## Slide 14
Development of ARKADIA
  Development motivation
  Evaluation flow and system structure
  ARKADIA-Design and -Safety
Simulation technologies of ARKADIA-Design
  Module structure
  Validation analyses
Simulation technologies of ARKADIA-Safety
  Development motivation
  Numerical models
  Functional test analysis
Summary

## Slide 15: Base module of ARKADIA-Safety
AI-aided platform
EAS
(Enhanced and AI-aided
optimization System)
KMS
(Knowledge
Management
System)
VLS
(Virtual plant
Life System)
ARKADIA-Safety
SPECTRA code for integrated analysis of in- and ex-vessel phenomena during SAs in SFRs
(Severe-accident PhEnomenological Computational tool
for TRansient Assessment)

## Slide 16: Development motivation
Initiating phase
Transition phase
Penetration
PAMR/PAHR*
Ex-vessel phenomena
SPECTRA
Event
progress
during SA
in SFR
Evaluate in- and ex-vessel phenomena consistently by a single code
Evaluation of multiple SA scenarios and parametric analyses by this single code
Optimization of a plant design from safety evaluation
* Post-Accident-Material-Relocation/Post-Accident-Heat-Removal
Conventional
method
Code A
Code B
Code C
Code D
Results

## Slide 17: Selected phenomena during SA
: Ex-vessel
: In-vessel
: Already incorporated
into the code
Reactor vessel
Intermediate
heat exchanger
Secondary
cooling loop
Containment vessel
Atmospheric chemical reaction
Transport of fission products
Ex-vessel thermal hydraulics
Sodium fire
In-vessel thermal hydraulics
Transport of fission products
Neutronics and core disruption
Molten core relocation
Sodium-concrete interaction
Debris-concrete interaction

## Slide 18: Analytical models
Behavior of coolant (base model)
  Fully-implicit, single-pressure, multi-component, multi-fluid CFD model
Molten core relocation
  Dissipative Particle Dynamics (DPD) method
Coupling of CFD and DPD
  Porosity and permeability in CFD
  Exchange of momentum and energy
Behavior of multi-component gas and aerosol (base model)
  Fully-implicit, lumped mass model considering compressibility
Sodium fire
  Spray and pool fire models
Sodium-concrete interaction
Debris-concrete interaction
In-vessel
Ex-vessel
debris
Concrete
Sodium
Spray fire
Pool fire

## Slide 19: Functional test analysis (1/3)
In- and ex-vessel integrated analysis for hypothetical LORL* event
*Loss Of Reactor Level
**Containment Vessel
Upper part of CV**
70000[m3]
Lower part of CV 1500[m3]
Compartment
5000[m3]
N2: 97mol%
O2: 3mol%
Air
1.01010
[m3]
0 s
Rated operation
Circulating pump trips
Heat removal by IHX stops
Sodium fire starts →(1)
200 s
Sodium-debris-concrete interaction starts →(2)
Intermediate heat
exchanger
Circulating pump
Decay heat
2D Cartesian region
Air
1.01010
[m3]
Air
N2
(1)
(2)

## Slide 20: Functional test analysis (2/3)
This analysis starts from the condition of a uniform temperature.
The liquid surface fluctuation and the temperature change disappeared within a certain time.
The reached steady-state was used as an initial condition of LORL analysis.

## Slide 21: Functional test analysis (3/3)
In-vessel
Coolant level drops
Temperature in core region rises and molten core falls
Cooling path fails completely and coolant temperature rises
Ex-vessel
Atmosphere temperature rises due to sodium fire and sodium-debris-concrete interaction
Total mass of leaked debris
The SPECTRA code can evaluate the overall complex
thermal hydraulics phenomena.

## Slide 22: Summary
ARKADIA
  ARKADIA has the computational methods linked with the knowledge base and AI to optimize plant design based on safety evaluation automatically.
Simulation technologies of ARKADIA-Design
  Technologies have been developed for design optimization of core, structure, and maintenance.
  As one of the technologies, the coupled analysis method for neutronics, core deformation, and thermal hydraulics, and also the 1D-CFD coupled thermal hydraulics analysis method was developed and applied to the existing experiments.
Simulation technologies of ARKADIA-Safety
  SPECTRA has been developed for integrated analysis of in- and ex-vessel phenomena during SAs in SFRs.
  The functional test analysis for the hypothetical LORL event was performed.
This work was partially supported by MEXT Innovative Nuclear Research and Development Program Grant Number JPMXD0220354598.

## Slide 23
Appendix

## Slide 24: Structure of KMS
Technological achievements made through the development of MONJU
Information Infrastructure
Database Group
Databases are organized to enhance usability
Knowledge Group
Systematizes large amounts of data on the basis of design approaches
ARKADIA
-Design
ARKADIA
-Safety
To Support
designers evaluate and study designs
To Support verification and validation of numerical analyses
Design Documents
Domestic and Foreign Trouble Cases
Design Information
DB
Test Data DB
R&D reports
・・・
Trouble / Maintenance DB
・・・
Design Criteria
Judgment Conditions
Evidence, etc.
3D Plant Data
Modeling Information
Test Data, etc.
Notes: Knowledge management system, KMS consists of three layers.
Information infrastructure includes mainly documents of technological achievements made through development of prototype fast breeder reactor, MONJU, in Japan. For example, this layer includes design documents, R&D reports, and domestic and foreign trouble cases.
These information is compiled into a database and stored in the second layer. Second layer is called database group. In this group, databases are organized to enhance usability. This group includes design information database, test data database, and trouble / maintenance database, and so on.
Moreover, the database is systemized and stored in the knowledge group to support designers. This group systematizes large amounts of data on the basis of design approaches.
The knowledge group provides required information for ARKADIA-Design and –Safety.
Information infrastructure and database group will be utilized to support verification and validation of numerical analyses.

## Slide 25: Example of optimization problem
Size | Measures against sodium fire
Size A | Measure 1
Size B | Measure 2
・・・ | ・・・
Postulated event during SA
Optimization of CV design considering SA
(1)
(2)
(3)
(1) Sodium leakage and combustion
(2) Increase of temperature and pressure
(3) Failure of containment vessel
Containment vessel (CV)
Reactor vessel (RV)
Design
parameters
Constraint condition
Satisfy requirements on safety and economics
Objective
Find best solutions (minimize objective function)
What is a best design?

## Slide 26: Optimization process
Neural Network
x1
x2
x3
h1
h2
h3
h4
y1
y2
y3
Simulation
Design condition
Objective function
Optimum solution
learning & searching

## Slide 27: Dissipative particle dynamics
Dissipative particle dynamics (DPD) is an off-lattice mesoscopic simulation technique which involves a set of particles moving in continuous space and discrete time.
Particles represent whole molecules or fluid regions.
The particles’ internal degrees of freedom are integrated out and replaced by simplified pairwise dissipative and random forces, so as to conserve momentum locally and ensure correct hydrodynamic behavior.
The main advantage of this method is that it gives access to longer time and length scales than are possible using conventional MD simulations.
(https://en.wikipedia.org/wiki/Dissipative_particle_dynamics)

## Slide 28: Validation of sodium fire model (1/2)
Sodium leak conditions:
3.3 g/s, 1505 s, 505C
Computational setup
Pool fire experiment
Notes: I will explain one example of validation of sodium fire model. Pool fire experiment was analyzed in this example.
Left figure illustrates test apparatus consisting of the stainless-steel vessel, liquid sodium discharging system, catch pan, air ventilation lines.
505°C liquid sodium was discharged from 0.1 m-height nozzle to the catch pan with the average leak rate of about 3.3 g/s for 1505 seconds. Liquid sodium fell with a column shape and formed a pool at the center of the catch pan. Air in the vessel was ventilated with a steady flow.
Computational model of this experiment consists of three control volumes and two flow paths as shown in right figure. The control
volume corresponding to the test vessel shown in left figure is connected to two environmental volumes. All parameters, such as temperature,
pressure, and gas composition are constant in the two environmental volumes. Velocity at the flow path connected to downstream side is kept
to constant, which corresponds to experimental condition. Liquid sodium is discharged as droplets at 0.1 m height from the catch pan for 1,505 s. Pool spreading on the catch pan is calculated by conservation equation.

## Slide 29: Validation of sodium fire model (2/2)
Increase of
combustion rate
Decrease by the effect of the combustion products
Rapid increase by combustion flame
SPECTRA reproduced pool temperature transition reasonably except for the rapid increase by the combustion flame
Sodium leakage duration
Notes: This slide shows comparison of numerical results with experimental data. Numerical results by existing sodium fire analysis code, SPHINCS, are also plotted.
Left figure shows pool combustion rate and right figure shows pool temperature against time.
SPECTRA reproduced increase of combustion rate in early stage of this experiment. After sodium leakage finished, pool combustion rate decreased with a relatively high speed. This is due to the effect of the combustion products which covered the pool. Numerical analysis could not reproduce this behavior because this effect is modeled by simple assumption.
In the right figure, you can see rapid increase of pool temperature. This seems to be due to combustion flame. SPECTRA reproduced pool temperature transition reasonably except for the rapid increase by the combustion flame.
Numerical results by two codes almost completely agreed each other.

## Slide 30: Current model for sodium-debris-concrete interaction
Sodium-concrete
interaction model (1D)
Debris-concrete
Interaction model (2D r-z)
The current model is unsuitable for a coexistence state of
sodium, debris, and concrete.

## Slide 31: Design of ex-vessel integrated model
Transport calculation module
Atmosphere
(energy and mass)
Sodium pool and concrete
(energy and mass)
Individual phenomena calculation module
Sodium pool fire
(heat and mass source)
Sodium-concrete interaction
(heat and mass source)
Debris-concrete interaction
(heat and mass source)
conditions
Heat and
mass source
Sodium pool
Sodium-concrete interaction
Debris-concrete interaction
Non-damaged concrete