## Slide 1
Myungkyu Kim, Seung-ju Lee, Jaesic Hong
Korea Institute of Fusion Energy, Republic of Korea
Event reconstruction using KSTAR FIS event counter in hot KSTAR plasma

## Slide 2
Contents
Motivation
  What happened during plasma discharge?
  System briefing
Implementation
  Configuration
  Programs(FPGA, User Panel, Analyzer)
Commissioning
  KSTAR plasma shots
Conclusion and Future works

## Slide 3
Motivation
  To check and confirm of Who/Why killed plasma?
  Event collecting in one place.
  Fast processing time ~ 10 us.
  The necessity of confirming the causal relationship of events occurring during plasma discharge.
  For system stability improvement and PCS debugging.
FPGA in FIS

## Slide 4
Implementation
  FIS Block diagram
  Event counter logic
  Link programs – FIS user panel, KSTAR PASS, Labview event analyzer
What is event counter?
  In 2017, KSTAR 4th version of Fast Interlock System adopts event counter, https://doi.org/10.1016/j.fusengdes.2020.111954
  NI-cRIO (FPGA) based event counter.
  Publishing clock counter for KSTAR’s various event.
  EPICS IRIO driver was used for event PVs.

## Slide 5
KSTAR FIS
Implementation
  FIS Block diagram
NI-cRIO
FPGA
EPICS
IOC
Heating Sys.
PCS
SIS
CTU
Rogowski coil
PASS
Event Analyzer
Plasma current
Timing gate
CTU : Central Timing Unit
FIS : Fast Interlock System
PCS : Plasma Control System
SIS : Supervisory Interlock System
PASS : Pulse Automation and Scheduling System
Heating Sys. : NBI, ECH, LHCD, etc
Heating
STOP

## Slide 6
Event counter Logic
Ip protection loop
Ip<Ipth
T1
Ip>Ipth
Then
Ip<Ipth
ANY
100kHz
Counter loop
PCS HBT
i=i+1
i
counter
100kHz
PCS faults
i=i+1
counter
Heating Stop
i=i+1
counter
NBI Faults
i=i+1
counter
Heating stop & reset loop
Enable
Heating Stop
100kHz
Reset
to Heatings
Faults
from
CCS
to PCS
Heating Stop
Heating Stop
…
Heartbeat loop
1kHz
check
heartbeat
FIS, FPGA, PCS
T2
S
S
S
S
S (14 I/O)
: Hard wired I/O,
EPICS PV I/O
[FIS] Heating Stop | [SIS] LV3-1 MG
[PCS] LV3-1 | [FIS] LV3-2 NBI PS
[PCS] LV3-2 | [FIS] LV3-2 NB1 Armor
[PCS] LV3-3 | [FIS] LV3-2 NB2 Armor
[PCS] HEARTBEAT | [FIS] LV3-2 PFC
[SIS] LV1,2,3 | [FIS] LV3-3 IPS
[SIS] LV3-1 MPS | [PCS] LV3-3 EC CUTOFF

## Slide 7
Implementation
  FIS User Panel in usual operation
Event Counters show operation status

## Slide 8
Implementation
  KSTAR PASS User Panel
Event messages
from FIS

## Slide 9
Event Message generation
  Labview FIS counter analyzer program
  Event counter read from FIS -> counter sorting by time
  -> event name mapping -> caput to Event IOC

## Slide 10
Commissioning
  KSTAR Plasma Experiment
  Special case(start-up failure, soft landing)
  Event occurrence in plasma discharge
  [FIS] Heating Stop(HS) : STOP by FIS(FPGA)
  [PCS] LV3-1 : STOP by PCS

## Slide 11
FIS HS
PCS 3-1
27122(start-up failure)
Start-up failure
Commissioning
Ip from MDSplus

## Slide 12
27124 (Soft landing)
Commissioning
FIS HS
PCS 3-1

## Slide 13
Conclusion and Future works
  Conclusion
    It was helpful to understand anomalies that occur during plasma discharge using the event counter.
    It was helpful to find the cause of the problem by analyzing the causal relationship of the occurrence of the event.
    It was confirmed that the FPGA logic has sufficient stability and precision.
  Future works
    Extend to more events
    Extended sharing of event messages (web, SNS, etc.)