## Slide 1: Decision logic in ASDEX Upgrade real time control system
I. Gómez Ortiz, W. Treutterer, B. Sieglin, O. Kudlacek and the ASDEX Upgrade Team
Max Planck Institute for Plasma Physics

## Slide 2: Our daily bread: A small change but a big impact
Use recovered diagnostic sources
Do not use recovered diagnostic sources
IF THEN ELSE
HFSM(Hierarchical Finite State Machine)
Own experience: benchmarking for a change in the electron density evaluator

## Slide 3: Motivation and Proposal
Why do we need to do something?
  Decisions in large Tokamaks are increasing in number and complexity
  The most common decision algorithms, If-Then-Else and HFSM*, are hard to scale
  Wrong decisions => Damages
  Requirements for modern decision algorithms
What do we propose?
  Behaviour trees, extensively used in robotics and the videogame industry
  Tree structure dedicated to call functions
  Suitable for deliberative and reactive architecture.
Main characteristics:
  high flexibility:
    configurability
    stateful/ stateless behaviour
    high node customizability
  modularity: using subtrees
  transparency: visual tree structure
Behaviour Trees: One point of change for adding or removing nodes
HFSM*: Review all the connections to other nodes
* HFSM: Hierarchical Finite State Machines
Behaviour trees ➜ build behaviours from simple actions.
Behaviour Trees ≠ Decision Trees.
    - More informed/ aware
    - Flexible
    - Scalable
    - Transparent
Notes: Decisions in tokamaks: always more abundant and more sophisticated. The greater the system the more relevant due to the larger number of subsystems and the consequences of damages
Exceptions: A large number of exceptions, and their combination make the complicated to handle. Traditional approaches such as If-Then-Else are hardly scalable after a certain number of elements and hard to make them configurable. HFSM are difficult to maintain due to the intrinsic stateful nature, which force the designer to check all the connections every time it introduces a new node
ASDEX Upgrade make use of a large number of decision algorithms, most of them implemented as long nested If-Then-Else. These approach make configuration extremely complicated and update the logic an error prompt task
The tokamaks keep surprising us with new revelations about the system, which often lead to modifications in their control system. Large machines such as ITER require a short, but sure, development times to cope with new findings. The If-Then-Else, with their lack of configurability and transparency as they increase in size, and the HFSM with the obligation of checking all transitions every time a node is included, are no match for Behaviour Trees which tries to address these limitations with an intuitive tree structure, their modularity and configurability

## Slide 4: What is a Behaviour Tree?
Tasks are combined to achieve a goal
The nodes evaluate their action or their children’s result. The nodes pass their result to its parent node until they reach the root node. If the returned value is success or running the tick is over and it waits for the next tick.
Its strength comes from its ability to perform very complex activities by composing simple tasks.
A Behaviour Tree is:
  a software structure used to call functions based on some conditions
  represented graphically as a directed tree composed of different nodes
Evaluated (ticked) in every cycle from top to bottom and left to right. From root node to leaf nodes.
C:
Pellets?
Sequence
inverter
Fallback
Sequence
Node Types
Composite node: Control the execution flow
Decorator node: Modify child node status
Leaf node: Execute a specific action
Tick: Trigger to execute a node
Blackboard: Behaviour tree’s internal variables
Success
Failure
Running
Evaluation order
Evaluation order
A: Take DCN
Sequence
C:
DCN valid?
C:
DCR valid?
A: Take DCR
A: Take Bremsstr
Sequence
A: Take Default
C:
Bremsstr valid?
C:
Pellets?
Sequence
inverter
Fallback
Sequence
Node Types
Composite node: Control the execution flow
Decorator node: Modify child node status
Leaf node: Execute a specific action
Blackboard: Behaviour tree’s internal variables
Success
Failure
Running
Evaluation order
Evaluation order
A: Take DCN
Sequence
C:
DCN valid?
C:
DCR valid?
A: Take DCR
A: Take Bremsstr
Sequence
A: Take Default
C:
Bremsstr valid?
C:
Pellets?
Sequence
inverter
Fallback
Sequence
Node Types
Composite node: Control the execution flow
Decorator node: Modify child node status
Leaf node: Execute a specific action
Tick: Trigger to execute a node
Blackboard: Behaviour tree’s internal variables
Success
Failure
Running
Evaluation order
Evaluation order
A: Take DCN
Sequence
C:
DCN valid?
C:
DCR valid?
A: Take DCR
A: Take Bremsstr
Sequence
A: Take Default
C:
Bremsstr valid?
C:
Pellets?
Sequence
inverter
Fallback
Sequence
Node Types
Composite node: Control the execution flow
Decorator node: Modify child node status
Leaf node: Execute a specific action
Tick: Trigger to execute a node
Blackboard: Behaviour tree’s internal variables
Success
Failure
Running
Evaluation order
Evaluation order
A: Take DCN
Sequence
C:
DCN valid?
C:
DCR valid?
A: Take DCR
A: Take Bremsstr
Sequence
A: Take Default
C:
Bremsstr valid?
C:
Pellets?
Sequence
inverter
Fallback
Sequence
Node Types
Composite node: Control the execution flow
Decorator node: Modify child node status
Leaf node: Execute a specific action
Tick: Trigger to execute a node
Blackboard: Behaviour tree’s internal variables
Success
Failure
Running
Evaluation order
Evaluation order
A: Take DCN
Sequence
C:
DCN valid?
C:
DCR valid?
A: Take DCR
A: Take Bremsstr
Sequence
A: Take Default
C: Bremsstr valid?
C:
Pellets?
Sequence
inverter
Fallback
Sequence
Node Types
Composite node: Control the execution flow
Decorator node: Modify child node status
Leaf node: Execute a specific action
Tick: Trigger to execute a node
Blackboard: Behaviour tree’s internal variables
Success
Failure
Running
Evaluation order
Evaluation order
A: Take DCN
Sequence
C:
DCN valid?
C:
DCR valid?
A: Take DCR
A: Take Bremsstr
Sequence
A: Take Default
C:
Bremsstr valid?
C:
Pellets?
Sequence
inverter
Fallback
Sequence
Node Types
Composite node: Control the execution flow
Decorator node: Modify child node status
Leaf node: Execute a specific action
Tick: Trigger to execute a node
Blackboard: Behaviour tree’s internal variables
Success
Failure
Running
Evaluation order
Evaluation order
A: Take DCN
Sequence
C:
DCN valid?
C:
DCR valid?
A: Take DCR
A: Take Bremsstr
Sequence
A: Take Default
C:
Bremsstr valid?
C:
Pellets?
Sequence
inverter
Fallback
Sequence
Node Types
Composite node: Control the execution flow
Decorator node: Modify child node status
Leaf node: Execute a specific action
Tick: Trigger to execute a node
Blackboard: Behaviour tree’s internal variables
Success
Failure
Running
Evaluation order
Evaluation order
A: Take DCN
Sequence
C:
DCN valid?
C:
DCR valid?
A: Take DCR
A: Take Bremsstr
Sequence
A: Take Default
C:
Bremsstr valid?

## Slide 5: Behaviour trees: A small change and still a small impact
?
➜
?
➜
➜
act
?
➜
➜
act
➜
act
act
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
cmp
?
➜
cmp
?
➜
cmp
➜
cmp
act
?
➜
cmp
➜
cmp
act
➜
cmp
act
act
?
➜
?
➜
cmp
➜
cmp
act
?
➜
cmp
➜
cmp
act
➜
cmp
act
act
?
Fail
➜
cmp
act
cmp
?
➜
?
➜
➜
act
?
➜
cmp
➜
cmp
act
➜
cmp
act
act
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
cmp
?
➜
?
➜
➜
act
?
➜
cmp
➜
cmp
act
➜
cmp
act
act
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
➜
?
➜
➜
act
?
➜
➜
cmp
act
➜
cmp
act
act
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
➜
?
➜
➜
act
?
➜
➜
act
➜
cmp
act
act
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
➜
?
➜
➜
act
?
➜
➜
act
➜
act
act
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
➜
?
➜
➜
act
?
➜
➜
act
➜
act
act
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
Fail
➜
cmp
act
cmp
?
➜
?
➜
➜
act
?
➜
➜
act
➜
act
act
Subtree
Comp. with memory
Subtree
Comp. with memory
Subtree
Comp. with memory
Subtree
Comp. with memory
Subtree
Comp. with memory
Subtree
Comp. with memory
Not recovering old sources
Applying the same change as for the If-Then-Else and the HFSM in the first slide.
Changes applied on one point of contact
More complex tasks = combination of simple tasks
Recovering old sources
?
➜
cmp
?
➜
cmp
➜
cmp
act
?
➜
cmp
➜
cmp
act
➜
cmp
act
act

## Slide 6: Implementation
Final implementation: in the DCS Framework (C++) in ASDEX Upgrade. Implementation under development.
  C++ library: BehaviorTree.CPP library: developed at Eurecat with the joint efforts of the Italian Institute of Technology
  Visual editor for behaviour trees: Groot
Prototype implementation: MATLAB/Simulink behaviour tree framework developed at IPP
Development of control system specific nodes: Some examples
- Threshold comparison with debouncing node
- Signal reference generation
- Ramp down node
- Assign values node
Behaviour Tree Simulink Component in library
Behaviour Tree simulation analyser

## Slide 7: Electron density evaluation
Electron density evaluation in ASDEX Upgrade Discharge Control System (DCS): Interferometry and Bremsstrahlung
Currently implementation: if-then-else
* This is a simplified version of the algorithm
Source | Channel | Usage conditions
Interferometry | DCN H1 | No pellets No fringe detected in DCN H1 DCN H1 interferometry signal valid
 | DCN Hx | No pellets No fringe detected in enough DCN Hx Above signal cannot be used DCN Hx interferometry signal valid
 | DCR H1 | No fringe detected in enough DCN Hx Above signals cannot be used DCR H1 interferometry signal valid
 | DCR Hx | No fringe detected in enough DCR Hx Above signals cannot be used DCR Hx interferometry signal valid
Bremsstrahlung |  | Above signals cannot be used Bremsstrahlung signal is valid
Cond: No Pellets
Sequence
DCN
Subtree
Ne from DCN
Cond: Bremsstrahlung Signal Valid
Fallback
Sel ne
Sequence
Bremsstr
Action: Assign value ne
Subtree
Ne from DCR
Action: Assign value ne
Cond:
No fringe
Sequence
H1
Fallback
Source X
Cond:
H1 valid
Action: Assign value ne
Sequence
HX
Cond:
HX valid
Action: Assign value ne
X=DCN
X=DCR
Behaviour trees: visual approach => easier review of the logic => reduced possibility of failures
Decision Logic
Behaviour Tree
If-Then-Else: complex nested structure=> hard to review => difficult to scale

## Slide 8: Conclusion/ Future
Simulink Behaviour Tree framework
Coupling the Simulink Behaviour Tree framework with a simulation platform => learning system
Utilisation in ASDEX Upgrade:
  Global level: Segment selector
  Local level: Diagnostics, Controllers and Actuator Manager
Enabler technology: Behaviour Trees enables a “goal oriented” machine
New nodes => more sophisticated decision logic in ASDEX Upgrade (Ex: fuzzy or utility based decisions)

## Slide 9
Thank you!

## Slide 10: What is a behaviour tree made of?
Note: The list below only shows the most common nodes types
Behaviour tree
Nodes
Subtree
Blackboard
Composite nodes
Decorator nodes
Leaf nodes
Sequence
Fallback
Switch
Inverter
Always success
Always failure
It collects a branch of the decision tree. It is useful for clarity and reuse.
It provides a key-value storage for the behaviour tree internal variables
Comparison
Assign value
They perform some specific action, it is fully customable. It is basically a function call
They are the executing elements triggered by a tick. The nodes must always return the result of their evaluation, either self evaluated or passed-through from their children nodes.
The result may be: success, failure or running. They return running if their evaluation is not finished during the tick.
They control the execution
They transform the result of the child node
It runs its children nodes in order (left to right) until all are over or one returns failure
It runs its children nodes in order (left to right) until all are over or one returns success
It runs the selected children based on a control signal
It runs its child and inverts whatever result the child returns
It runs its child and always return success to its parent node
It runs its child and always return failure to its parent node
Compares two values
Assign value to variable
Reference generation
Reference signal generation task
Notes: Always failure: This node could be confusing, without getting not details, this node could be used when a sequence node need to execute all its node independently of their return value, for instance compare to a variable and then another value which stores the past states of that variable

## Slide 11: Use case 2: Discharge program segment selection
A highly configurable component implemented in ASDEX Upgrade Discharge Control System (DCS), the DCS global Supervisor, translates the plasma discharge configuration (pulse schedule) defined in XML into concrete waveform references as well as event detection and decision taking rules.
Example: increasing the requested NBI power to cope with a current excessively high level of impurities
selection of a new segment
    actions to modify one or more running trajectories
The Global Exception Handling, implemented using a behaviour trees permits more sophisticated decision taking during:
  normal operation: selection of next segment
  off-normal operation: repair or mitigation actions: