## Slide 1
#Sakharov in Saint Tropez

## Slide 2: CarMa0NL modelling of halo currents on COMPASS
2nd IAEA TM on Plasma Disruptions and their Mitigation, July 19, 2022
V. Yanovskiy1, E. Matveeva1, A. Casolari1, J. Cavalier1, J. Havlicek1, A. Iaiunese2,
N. Isernia2, S. Leonov3 and F. Villone2
1Institute of Plasma Physics of the CAS, Praha
2Consorzio CREATE, Napoli
3Haute École de musique de Genève
Acknowledgements: R. Paccagnella, V. D. Pustovitov

## Slide 3: Outline
Motivation (COMPASS-U)
COMPASS magnetics
Measured vessel currents for #19172
CarMa0NL modelling for #19172
Conclusions

## Slide 4: Motivation: design of COMPASS-U
to support the design of vacuum vessel, passive stabilizing plates, plasma facing components and magnetic diagnostics we perform disruption modelling on CarMa0NL.
COMPASS-U:
Magnetic field 5 T
Plasma current 2 MA
Major radius 0.9 m

## Slide 5: CarMa0NL: 2D plasma + 3D conductors
CarMa0NL describes the evolutionary equilibrium of axisymmetric plasmas in presence of 3D volumetric conducting structures
*F. Villone et al., Plasma Phys. Control. Fusion 55 095008 (2013)
**S. L. Chen, Nucl. Fusion 59 (2019) 106039

## Slide 6: CarMa0NL code
INPUT
Time evolution of:
Toroidal plasma current and pressure profiles
Halo width (see definition on the right, in terms
of poloidal magnetic flux)
OUTPUT
Plasma radial and vertical motion
Eddy and halo currents in conducting structures
Related electromagnetic forces
APPLICABILITY
CarMa0NL allows performing multiple parameter scans in reasonable time, which makes it very convenient for design purposes.
Requires some physical insight for prescribed halo width dynamics.

## Slide 7: Observation from COMPASS-U simulations
Total poloidal halo current depends on q @ LCFS.
Is there a limit for q @ LCFS in real disrupting plasma?
We will use COMPASS data to answer this question.

## Slide 8: Outline
Motivation
COMPASS magnetics
Experimental data for #19172
CarMa0NL modelling for #19172
Conclusions

## Slide 9: Vacuum vessel

## Slide 10: Magnetics
24x3 toroidal Mirnov coils at 3 toroidal angles (coil sets A, B and C) allow to estimate distribution of poloidal current (eddy+halo) using Ampere’s law.
Diamagnetic signal (D) allows to deduce poloidal eddy current (the fundamental harmonic of the poloidal current)*
*V. Yanovskiy et al, P4.1056, Proceeding of the 46th EPS 2019, Milan

## Slide 11: 360 mesh with all port openings
CarMa0NL modelling of 2D plasma VDEs for 360 degree vessel with all port openings showed that Mirnov coils in the set B on LFS are affected by the wall asymmetries.

## Slide 12: Poloidal vessel currents (eddy & halo)
Initial pre-disruption equilibrium for COMPASS #19172
Poloidal eddies during TQ (counter-clockwise)
Poloidal eddies during CQ (clockwise) + halo currents (in both directions)
Halo = Total – Eddy:

## Slide 13: Mag. Diag. for total poloidal eddy current
Diamagnetic signal allow to deduce poloidal eddy current (the fundamental harmonic of the poloidal current) [1, 2]
- measured voltage
- poloidal vessel resistance
[1] Pustovitov V D 2019 Fusion Eng. Des. 138 53-58
[2] V. Yanovskiy et al, P4.1056, Proceeding of the 46th EPS 2019, Milan

## Slide 14: Magnetic diagnostics for total poloidal current
24x3 toroidal Mirnov coils at 3 toroidal angles (coil sets A, B and C) allow to deduce poloidal eddy+halo current using Ampere’s law.
Toroidal symmetry assumed here.
Otherwise there is no simple way to
relate magnetic perturbation and the current.
*V. Yanovskiy et al, P4.1056, Proceeding of the 46th EPS 2019, Milan

## Slide 15: Outline
Motivation
COMPASS magnetics
Experimental data for #19172
CarMa0NL modelling for #19172
Conclusions

## Slide 16: #19172
We will analyse a shot #19172 already modelled with JOREK (2D) [1]
[1] F J Artola et al 2021 Plasma Phys. Control. Fusion 63 064004

## Slide 17: An example: two coils (from top and bottom)
For a downward disruption #19172 the coil 10 is not affected by halo and, therefore, gives the poloidal eddy current only (to compare with eddies deduced from diamagnetic loop (DL) signal).
In contrast, the coil 18 (inside the halo region) gives poloidal halo + poloidal eddy currents.

## Slide 18: Poloidal eddy current (downward VDE)
Poloidal eddy current as measured by Mirnov coils A10, B10, C10 at three toroidal angles and by the diamagnetic loop (DL): good agreement.
Negative spike due to the TQ and the positive spike due to the CQ.

## Slide 19: Poloidal halo+eddy current (downward VDE)
Poloidal halo+eddy current as measured by Mirnov coils A18, B18, C18 at three toroidal angles.
One can deduce the toroidal asymmetry of halo current.

## Slide 20: 24x3 Mirnov coil signals + 1 diamagnetic loop signal

## Slide 21: Poloidal current (halo only) dynamics at 3 tor. angles
Maximum halo amplitude is 50 kA
(15% of pre-disruption plasma current)

## Slide 22: Constant halo amplitude over a wide area (coils 17-21)
Amplitude of the halo current is almost the same between coils 17 and 21.
Tiles cover coils on the bottom of the vessel.

## Slide 23: Outline
Motivation
COMPASS magnetics
Experimental data for #19172
CarMa0NL modelling for #19172
Conclusions

## Slide 24: #19172 settings: current in FABR circuits
The VDE is triggered by the voltage kick in the circuit for radial field.
Used as input for CarMa0NL

## Slide 25: #19172 settings: poloidal beta and TQ duration
We fit pre-disruption poloidal beta (and TQ duration) to negative peak in the poloidal eddy current (measured with diamagnetic loop)
The TQ duration is determined also by SXR measurements

## Slide 26: #19172 settings: internal inductance and dz/dt
We fit internal inductance (of pre-disruption equilibrium) to fit the dynamics of vertical displacement
Good agreement in dz/dt

## Slide 27: We vary \chi to obtain the best fit of the halo footprint

## Slide 28: #19172 overview
TQ -> negative peak in poloidal eddy current.
CQ -> positive peak in poloidal eddy current.
Good agreement between measured and calculated pol. & tor. eddy currents.
The best fit of the measured halo footprint corresponds to the q @ LCFS around 1.

## Slide 29: Best fit of the halo footprint
Best fit of the halo footprint is obtained for such chi(t), that leads to q@LCFS around 1.

## Slide 30: Summary
The best fit with the measured halo footprint is obtained for such halo width (chi)
that leads to q@LCFS around 1.
This suggests that the role of m/n=1/1 mode might be dominant in defining the halo width.
Further studies will explore the sensitivity of the finding to plasma parameters, for example, current profile evolution.

## Slide 31: #19172 with magnetic sound from Mirnov coil A3