## Slide 1: Non-axisymmetric Radiation Modeling of JET SPI Discharges using Emis3D
B. Stein Lubrano1, R. Sweeney1, D. Bonfiglio2, J. Lovell3, P. Carvalho4, L. Baylor3, R.S. Granetz1, S. Jachmich5, E. Joffrin6, M. Lehnen5, C. Maggi4, E. Marmar1, E. Nardon6, U. Sheikh7, D. Shiraki3, S. Silburn4, and JET Contributors8
1MIT Plasma Science and Fusion Center, Cambridge, Massachusetts 01239, USA
2Consorzio RFX, Corso Stati Uniti 4, 35127 Padova, Italy
3Oak Ridge National Laboratory, Oak Ridge, Tennessee 37831, USA
4Culham Centre for Fusion Energy (CCFE), Culham Science Centre, Abingdon, UK
5ITER Organization, Route de Vinon sur Verdon, 13115 St Paul Lez Durance, France
6CEA, IRFM, F-13108 Saint-Paul-lez-Durance, France
7École Polytechnique Fédérale de Lausanne (EPFL), Swiss Plasma Center (SPC), Lausanne CH-1015, Switzerland
8See the author list of 'Overview of JET results for optimising ITER operation' by J. Mailloux et al published in Nuclear Fusion Special issue: Overview and Summary Papers from the 28th Fusion Energy Conference (Nice, France, 10-15 May 2021)

## Slide 2: Disruption Bolometry Analysis is Challenged by Lack of Axisymmetry
High radiated fraction , low peaking required in SPI/MGI mitigated discharges to prevent damage
  ITER research plan for peak operation, SPARC Primary Reference Discharge (PRD) both expect damage to divertor if
  Both machines require low toroidal peaking factors (TPFs) to avoid flash melting
A 3D tomography tool (Emis3D) is developed to validate these performances on present day experiments (e.g. JET)
Fractional error in radiated power of KB5 weighted sums, by radiation source location
[J. Lovell et al. Review of Scientific Instruments 92, 023502 (2021)]
Present disruption bolometry techniques can suffer from up to +/-50% errors
Bolometry diagnostics limited, optimized for flattop

## Slide 3: Emis3D has undergone significant development; first application is two nominally identical JET discharges
Nominally identical discharges (95709, 95711)
  ,
  ;
Disrupted by identical Shattered Pellet Injection (SPI)
  Ne atoms
  D2 atoms
  ~35ms flight times
Different according to TOPI (standard weighted average of bolometer channels): 0.80 vs 0.90
Question motivating this study: Why such different for nominally identical mitigation attempts?
JET SPI 96874

## Slide 4: JET Bolometry in 2019-2020
Two toroidally separated bolometer fan arrays, KB5H & V
KB1s mostly not used;
noise/ slower time
resolution
Injection Location

## Slide 5: Emis3D is a Rigorous Guess and Check Algorithm, Capable of Fitting 2D and 3D Structures
Observation by Cherab
Library of Candidate Radiation Structures
Calculate Reduced 𝜒r²
Best Fit
Each Timestep
Each Structure
Convert to P Value
Uncertainty Pool
=
(t)
Synthetic Bolometry Data
Experimental Bolometry Data
Lowest P Value
Within 2

## Slide 6: Candidate Radiation Distributions
Helical
BOLT (Unwrapped)
[Pedro Carvalho]
JOREK Simulated
“RadDist” object: a 3D function of local emissivity
  [W/m3]
  Only shape; overall amplitude and toroidal distribution are determined in fitting

## Slide 7: Candidate Radiation Distributions
Build many distributions of each type to sample
Variation in poloidal width
Variation in helicity
Centered on different field lines

## Slide 8: 95709: Emis3D Finds Higher Than TOPI
10.95 MJ (
  Uncertainty range 0.68-1.0
Dominated by CQ, TQ Peak
TOPI is not designed for disruption radiation
TOPI is within error bars, but lower than best fits
CQ Best Fits are tomographic inversions
Helicals within the uncertainty during the CQ
  Helical fits w/ toroidal peaking assumptions would lead to lower
  Leads to lower, but not upper, error bars
TOPI
Emis3D
Spike Time

## Slide 9: Shot 95709 Best Fits: Pre-TQ
  Possibly a more complicated structure than included in our pool
Early Pre-TQ ()
Late Pre-TQ ()
Inboard
Outboard
Injection plane
Injection plane
Early radiation peaks near injector
  Spreads toroidally from
  Spreads faster towards inboard side; magnetic nozzle effect?
Later Pre-TQ radiation is closer to plasma center

## Slide 10: In the early pre-TQ, transport consistent with the magnetic nozzle effect is observed
Early Pre-TQ; impurities spread faster along field lines towards high-field (inboard) side
  Proposed mechanism is particle flux conservation in a fluid mechanics model (?) See V.A. Izzo et al., NF 55 (2015)
Fast camera images of JET SPIs sometimes show this behavior (depends on filter)
Best fit helical distributions in Emis3D also support this model
  Note Emis3D assumes radiation peak at
Injection

## Slide 11: Shot 95709 Best Fits: TQ & CQ
Best fits for TQ and CQ are axisymmetric tomographies
  [Credit: Pedro Carvalho]
  Toroidally symmetric
  Only CQ-specific distributions currently in pool
TQ, Rad Peak ()
Mid CQ ()
Injection plane
Injection plane

## Slide 12: KB1s Suggest the Emis3D Best Fits are “Too Axisymmetric”
Four individual foil bolometer channels KB1.1-4
  Located at different (~34°, 79°, 214°, 259°)
  Otherwise identical views of plasma
  Time-averaged over disruption; too noisy for fast time resolution
KB1.1 is nearest to
Experimentally, around 2x higher brightness seen in KB1.1 than 2-4
  In Emis3D, similar brightness predicted for all four channels

## Slide 13: KB1s Suggest the Emis3D Best Fits are “Too Axisymmetric”
Four individual foil bolometer channels KB1.1-4
  Located at different (~34°, 79°, 214°, 259°)
  Otherwise identical views of plasma
  Time-averaged over disruption; too noisy for fast time resolution
KB1.1 is nearest to
Experimentally, around 2x higher brightness seen in KB1.1 than 2-4
  In Emis3D, similar brightness predicted for all four channels
Possible resolutions:
The current quench radiation is more inboard than the tomographic inversions find, out of view of the KB1s
The thermal quench is more toroidally peaked AND the current quench radiation is less
  Given frad~1, higher TQ peaking requires less radiation in the CQ for energy conservation

## Slide 14: Emis3D suggests only two thirds of is radiated before the Ip spike; the full thermal energy is radiated 0.5 ms after spike
If we separate TQ & CQ by current spike time:
  Resulting is greater than stored magnetic energy
  Resulting is
  (, )
For equal , , would have to separate after current spike
  This is not a result of the standard bolometer time shift, which is already accounted for
  Bolo time resolution is order 1ms

## Slide 15: Emis3D suggests only two thirds of is radiated before the Ip spike; the full thermal energy is radiated 0.5 ms after spike
If we separate TQ & CQ by current spike time:
  Resulting is greater than stored magnetic energy
  Resulting is
  (, )
For equal , , would have to separate after current spike
  This is not a result of the standard bolometer time shift, which is already accounted for
  Bolo time resolution is order 1ms
Possible resolutions:
Just a time shift error
  Consistent with the extended heat load deposition time found in G. Arnoux NF 2009
  Or, just entirely due to bolometer time resolution
No time shift error, analysis is correct
  is low
  is over-estimated by toroidally symmetric fits. BOLTs possibly over-fit

## Slide 16: Magnetic Nozzle Effect
“To explain the asymmetry in the parallel flow of the ionized plume, we assume a steady state model for the ionization source. The source region coincides with the region localized in front of the injection port where the jet neutrals diffuse across the magnetic field and become ionized. The parallel flow of the ionized impurities away from the source region therefore obeys the continuity equation , where is the mass density of the impurity ions, A is the cross sectional area of the flux tube, and U is the flow velocity. Since BA = constant, the differential form is
The impurity plume and background plasma are rapidly heated to some common equilibrium temperature reflecting the balance between ohmic heating and radiation losses. The momentum equation , can therefore be written as , where is the square of the isothermal sound speed, with m and Z being the mass and mean charge state of the ions, respectively. Elimination of between this equation and equation (1) leads to a ‘nozzle’ flow equation
where is the isothermal Mach number, which is very small (M ≪ 1) near the source. The fluid speed therefore increases as it approaches the high field side ( is positive) and continues accelerating until it reaches M = 1 at the inboard side of the torus where . The flow towards the low field side is thwarted since is negative. This simple nozzle model offers an explanation for the impurity flow asymmetry predicted by NIMROD. Experimental confirmation of this particular flow attribute remains to be seen. Previously, the effect of grad-B on radial transport of ablated pellet material has been considered by Parks [16]. Also in the context of pellet cloud expansion, a ‘magnetic nozzle’ effect has been previously discussed by Chang [17], but only as a consequence of local expansion of the magnetic field around the pellet cloud, not due to the global magnetic field gradient.”
[V.A. Izzo et al., NF 55 (2015)]

## Slide 17: 95711: Similar frad to 95709 and comparable to TOPI
11.48 MJ (
  Uncertainty Range 0.81-1.0
Overall similar trends to 95709
Smaller increase in
  TOPI’s radiation peak was much higher for 95711 than 95709
Higher TPF at TQ time than 95709; peaked near KB5V?
  Would explain TOPI overestimate
TOPI
Emis3D
Spike Time

## Slide 18: Shot 95711 Best Fits: Similar to 95709
Early Pre-TQ ()
Late Pre-TQ ()
TQ, Rad Peak ()
CQ
()

## Slide 19: JOREK simulations exhibit some magnetic nozzle behavior and produce similar radiation structures to Emis3D best fits
Early Pre-TQ
First Simulation
Second Simulation
Late Pre-TQ
First Simulation
Second Simulation
Emis3D Best Fits

## Slide 20: A GUI is developed and available for use on JET SPI experiments

## Slide 21: Conclusions
Near full mitigation is predicted in discharges 95709 and 95711, but questions remain:
  Why is only ~70% of the thermal energy radiated prior to the Ip spike?
  Why is the asymmetry observed by the KB1s underpredicted?
Q: Why such different frad for nominally identical mitigation attempts?
  A: TOPI overestimates TQ peak radiation for 95711 compared to 2D inversions
  95711 TQ radiation is peaked near KB5V more than 95709
  95711 has shorter pre-TQ; less impurity spreading -> more peaked?

## Slide 22: Next Steps
Continued 95709 and 95711 analysis:
  Remove the flux-aligned requirement for the CQ tomographies and make coarser to avoid overfitting
  Entertain “designer solutions” to improve agreement with KB1s
Use Emis3D to qualify the SPARC disruption bolometer
With Emis3D fully developed and tested, re-evaluate the frad vs. fth JET dataset
  Clear differences in bolometry observable “by eye” across the SPI discharges, and Emis3D will help to understand this
  Older MGI discharges exhibiting this trend will also be studied

## Slide 23: Extra Slides

## Slide 24: Cherab Overview
Ray-tracing, synthetic diagnostic framework
  Raysect based (https://www.raysect.org/)
Fast Camera Image
Cherab Synthetic Camera
Traces bolometer sightlines, integrates emissivity
Produces synthetic bolometer brightnesses for each candidate radiation structure

## Slide 25: Emis3D High Level Overview
Physics motivated “guess and check” tool for 3D emissivity structures
A library of emissivity structure “candidates” is constructed in advance
At each timestep:
  Each candidate is tested against the bolometry data. Goodness of fit quantified by a reduced 𝜒r² statistic:
    Bolometry data is compared to synthetic data associated with each candidate. Synthetic data is obtained using the Cherab synthetic diagnostic framework [M. Carr et al. EPS 2017]
    The best fit out of the full library is identified
  An “uncertainty pool” of candidates within 2 standard deviations of the best fit is identified
This process is repeated for every time step in the disruption
The result is a sequence of best fit radiation structures, which provide corresponding time-resolved radiated powers and toroidal peaking factors
  Error bars are derived from the uncertainty pool
Does not assume toroidal symmetry: non-axisymmetric candidates permitted

## Slide 26: Emis3D High Level Overview
Observation by Cherab
Library of Candidate Radiation Structures
Calculate Reduced 𝜒r²
Best Fit
Each Timestep
Each Structure
Convert to P Value
Uncertainty Pool
=
(t)
Synthetic Bolometry Data
Experimental Bolometry Data
Lowest P Value
Within 2

## Slide 27: 𝜒r² Fitting of Candidates to Bolometry
Cherab observes radiation distribution, produces Synthetic Measurements
Compare to Experimental Measurements, produce a 𝜒r² value for goodness of fit
Some variation in fitting by distribution type. “Helicals” can have up to two punctures
Signal magnitudes fit independently at each array
  This provides more freedom for BOLTs, Joreks, Rings to fit the data; some risk of over-fitting

## Slide 28: 𝜒r² Fitting of Candidates to Bolometry

## Slide 29: Toroidal Overlay for Helicals
Helical radiation structures follow field lines
  Can wrap around tokamak multiple times
  Multiple punctures through plane of each KB5 array
  Emis3D follows up to 2 punctures
Best fit magnitudes of each puncture found in fitting process
  Condition:
  Provides four toroidal data points
Toroidal distribution fit to these 4 points
  We assume an asymmetric gaussian shape peaked at
  This choice affects but not best fit

## Slide 30: Emis3D High Level Overview
Observation by Cherab
Library of Candidate Radiation Structures
Calculate Reduced 𝜒r²
Best Fit
Each Timestep
Each Structure
Convert to P Value
Uncertainty Pool
=
(t)
Synthetic Bolometry Data
Experimental Bolometry Data
Lowest P Value
Within 2

## Slide 31: Workflow: Each Timestep
All distributions give a 𝜒r² at each timestep
Lowest 𝜒r² is Best Fit solution
𝜒r² corresponds to P-value according to the formula [add formula here]
Candidates with are in the “Uncertainty Pool” ( std errors)
  This is what we use to calculate error bars for total radiated power, peaking factor, etc.
  Uncertainty pool definition has some trade-offs. See optional slide

## Slide 32: Uncertainty Pool and Error Bars
related to P value through distribution
P value related to standard errors through 68-95-99.7 rule
Trade-offs
  not well known during disruptions
  Size of error pool is dependent on available candidates. Worse smaller pool
Current approach; cutoff at 2 std. errors above best fit
[Data Reduction and Error Analysis for the Physical Sciences, 3rd edition, Bevington & Robinson, pg 258]
P Value

## Slide 33: 95709 and 95711 Best Fit Plots

## Slide 34: Acknowledgements
The JET SPI project is a collaborative effort of EURATOM, the ITER Organization, and the US Department of Energy. It received funding from the ITER Organization.
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization
This work was funded by the U.S. Department of Energy, Fusion Energy Sciences Agreement DE-SC0014264, the ITER Organization (TA C18TD38FU), and the EUROfusion Consortium framework, Euratom research and training programme under grant No 633053