## Slide 1: Avoiding Sensor Induced Disruptions With Use of Machine Learning
Egemen Kolemen (Princeton University, PPPL)
Josiah Wai (Princeton University)
Azarakhsh (Aza) Jalalvand (Ghent University, Princeton University)
Presented at the
ITER Technical Meeting
20 July 2022

## Slide 2: Outline
Sensor failure types and mitigations
Use case
  DIII-D: Alfvén eigenmode detection using ECE sensors
  NSTX-U: Equilibrium reconstruction using magnetic sensor
Conclusion

## Slide 3: Sensor fault: types and mitigation
Cause of fault
  Material corrosion over time
  Physical damage
  Short circuits
  Calibration errors

## Slide 4: Sensor fault: types and mitigation
Cause of fault
  Material corrosion over time
  Physical damage
  Short circuits
  Calibration errors
Circuit brakers of the Ohmic heating (OH) circuit in JET
Switch lifetime
After
installation
End of life

## Slide 5: Sensor fault: types and mitigation
Avoid/control fault
  Sensor maintenance
    Reactive
    Preventive
    Predictive
  Data augmentation
  Estimate the faulty data based on available data
  Robust ML model
    Sparse networks
    Drop-out training
  Adaptive ML model
Neural Net.
Data
Sensors

## Slide 6
Input: 40 raw ECE signals (No preprocessing!)
Output: Score of five AE modes (LFM, BAE, EAE, RSAE, TAE) per time step
ML model: Reservoir Computing Network (RCN)
NN-based AE detector:
Detecting Alfvén Eigenmode Using ECE
Jalalvand et al 2022 Nucl. Fusion 62 026007
Notes: “Model A” is supplied with RAW ece signals as they are collected from the sensors; no preprocessing, no cut-off, no denoising
The output of the model is “probability” of each AE mode at time t

## Slide 7
True Positive Rate: %91
False Positive Rate: %7
Jalalvand et al 2022 Nucl. Fusion 62 026007
NN-based AE detector:
Detecting Alfvén Eigenmode Using ECE
Notes: Top: example of an ECE spectrogram just to show to the AE patterns to audience
Middle: The model’s output
Bottom: The rough labels used to train the model

## Slide 8
NN-based AE detector:
Robustness of the Models in Case of ECE Sensor Failure
The impact depends on the relative location of AE modes and the defective prob
What if an ECE signal drops?
Zero out ECE#17
(Replaced by ECE#16)
Mitigation: Replace the lost ECE with the neighboring signals
Zero out ECE#17
Zero out ECE#1
Notes: To study the robustness, we zero out ECE signals and study how it influences the model’s output
For model A, the impact highly depends on which ECE signal is zerod out. Since most AE modes occur around core and middle, removing ECE#1 (near the core) does not change the output
But removing a middle ECE (e.g #17) highly influences the output
Mitigation: We can replace the corrupted signal witht the neighboring signals. The result is promising

## Slide 9
NN-based AE localizer:
Detecting and Locating Alfvén Eigenmode Using ECE
Input: Spectrogram of each ECE channel
Output: Probability of AE modes per ECE per time step
RCN
Spectrogram Enhancement
Time (s)
Time (s)
Time (s)
Time (s)
⍴
Kaptanoglu et. al., 2022
Nucl. Fusion (Accepted)
TAE
RSAE
BAE
LFM
Notes: Model B is trained with each ECE spectrogram individually
By processing each ECE at each time step, the model provides the probability of AE modes in time and space

## Slide 10
DIII-D discharge #178636
LFM BAE RSAE TAE
⍴
Kaptanoglu et. al., 2022
Nucl. Fusion (Accepted)
⍴
Time (s)
Time (s)
Time (s)
Time (s)
Label:
Ouput:
NN-based AE localizer:
Detecting and Locating Alfvén Eigenmode Using ECE

## Slide 11: ECE spectrogram analysis NN-based AE localizer: Detecting and Locating Alfvén Eigenmode Using ECE
Edge  Core
Position (ECE#)
Freq.
Time

## Slide 12
What if an ECE signal drops?
Every lost ECE signal results in a zero line in the probability space
LFM BAE RSAE TAE
Image enhancement
ECE spectrogram
ECE spectrogram
(Enhanced)
RCN
AE mode probability
ECE signal
⍴
Time (s)
Time (s)
Time (s)
Time (s)
NN-based AE localizer:
Robustness of the Models in Case of ECE Sensor Failure
Zero out
ECE#17

## Slide 13
Trained with NSTX-U data from most recent campaign
Maps magnetic diagnostics to flux surfaces or equilibrium shaping parameters
EQNET:
a neural net equilibrium reconstructor
J.T. Wai et. al., 2022
Nucl. Fusion (Accepted)

## Slide 14
Shape controller relies on equilibrium reconstruction as input
standard tool is Real-Time EFIT (RTEFIT)
single iteration per equilibrium  less accurate than EFIT01
Neural nets also capable of performing this task within required time (<1ms)
Need robust real-time reconstruction to avoid control issues. E.g. wall collision and disruption
EQNET:
Robust reconstruction needed for shape control
J.T. Wai et. al., 2022
Nucl. Fusion (Accepted)

## Slide 15
Architecture based on fully-connected ANN with PCA data compression
220 shots = 25,000 equilibria from 2015-16 campaign
Use raw sensor data including bad and noisy data
Also add dropout (p=0.02) to magnetic sensor inputs
EQNET:
The model is based on fully-connected network
J.T. Wai et. al., 2022
Nucl. Fusion (Accepted)

## Slide 16
Boundary error increases by roughly 1.3cm, on par with RTEFIT
Degrades slightly more than EFIT01 degrades (0-1.1cm versus 0.5-1.85cm)
Losing specific sensors (upper) can cause upper-single-null prediction not seen with EFIT01.
EQNET:
Losing a sensor degrades prediction ~1cm
205005 @ 500ms: effect of zeroing out each of the 75 B-probes
EFIT01 Dead B-Probes
EQNET Dead B-Probes
J.T. Wai et. al., 2022
Nucl. Fusion (Accepted)

## Slide 17
Parameter estimates are dependent on the sensor.
ZCUR depends heavily on measurements from inner wall
ROMP is one of the most sensitive, affected by most sensors and especially outer midplane/inner midplane
EQNET:
Sensitivity is parameter and sensor-dependent
J.T. Wai et. al., 2022
Nucl. Fusion (Accepted)

## Slide 18
Training RCN with ECE signals is a robust approach for detecting Alfven Eignemodes
Losing an ECE signal causes manageable degradation in detection
The degradation depends on the relative location of AE mode and the lost ECE sensor
Next Steps
  Study predictive maintenance on DIII-D sensors
  Predicting and manipulating AE modes using ML approaches
Conclusions and next steps

## Slide 19
Thank you!

## Slide 20: Eqnet compensates for dynamic changes and vessel currents
Neural net responds better to dynamic changes and induced vessel currents than online method
Removes 5ms phase delay during oscillations – improves controller chance for recovery
Does not suffer from convergence-related issues since NN is non-iterative
Plasma motion (limiteddiverted) induces strong vessel currents
Notes: Potential talking points:
Figure A: rtefit error from 0.2-0.25 is plasma motion (limited diverted) inducing vessel currents
Figure B: plasma is experiencing strong oscillations and motion which induces vessel currents. Eqnet compensates for these better, RTEFIT is 5ms phase-delayed
Figure C and D: RTEFIT errors due to lack of convergence (plasma was moving a lot)
If people get upset that RTEFIT errors look unrealistically big (figure C and D):
- This is a cherry-picked bad example of RTEFIT due to lack of convergence
- the internal measurements like Zmaxis are much worse than boundary measurements which is what the shape controller actually uses (the 50cm Zmaxis error only has a few cm boundary error)

## Slide 21: Alfvén Eigenmode Dataset
AE labels for 1069 DIII-D shots
919 shots after removing uncertain labels
5 AE modes (BAAE/LFM, BAE, EAE, RSAE, TAE)
LFM (BAAE)
BAE
EAE
TAE
RSAE
Distribution of occurrences
over time
Shot 170670 - ECE15
Notes: Top right: Example of the imperfect labels we deal with; The timing of the AE modes are only roughly determined
Bottom left: Data is highly imbalanced

## Slide 22: Enhancing spectrogram
Gaussian blur filter
(window of 31x3)
Remove mean
(per frequency channel)
Freq. (KHz)
Freq. (KHz)
Original image
Step (2)
Step (3)
Time (s)
Time (s)
Freq. (KHz)
Freq. (KHz)
Quantile-0.9 threshold
(per time step)
Step (1)
Image processing techniques to enhance the spectrogram

## Slide 23
Original spectrogram
Enhanced spectrogram
Autoencoder

## Slide 25
Robustness of the Models in Case of ECE Sensor Failure
Model A
The impact depends on the relative location of AE modes and the defective prob
What if an ECE signal drops?
Zero out
ECE#1
Zero out
ECE#17
Baseline
Zero out
ECE#17
(Replaced
by ECE#16)
Mitigation: Replace the lost ECE with the neighboring signals
Average RMSE = 0.22
Average RMSE = 0.03
Notes: To study the robustness, we zero out ECE signals and study how it influences the model’s output
For model A, the impact highly depends on which ECE signal is zerod out. Since most AE modes occur around core and middle, removing ECE#1 (near the core) does not change the output
But removing a middle ECE (e.g #17) highly influences the output
Mitigation: We can replace the corrupted signal witht the neighboring signals. The result is promising

## Slide 26: Use case 2: Alfvén Eigenmode Instabilities in DIII-D
US DOE Project:
  Machine Learning for Real-time Fusion Plasma Behavior Prediction and Manipulation (DE-SC0021275)
Tasks
  Detect/classify Alfvén eigenmode (AE)
  Detect the location and shape of AE in plasma
  Predict and control AE
Data
  40 ECE signals as inputs (ECEs provide spatial information)
  In progress: multi-diagnostic inputs
    ECE + BES + Interferometry + Magnetics