## Slide 1
Discussion on Disruption Mitigation
Pre-TQ SPI
Akinobu Matsuyama, Ben Stein-Lubrano, Brendan Lyons, Di Hu, Paul Heinrich, Jeff Herfindal, Pavel Aleynikov, Jaungwon Yoo, Matthias Hoelzl, Shilin Hu, Jayhyun Kim, Sergei Gerasimov
Do we understand the physics? What is missing in present models?
  Pellet ablation and plasmoid drift
  MHD excitation: cold front penetration, helical cooling, effect of pre-SPI plasma state
  TQ dynamics: MHD relaxation, heat transport, material mixing, radiation and its asymmetry
  CQ physics
What strategy for ITER?
  Is it possible and desirable to dilute before the TQ?
    2 step SPI starting with pure H2 may not work for hot plasmas because of too large drifts
    1 step SPI with Ne+H2 could work, according to INDEX and JOREK
    Potential massive benefits for RE avoidance and heat loads
    Effect on radiation and its asymmetry?
  Origin of the 50-150 ms window for the CQ timescale? Confidence in these numbers? Impact on mitigation strategy?

## Slide 2
Post-TQ SPI for RE mitigation
  Carlos Paz-Soldan, Chris McDevitt, Umar Sheikh, Vinodh Bandaru
  Understanding is progressing but the physics is very complex
    SPI into RE beam, recombination of background plasma
    « MHD » crash with REs + ensuing dynamics (re-ionization of the gas, …)
  Will it work in ITER?
    Can we achieve recombination?
    Re-avalanching looks like a potential issue
RE mitigation with passive 3D coil
  Val Izzo, David Weisberg