# NEUTRON SPECTRA IN Fusion-fission HYBRID REACTOR (FFHR) FOR SPENT FUEL TREATMENT

J.A. GARCIA GALLARDO1, J. L. GERVASONI1,2, F. RUIZ1,2 , M.A.N. GIMENEZ1

1Comisión Nacional de Energía Atómica (CNEA), Bariloche, Argentina
2Consejo Nacional de Investigaciones Científicas y Técnicas (CoNiCeT), Bariloche, Argentina

Email contact of corresponding author: gervason@cab.cnea.gov.ar
INTRODUCTION
The new concepts in energy generation are characterized by tending to greater efficiency and better use of resources; so, new proposals for reactors are under evaluation, such as GEN IV, Fusion Reactors, Accelerator Driven Subcritical Reactors (ADS) and Hybrid Fusion-Fission Reactors (FFHR); which pose the possibility of solving the problems associated with spent fuel elements, not only by reducing the generation of these by-products in future power plants, but also by burning those already accumulated [1, 2].
Among them, the Hybrid Fusion-Fission Reactors (FFHR) are arrangements formed by a nuclear-fusion device and a subcritical-fission-set. The function of the fusion device is to provide neutrons to drive the subcritical assembly which then, uses those neutrons to generate energy. In the other hand, these subcritical assemblies are systems incapable of sustaining fission chain reactions without the presence of an external neutron source, this means that the multiplying parameter keff is always less than one, which in principle reduces the possibility of a severe accident, since turning off the neutron source, shut downs the entire system [3, 4]. This concept dates from the mid-1950s, but was soon abandoned in the face of, at that time, the advent of the pure nuclear fusion reactor was believed to be imminent; but in the early-1970s, the topic was resurrected since it was soon realized that the development of the pure fusion reactor would entail a long and costly research process [5, 6].
Undoubtedly, one of the most controversial aspects of nuclear energy is the handling of spent fuel elements coming from nuclear power plants, which in popular jargon is known as nuclear waste. As we know, among the isotopes that arouse the major concern in the industry are minor actinides, given their radiotoxicity, and the plutonium associated with proliferation. The fast neutrons generated by an FFHR could provide the appropriate spectra to burn these isotopes.
To date, the most advanced hybrid reactor project for actinide processing is called In-Zinerator, and it is basically a molten salt reactor that would use lithium fluoride as eutectic to dissolve plutonium together with the minor actinides. The main problem with this system is that its source of neutrons has not yet been developed. The project to develop such a source, is based on a fusion reactor by inertial confinement currently operating at the Sandia National Laboratory, which is capable of generating 4×1013 neutrons with each pulse of 3 MJ, and so far, it can only produce two pulses per day; therefore, still needing a lot of development to meet the In-Zinerator requirements [1, 7]. Another project aimed at burning transuranics from spent fuels, is the Subcritical Advanced Burner Reactor (SABR), a design that combines sodium-cooled metallic fuel technology, with the Tokamak-type fusion reactor. Such a Tokamak is expected to produce on the order of 1020 neutrons per second, however, its technology is based on the ITER project, so it is still waiting for the progress of the latter. Other projects, although with more modest demands, are based however, also in ITER, posing similar limitations. Among these complications is the complexity of the technology associated with the tokamak and the difficulty of integrate these delicate systems into the environment of a fission reactor [8, 9].
REACTOR CONCEPT
In essence, an FFHS consists of three parts: a fusion reactor that acts as a source of neutrons, a subcritical system where the fissionable fuel is placed, and a tritium generating blanket that feeds the required fuel to the fusion reactor. Usually, all the system is also fitted with a neutron reflector. These parts are arranged concentrically forming a three-layer system to optimize the use of neutrons [10-14].
Nevertheless, achieving a reasonable neutron yield, in order to drive an FFHR, is difficult with current fusion devices, which is why the use of so-called multiplier cascades has been proposed [11-14]. These cascades consist of concentric shells where the fissile material is placed, separated by a very large empty space. The dimensions, shape, and fuel of the shells and the size of the empty space between them, determine the multiplying capacity of the system.
A distinctive feature of the hybrid reactor is that, since it is actually made up of two reactors, it requires two different fuels: in addition to the fissile material, the use of Deuterium and Tritium is required (D-T). Deuterium is a reasonably readily available gas, but Tritium, given the complications involved in storage and transportation, is preferred to be generated on-site. For this reason, an hybrid reactor while using fusion technology, will need to be fitted with a Tritium generating shell. This shell is usually made of a Lithium compound, which generates Tritium by means of the 6Li(n,t)4He and 7Li(n,n′t)4He channels [15-19]. Silicates are among the proposed candidates to form these Tritium Breeder Blankets (TBB), due to its mechanical and thermal properties [20-22].
FIG. 1. Concentric model for an FFHR.

Figure 1 shows a model of FFHR following theses principles, where two shells of 8% enriched Uranium are placed as fuel, a Lithium silicate is used as TBB, and a Tungsten layer plays the role of reflector and shielding [23]. This arrangement was simulated using MCNP5 to find the spectra of the whole system.
RESULTS AND DISCUSSION
Our analysis is centred on a device based on that one presented by Clause et al., in which the two fuel shells are composed by metallic Uranium enriched 8% [11].
TABLE 1.	Composition of the system analysed. Different materials in the TBB would lead to different values of the multiplying parameter keff for the whole system.

Fuel Shell 1	Internal radius	40 cm
	Thick	5.4 cm
	Volume	0.1239 m3
	Mass	2366 Kg
	Fuel	8% enriched U
Fuel Shell 1	Internal radius	411.8 cm
	Thick	14.2 cm
	Volume	31.3 m3
	Mass	598128 Kg
	Fuel	8% enriched U
TBB	Internal radius	426 cm
	Thick	50 cm
	Volume	127.7 m3
	Material	Li4SiO4 Li2SiO3
	Mass	303934 Kg 321813 Kg
Reflector	Internal radius	476 cm
	Thick	4 cm
	Mass	221659 Kg
	Volume	114.8 m3
	Material	Natural W
multiplying parameter	(keff)	0.969 0.980

To determine the usefulness of the system for burning actinides, it will be necessary to produce a fast spectrum [1,8,24], but since the complete system also consists of a Lithium Breeder Blanket (LBB) and a Tungsten Reflector, it is also necessary to see if the reflection or attenuation of neutrons in those components severely modify the spectrum. Therefore, by means of MCNP, the neutron spectra are found in both the fuel shells, the TBB and Tungsten reflector, for 200 energy groups from 10−8 to 102 MeV.
The spectra obtained show (See Fig. 2) that in the fuel layers the operation of this device is similar to fast reactors. Note the peak around 14 MeV in the first shell, indicating that there are a relevant component of fusion neutrons there. This peak disappears completely in the second fuel shell. These two layers show that the fuel spectra are quite similar to that ones expected in conventional fast reactors, and therefore, compatible with actinide burn [25].
As the neutrons traverses the LBB, the spectra shifts to lower energies. Natural lithium has two isotopes: 6Li (7.6%) and 7Li (92.4%), whose cross sections as a function of neutron energy, are very different. The neutron spectrum in the TBB compared to the cross sections for Tritium generation, shows that the peak of the spectrum is very close to the resonance of the reaction the reactions 6Li (n, t)4He, while it decays rapidly near the threshold for 7Li (n, n′t)4He [15–19]. Therefore, we can wait that the largest contribution to Tritium generation comes from 6Li. This also indicates that altering the proportion of this isotope can markedly alter the number of neutrons reflected into the device.
Also, as was stated previously, the use of a multiplicative cascade has a favourable effect in Tritium generation, as the few neutrons of 14 MeV generated in the fusion device, are converted into many neutrons of a lower energy, more appropriate to generate Tritium [14].
FIG. 2. Normalized flux for different shells, with the 8% enriched-Uranium fuel in the FFHR. Left: with a Lithium-breeder shell made of orto-silicate. Right: the same arrangement but with a Lithium-breeder shell made of meta-silicate.

In the shell of the Tungsten reflector, the spectra are shifted to lower energies even more. This attenuation in the energy of the neutron, has already been noticed previously [23].
Finally, the multiplying parameter keff for the whole system was also calculated for both orto- and meta-silicate, finding that its value changes notably. This is due to the different amount of Lithium in these compounds. As Orto-silicate has more Lithium by volume unit, its capability to absorb neutrons is greater, limiting this way the amount of neutrons reflected back to the fuel shells, reducing then, the multiplying parameter.
CONCLUDING REMARKS
In this work an example of Fast Fusion-Fission Hybrid Reactor fuelled with 8%-enriched Uranium and D-T has been presented in order to analyse its neutron spectra. These simulations shows that in the fissile shells, this reactor shows a fast spectra as required to burn minor actinides. In the TBB, these spectra are shifted towards lower energies, which is even more notably in the Tungsten-made reflecting shell.
The difference whether using meta- or orto-silicate is irrelevant in the fuel shells spectra, and barely distinguishable in the TBB and Tungsten shell, but it is crucial in order to find the appropriate multiplying parameter.
References
1. T.A. MEHLHORN, B.B. CIPITI, C.L. OLSON AND G.E. ROCHAU. Fusion-fission hybrids for nuclear waste transmutation: A synergistic step between Gen-IV fission and fusion reactors. Fusion Engineering and Design, 83, (2008). 948953.
2. R. PLUKIENĖ, A.PLUKIS, L.JUODIS,V.REMEIKIS, O. S̆ALKAUSKAS, W. GUDOWSKI. Transmutation considerations of LWR and RBMK spent nuclear fuel by the fusion-fission hybrid system. Nuclear Engineering and Design, 330, (2018) 241-249.
3. NIFENECKER, S DAVID, J. M. LOISEAUX, A. GIORNI. Hybrid Nuclear Reactors. Progress in Particle and Nuclear Physics, 43, 1999. pp. 683-827.
4. H. R. VEGA-CARRILLO, I. R. ESPARZA-GARCÍA, A. SANCHEZ. Features of a subcritical nuclear reactor. Annals of Nuclear Energy, 75, 2015. pp. 101-106.
5. H. IMHOFF, W. H. HARKER, F. E. BJORKLAND, H. A. BRAMMER and A. E. STODDART. A driven thermonuclear power breeder. California Research Corporation Report, CR-6, June (1954)
6. H. A. BETHE. The fusion hybrid. PPhysics Today, May, (1979)
7. B. B. CIPITI , V. D. CLEARY , J. T. COOK , S. DURBIN , R. L. KEITH , T. A. MEHLHORN, C. W. MORROW , C. L. OLSON , G. E. ROCHAU , J. D. SMITH , M. C. TURGEON , M. F. YOUNG, L. EL-GUEBALY, R. GRADY, P. PHRUKSAROJANAKUN , I. SVIATOSLAVSKY, P. WILSON , A. B. ALAJO , A. GUILD-BINGHAM , P. TSVETKOV , M. YOUSSEF , W. MEIER , F. VENNERI , T. R. JOHNSON , J. L. WILLIT , T. E. DRENNEN , W. KAMERY. Fusion transmutation of waste: Design and analysis of the in-zinerator concept. Sandia Report, SAND2006-6590, 2006.
8. I. Z. SANI AND M. MAHDAVI. Nuclear waste transmutation and tritium production in a fusion-driven hybrid reactor based on different reflectors. Fusion Engineering and Design, 161, 2020. 111925.
9. W. M. STACEY, C. L. STEWART, J.-P. FLOYD, T. M. WILKS, A. P. MOORE, A. T. BOPP, M. D. HILL, S. TANDON AND A. S. ERICKSON. Resolution of fission and fusion technology integration issues: An upgraded design concept for the subcritical advanced burner reactor. Nuclear Technology, 187, 2014. July.
10. Y. WU. Neutronics Design Principles of Fusion-Fission Hybrid Reactors. Fusion Neutronics, 2017. 283.
11. A. CLAUSSE, L. SOTO, C. FRIEDLI and L. ALATAMIRANO. Feasibility study of a hybrid subcritical fission system driven by plasma-focus fusion neutrons. Annals Of Nuclear Energy, 78, (2015) pp10-14.
12. H. TALEBI and S.M.S. KIAI. Conceptual design of a hybrid fusion-fission reactor with intrinsic safety and optimized energy productivity. Annals Of Nuclear Energy, 105, (2017) pp106-115.
13. S.M.S. KIAI, H. TALEBI, S. ADLPARVAR. A compact fusion-fission hybrid reactor. Journal of Fusion Energy, 37, (2018) pp. 161-167.
14. J.A. GARCÍA GALLARDO, M.A.N. GIMÉNEZ, Self-sustainability and energy-balance in a fast Fusion–Fission Hybrid Reactor (FFHR) based on Dense Plasma Focus (DPF) and multiplicative cascade, Progress in Nuclear Energy 147 (2022) 104184
15. L.E. KIRSCH, M. DEVLIN, S.M. MOSBY, J.A. GOMEZ. A New Measurement of the 6Li(n,α)t Cross Section at MeV Energies Using 252Cf Fission Chamber and 6Li Scintillators. Nuclear Instrumetns an Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipement, 874, 2017. pp. 57-65.
16. A.D. CARLSON, V.G. PRONYAYEV, R. CAPOTE, G.M. HALE, Z.-P. CHEN, I. DURAN, F.-J. HAMBSCH, S. KUNIEDA, W. MANNHART, B. MARCINKEVICIUS, R.O. NELSON, D. NEUDECKER, G. NOGUERE, M. PARIS, S.P. SIMAKOV, P. SCHILLEBEECKX, D.L. SMITH, X. TAO, A. TRKOV, A. WALLNER, W. WANG. Evaluation of the Neutron Data Standards. Nuclear Data Shets, 148, 2018. pp. 143-188.
17. F. BROWN, R. H. JAMES, J. L. PERKIN and J. BARRY. THE CROSS SECTION OF THE 7Li(n, t) REACTION FOR NEUTRON ENERGIES BETWEEN 3.5 AND 15 MeV. Reactor Science and Technology (Journal of Nuclear Energy Parts A/B), 17, 1963. pp. 137-141.
18. H. LISKIEN and A. PAULSEN. Determination Of 7Li (n, t) Cross Sections between 6 and 10 MeV. Annals of Nuclear Energy, 8, 1981. pp.423-429.
19. DONALD L. SMITH, MANUEL M. BRETSCHER AND J. W. MEADOWS. Measurement of the Cross Section for the 7Li(n, n′ t)4He Reaction in the 7- to 9-MeV Energy Range. NUCLEAR SCIENCE AND ENGINEERING, 78, 1981. pp.359-369.
20. S. SATO, K. OCHIAI, Y. VERZILOV, M. WADA, N. KUBOTA, K. KONDO , M. YAMAUCHI, T. NISHITANI AND C. KONNO. Measurement of tritium production rate in water cooled pebble bed multi-layered blanket mockup by DT neutron irradiation experiment. Nuclear Fusion, 47, 2007. pp. 517521.
21. SHRICHAND JAKHAR, MITUL ABHANGI, C.V.S. RAO, T.K. BASU, SONALI P.D. BHADE, PRIYANKA J. REDDY. Measurement of tritium production rate distribution in natural Li Al O2 /HDPE assembly irradiated by D-T neutrons. Fusion Engineering and Design, 87, 2012. pp. 184187.
22. WANG Xin-Hua, GUO Hai-Ping, MOU Yun-Feng, ZHENG Pu, LIU Rong, YANG Xiao-Fei, YANG Jian. Measurement of tritium production rate distribution for a fusion-fission hybrid conceptual reactor. Chinese Physics C, 37, No. 5, 2013. 056202.
23. J.A. GARCÍA GALLARDO, M.A.N. GIMÉNEZ AND J.L. GERVASONI. Nuclear properties of Tungsten under 14 MeV neutron irradiation for fusion-fission hybrid reactors. Annals of Nuclear Energy, 147, (2020). 107739.
24. CHARLES E. TILL. Energy Over The Centuries: The IFR Options. Argonne National Laboratory, 1994.
25. J.F. PARISOT. Treatment and recycling of spent nuclear fuel, Ed. Le Moniteur, Comisariat à l’énergie nucleaire, Saclay, 2008.