## Slide 1: The Simplified Radionuclide Transport (SRT) Code for the Source Term Assessment of pool-type metal fuel sodium fast reactor severe accidents
March, 2023
Matthew Bucknor, Dave Grabaskas, Tyler Starkus, Dong Hoon Kam, Shayan Shahbazi
Argonne National Laboratory

## Slide 2
Phenomena
SRT Overview
Models
Example
SQA

## Slide 3
Phenomena
SRT Overview
Models
Example
SQA

## Slide 4: Pool-Type Metal Fuel Phenomena
Key Differences
  There are significant differences in severe accident behavior and fuel failure phenomena between oxide and metal fuel for SFRs
Recent Studies
  Argonne studies explored the most “credible” fuel damage scenarios for pool-type metal fuel SFRs.
  Scenarios included extended protected loss-of-heat sink events (eutectic cladding failure without fuel melting) and severe transient overpowers or localized fuel blockages (localized, short-term fuel melting)
ANL-ART-3
ANL-ART-38
ANL-ART-49

## Slide 5: Pool-Type Metal Fuel Phenomena
Eutectic Failure without Fuel Melting
Failure with Fuel Melting

## Slide 6: Pool-Type Metal Fuel Phenomena

## Slide 7
Phenomena
SRT Overview
Models
Example
SQA

## Slide 8: SRT Overview
Purpose: Conduct rapid source term analyses and uncertainty/sensitivity analyses of radionuclide transport phenomena for SFR and microreactor source term analyses
Scope: SRT assesses the release and transport of radionuclides through the reactor system and to the environment for designated accident sequences
Goal: Provide simplified phenomena models that are easily modified by the user (primarily data-driven), with option to utilize more detailed model (or create your own)

## Slide 9: SRT Overview
Capabilities
  Performs a time-dependent analysis of radionuclide transport from the fuel through the reactor system and to the environment
  Contains both an SFR and microreactor model, with a focus on metal fuel designs
  Includes models for many different transport/retention phenomena, allowing an integral analysis
  Does not model the transient itself, such input information can be provided by a system-level code (like SAS4A/SASSYS-1) or postulated
Structure
  Code is a mix of fuel release/transport models and 0-D compartment model
  Variable timestep: 1 sec to 1 hour
  Currently tracks 770 separate isotopes of the elements in NUREG-1465 plus U and Na. Includes stable isotopes also, which may be important for chemistry
  Accounts for radionuclide decay (with daughter products of short-lived noble gases)

## Slide 10: SRT Overview

## Slide 11: SRT Overview
Uncertainty/Sensitivity Analysis
  Almost all input parameters can be specified as uncertainty distributions. The code will sample from the uncertainties and perform multiple “iterations.”

## Slide 12
Phenomena
SRT Overview
Models
Example
SQA

## Slide 13: SRT Models
Radionuclide Migration In-pin During Irradiation
  RN migration to bond/plenum based on user input burnup-dependent functions per RN class
Radionuclide Release from Fuel Pin
  RN release based on migration and user input burnup/temperature-dependent functions per RN class
Radionuclide Bubble Transport in Pool
  Two models available
  Simple model: User specifies bubble decontamination factor (DF)
  Detailed model: Calculates bubble DF based on Brownian diffusion, inertial deposition, gravitational settling, and condensation

## Slide 14: SRT Models
Pool Vaporization
  Response surfaces for each element based on HSC calculations (temperature and pool size dependent)
Cover Gas Region and Containment
  RNs separated into vapor/gases and aerosols
  RNs may switch classes depending on user-input (or when moving between cover gas and containment)
  Several aerosol deposition options
    Constant decay constant (per RN class or universal)
    Custom concentration-dependent power function
    Henry Fauske correlation
  Can use different aerosol deposition options in cover gas region and containment
  Can set minimum aerosol concentrations
  Leakage based on user input (vol% per day)

## Slide 15: SRT Models
Offsite Dispersion
  Performs simple 𝛘/Q calculation utilizing user input values
  Calculates whole body dose, thyroid dose, CEDE, and TEDE
  Can do segmented or integral doses
  Contains DCFs from FGR 11/12 but can use other values
  Time-dependent RN mass release also available for input into other codes (such as MACCS)

## Slide 16
Phenomena
SRT Overview
Models
Example
SQA

## Slide 17: Example
Example Analysis
  Purpose to demonstrate code capabilities, not representative of an actual accident scenario

## Slide 18: Example

## Slide 19: Example

## Slide 20: Example

## Slide 21
Phenomena
SRT Overview
Models
Example
SQA

## Slide 22: Software Quality Assurance (SQA)
SQA
  The SQA program includes version control, ticket system, and a suite of SRT SQA docs (software requirements, code description, users manual, verification tests, validation cases).
Verification
  Verification tests are conducted on the individual functions and integral code performance. Many of the verification tests are provided to licensed users to be utilized as regression tests.
Validation
  Depending on the model, different validation approaches are utilized. For data driven models utilizing user-supplied data, validation focuses on underlying assumptions of the model. For mechanistic models utilizing physical or chemical calculations, direct comparisons to experimental data are performed.

## Slide 23: Conclusions

## Slide 24: Conclusions
SRT provides integral mechanistic source term calculations for metal fuel pool-type SFRs, with a focus on sensitivity/uncertainty analyses
To support design and licensing calculations, significant efforts to support code SQA and V&V
SRT has now been licensed by multiple U.S. SFR vendors and was used for calculations performed as part of the conceptual phase of the USDOE Versatile Test Reactor (VTR) project.
  VTR calculations included those contained within the Conceptual Safety Design Report (CSDR), which was approved by the authorization body.