## Slide 2: Sustainable remediation in Brazil: Development, controversies, and future perspectives
Juliana G. Freitas, Stela Cota

## Slide 3: Contaminated sites management
1970
1980
1990
2000
2010
2020
Beginning…
1st generation
Complete removal pollutants
2nd gen
Risk based approach
3rd gen
Sustainable management
4th 5th gen?
- Nature based Solutions
- Prevention / Control
Slenders et al., 2017
DOI: 10.1002/rem.21509
Beginning…
First contaminated sites identified
2nd gen
First regulations and guidelines
State guideline values
Federal legislation
Risk assessment spreadsheets
3rd gen
4th 5th gen?

## Slide 4: Contaminated sites management in Brazil
Strategies and actions are very heterogeneous in Brazil
Half of the Brazilian states did not have a methodology for contaminated site management 5 years after federal legislation
Only 3 states have a register of contaminated sites
Number of contaminated sites in the country is still largely unknown
Is there an organizational structure for contaminated sites management?
no
partially
yes
???
Texeira et al., 2016
(Panorama GAC - IPT)

## Slide 5: Sustainable remediation
Remediation
Sustainable Remediation
  ‘‘that eliminates and/or controls unacceptable risks in a safe and timely manner, and which maximize the overall environmental, social, and economic benefits of the remediation work’’ (Surf-UK, 2010).
  “one that represents the best solution when considering environmental, social, and economic factors - as agreed by the [project] stakeholders” (Nicole, 2011)
UN, 2016
2ary impacts

## Slide 6: Sustainable remediation in Brazil
Remediation in São Paulo State
Total in 2023: > 6800 sites
Thermal: 2 in 2017, 11 in 2023
Chart: 
| 37377 | 37895 | 38292 | 38473 | 38657 | 38838 | 39022 | 39387 | 39753 | 40118 | 40513 | 40878 | 41244 | 41609 | 41974 | 42339 | 42705 | 43070 | 43435 | 44166 | 45139
P&T | 271 | 317 | 377 | 472 | 533 | 583 | 712 | 818 | 909 | 913 | 1021 | 1068 | 1148 | 1169 | 1198 | 1257
MNA | 23 | 35 | 47 | 61 | 46 | 110 | 226 | 387 | 500 | 508 | 623 | 633 | 696 | 700 | 689 | 675
Chemical oxidation / reduction | 6 | 7 | 11 | 19 | 27 | 36 | 67 | 94 | 131 | 148 | 206 | 238 | 306 | 323 | 355 | 428
Biorremediation | 9 | 10 | 14 | 16 | 17 | 21 | 34 | 42 | 48 | 49 | 54 | 63 | 68 | 70 | 76 | 87
MPE | 79 | 99 | 138 | 233 | 293 | 353 | 564 | 694 | 848 | 870 | 1048 | 1086 | 1182 | 1213 | 1258 | 1339
Excavation | 124 | 142 | 168 | 183 | 199 | 216 | 259 | 303 | 371 | 410 | 480 | 509 | 549 | 591 | 613 | 695
SVE | 171 | 173 | 185 | 196 | 203 | 216 | 251 | 264 | 281 | 280 | 298 | 302 | 324 | 331 | 342 | 377
Air Sparging | 56 | 68 | 82 | 96 | 107 | 124 | 146 | 158 | 165 | 162 | 172 | 174 | 183 | 186 | 187 | 193
Pump and treat
MPE
MNA
Excavation
Chemical
SVE
Air sparging
Bioremediation
Is sustainability playing a role in technology selection?

## Slide 7: Remediation end-point
How much should we remediate?
  Total removal
  General maximum acceptable values
  Site-specific risk assessment
  Compensation for contaminants left?
What is an acceptable risk?
  Safe
  ×
  Sustainable

## Slide 8: Remediation end-point
How much is acceptable?
  Probabilistic approach
    carcinogenic compounds: 10-5
    hazard quotient for non-carcinogenic: 1
    dose limit criteria for radionuclides: 1 mSv yr-1
Who decides?
“what is acceptable should be defined by those who experience the risk”

## Slide 9: At which step we consider sustainability?
Nowadays
Technology selection
Deciding how to apply the selected technology
  Example: using solar panels to operate a remediation system instead of the energy supplied by the power company

## Slide 10: How we evaluate / compare sustainability
Different sustainability assessment tools
  developed by consultant companies
  industry, academy? Validation?
Indicators
  Environmental
  Economic
  Social?
No national or state guidelines available
UN, 2016

## Slide 11: Stakeholders engagement
All stakeholders should be involved
Stakeholders must be listened to during the first steps of contaminated site management
Risk communication: mentioned in national and state regulations, but no clear definitions on how and by whom
Lack of transparency
CBH Rio das Velhas
Mariana dam disaster

## Slide 12: Lack of local studies
Lack of research and studies on sustainable remediation in Brazil
Low number of publications on sustainable remediation by developing countries, particularly Brazil
Sustainability assessments and comparison tools  majority developed in Europe and the US
“Sustainable remediation”
Peer reviewed articles
Scopus

## Slide 13: Future perspectives
Some good news…
Initiatives:
  NICOLE Latin America – Work group on Sustainable remediation
  CETESB
    Review of the Contaminated Sites Management Guidance
    São Paulo State Environmental Chamber for Contaminated Sites Management
  Nature-based Solutions

## Slide 14: Future perspectives
Discussions in different settings, institutions and groups of stakeholders are happening
  Rarely involve the ones affected or potentially affected by the risks…
  Unidirectional communication: experts  impacted community
For contaminated sites, sustainability should:
  Be considered from the start
  Involve all stakeholders
We need an integrated perspective considering ecological and societal settings

## Slide 15: Acknowledgements
Thank you!