## Slide 2: Applying a life cycle environmental perspective to the development of radioactive waste treatment technologies
J. Kirk, R. Clayton, A. Banford, L. Stamford
E: Laurence.stamford@manchester.ac.uk

## Slide 3: What is Life Cycle Assessment (LCA) ?
Quantification of environmental burdens
Translating burdens into potential impacts
Identification of opportunities for environmental improvements – 'hot spots'
ISO 14040/44
Figure 1: The four phases of life cycle assessment as defined in ISO 14044

## Slide 4: LCA Methodology
Defining Goal and Scope
  System boundaries and functional units
Inventory Analysis
  System definition – Process modelling
  Data collection – Ecoinvent database
  Estimation of burdens
Impact Assessment
  Impact assessment methodology selection – ReCiPe 2016
  Impact categories I.e., Climate change potential, human toxicity, metal depletion
  Estimation of Impacts
Interpretation
  'hot spot' identification
  Sensitivity analysis
  Conclusions
Figure 2: ReCiPe impact assessment methodology

## Slide 5: LCA and Life Cycle Costing (LCC) in PREDIS
LCC is less standardised but a general method exists (from the Society of Environmental Toxicology and Chemistry, SETAC)
PREDIS incorporates LCA and LCC into the development of treatment options for metallic wastes, liquid organics and solid organics, as well as waste store monitoring technology.
All LCC aligns with the LCA models with each flow having a cost attached
Protocol for the use of LCA/LCC: https://predis-h2020.eu/wp-content/uploads/2021/09/PREDIS_MS14_T2.5-LCA-protocol-guidance_31.8.2021.pdf
Figure 3: LCC methodology
Capital cost (production of materials/components)
Fixed operating costs
Variable operating costs
Waste management costs
End-of-Life costs
Transport costs

## Slide 6: LCA/LCC in Nuclear Sector
Literature review 2021-2022: established the very small pool of radioactive waste treatment LCA, few papers considering decommissioning or back end nuclear fuel cycle
  Over 120 papers screened
Nuclear Treatment Technologies/Methods
Nuclear LCA Studies
Minimal Crossover

## Slide 7: Case Study - Decontamination using Gel
Application of a self-drying cracking gel (SDC gel) which incorporates surface contamination
Collaboration on inventory data with CEA
FU is the treatment of 10 m2 of planar stainless steel surface
System boundary:
production of reagents and equipment  removal of the treatment gel
Figure 4: Impacts of treating 10 m2 of planar stainless steel surface using SDC gel
Chart: 
| Climate change, default, excl biogenic carbon [kg CO2 eq.] | Fine Particulate Matter Formation [kg PM2.5 eq.] | Fossil depletion [kg oil eq.] | Freshwater Consumption [m3] | Freshwater ecotoxicity [kg 1,4 DB eq.] | Freshwater Eutrophication [kg P eq.] | Human toxicity, cancer [kg 1,4-DB eq.] | Human toxicity, non-cancer [kg 1,4-DB eq.] | Ionizing Radiation [kBq Co-60 eq. to air] | Land use [Annual crop eq.·y] | Marine ecotoxicity [kg 1,4-DB eq.] | Marine Eutrophication [kg N eq.] | Metal depletion [kg Cu eq.] | Photochemical Ozone Formation, Ecosystems [kg NOx eq.] | Photochemical Ozone Formation, Human Health [kg NOx eq.] | Stratospheric Ozone Depletion [kg CFC-11 eq.] | Terrestrial Acidification [kg SO2 eq.] | Terrestrial ecotoxicity [kg 1,4-DB eq.]
Treatment [Gel Production] | 31.5896 | 0.048968 | 7.4341 | 0.18858 | 4.4727 | 0.013869 | 2.2569 | 226.8277 | 0.57751 | 0.82018 | 5.4392 | 0.0033162 | 3.0936 | 0.082912 | 0.081072 | 9.5381e-05 | 0.12107 | 138.8867
Application [Sprayer Production] | 0.00011384 | 4.1964e-07 | 3.8366e-05 | 2.4311e-06 | 7.0051e-05 | 2.3472e-07 | 5.5222e-05 | 0.0037617 | 6.563e-06 | 6.4162e-06 | 8.5369e-05 | 7.1836e-08 | 2.4048e-05 | 4.9931e-07 | 4.8661e-07 | 6.0577e-11 | 1.4806e-06 | 0.0025129
Energy Use [Equipment] | 0.32609 | 0.00016785 | 0.19262 | 0.0013185 | 0.0024207 | 2.5295e-05 | 0.0086878 | 0.10989 | 0.19183 | 0.035443 | 0.0031992 | 5.9097e-06 | 0.00035474 | 0.00059227 | 0.00057122 | 1.1216e-07 | 0.0004882 | 0.34493
Removal [Vacuum Production] | 39.3636 | 0.089156 | 14.4493 | 0.27611 | 35.2011 | 0.019913 | 4.793 | 163.9295 | 2.0654 | 1.4243 | 42.3318 | 0.0034382 | 0.55985 | 0.092803 | 0.088837 | 1.0949e-05 | 0.19481 | 701.3229

## Slide 8: Case Study - Decontamination using Gel
Once treated the stainless steel can be recycled/free-released
The carbon footprint of decontaminated stainless steel is 99.8% lower than that of virgin stainless steel, even before savings in disposal space are accounted for:
Figure 5: SDC gel treatment compared to stainless steel production
(Note that this assumes only surface decontamination was present, with no subsurface contamination/activation.)

## Slide 9: Case Study - Geopolymer Encapsulation
Tuff geopolymer encapsulation of radioactive solid organic waste (RSOW)
  Collaboration on inventory data with Politecnico di Milano
  FU: the pre-disposal processing of 1 kg of intermediate level RSOW surrogate
  System Boundaries: receipt of waste at the treatment facility to the handoff of a conditioned waste drum to a final repository
Varying waste loading scenarios based on R&D compared to OPC encapsulation
Figure 6: Climate Change potential of tuff geopolymer encapsulation
Chart: Climate change potential (kg CO₂ eq.)
| Geopolymer (40% Waste Loading) | Geopolymer (30% Waste Loading) | Geopolymer (20% Waste Loading) | Cement (20% Waste Loading)
Climate Change Potential (kg CO2 eq.) | 0.613 | 0.814 | 1.23 | 3.34

## Slide 10: Conclusions
LCA and LCC can be useful tools to identify the most effective and efficient routes for waste treatment R&D. Currently they are underutilised.
Gel decontamination of planar steel surfaces appears highly beneficial from an environmental perspective.
  Impacts are dominated by the gel and vacuum cleaner  alternative oxidants and minimisation/reuse of vacuum cleaners are the best strategy
Geopolymer encapsulation can outperform cementation by >60%.
  Costs and optimisation of waste loadings are key focal points
joel.kirk@postgrad.manchester.ac.uk rachael.clayton@postgrad.manchester.ac.uk laurence.stamford@manchester.ac.uk anthony.w.banford@uknnl.com