## Slide 2: Application of AGILE project Management Methodology in R&D to ensure the Safe and Sustainable Disposal of Legacy Waste
W. Wacquier (ONDRAF/NIRAS)
J. Denul (Threon)

## Slide 3: Context
ONDRAF/NIRAS plans to build and operate a surface disposal facility for LLW in Dessel
License application is underway
  Royal Decree creation & operating licence (05/2023)
   Start of the Construction
  Royal Decree for confirmation (expected ~ 2029)
   Start of the Operation
License with the License conditions
Demonstrate that we are compliant with the License conditions
  Construction
  Waste  Demonstration of the “Disposability” of the waste
= Big challenge for legacy waste (many uncertainties and high risks)  AGILE approach

## Slide 4: Our fine-tuned AGILE approach: Key elements of way of working
Slicing and decoupling of problems
Identify small parts of big challenge  to start working on it
 to get quickly first preliminary results!
Incremental discovery and delivery
Create incrementally a concept for a part of the big challenge
 Gain a deeper understanding (Studies, experiments, feedback loops with stakeholders, emergence of new problems)
 Develop multiple options
 Combine options and assess partial solutions
 Develop concept(s)
Learning by doing
Discover not only by just thinking, calculating but by doing: Make / Build /Test to visualise ideas
Risk management with options
Reduce the uncertainties & risks by identifying options that sufficiently cover a priority risk
Provide a clear framework to work:
Nested feedback and learning loops
Team autonomy within clear boundary

## Slide 5: Application of AGILE to incrementally develop solutions
Define specific measures
Adaption Safety Report
Safety Authority
Post-conditioning (IPM)
Disposal
Non conform/
Non admissible
Loading plan
Existing waste
Future waste (operation)
Future waste (dismantling)
Physical Controls
Is Waste conform?
Yes
No
Conformity files
Safety Authority
Safety Authority
Is Waste admissible?
Yes
No

## Slide 6: Application of our AGILE approach
How to fill the missing information of all legacy waste to assess the conformity?
Based on the available knowledge, a slicing was performed in three steps:
  Exclusion of the waste packages that are the least likely to conform (e.g. old historical waste with very limited information)
  Categorise the legacy waste based on waste producer & potential non-conformities
  Identify the legacy waste expected to conform easily
We start working on conformity files despite the complexity
We identify the top priority for non-compliant waste: development of a solution for concrete potentially sensitive to ASR (swelling reaction)
Conformity files

## Slide 7: Application of our AGILE approach
How to load the modules taking into account the production and the characteristics of the waste ?
First loading plan by hand (spreadsheet)
Development of a more robust IT tool
Set global objective & Identification of Functionalities
V0.1
V1.0
V0.2
Use increments of the tool & validation of the tool in parallel
   No need to establish detailed tech. spec. to start development of IT tool thanks to close day-by-day collaboration users & developers
Loading plan

## Slide 8
Pilot project to control the content of the legacy waste (11 waste packages)
 Building knowledge on adequate techniques for the controls on an industrial scale & on the nature on legacy waste
Removal of drum
Core drilling
Cutting & dismantling of pellets
Sorting & characterisation of waste materials
Application of our AGILE approach
Physical Controls

## Slide 9: Application of our AGILE approach
Caisson
Non-explosive cracking agent (waste)
Metallic container
Compressible material
Mortar
Monolith Type I with PE foam (R&D studies ongoing on degradation & impact on the sorption)
Monolith Type III with a box
Monolith Type III with RVC foam (carbon “inert”)
Several conceptual prototypes to be tested to develop a solution for concrete potentially sensitive to ASR
Define specific measures
Notes: BETONAMIT® | The non-explosive demolition agent
for the simple and targeted demolition of rock and concrete
Betonamit is an explosion-free demolition agent which enables relatively accurate demolitions without the need for special conditions or equipment. After a reaction time of only a few hours Betonamit develops an enormous expansion pressure, which is soon so powerful that every hard rock and even reinforced concrete is broken apart.

## Slide 10: Conclusion: Many advantages of AGILE approach
Allow a combination of focus & flexibility
Fast learning & understanding
  By doing
  Shared learning within the teams & with stakeholders
Allow to get started (by slicing the big & complex challenge)
We changed our mindset
  Efficient project management  how to get fast results
  Find the perfect solution  identify multiple options to maximise the chances of success