## Slide 2: Derivation of conditional clearance limits for the disposal of NORM waste from O&G industries in hazardous waste landfills
R.S.S.P. ALMEIDA, R. PASSOS, S. COTA, V. CUCCIA, V. VASCONCELOS
Nuclear Technology Development Center – CDTN/CNEN
Belo Horizonte, Brazil
F. SCHENATO, N. RUPERTI
Brazilian Nuclear Energy Commission – CNEN
Rio de Janeiro, Brazil

## Slide 3: Introduction
Oil and gas deposits often occur in aquifers containing brine (salty water), resulting in various types of waste during exploration, production, and decommissioning activities NORM
Industrial landfills can be a potential solution
Extraction process can concentrate waste containing radium and lead
Necessity of suitable solutions for safe and cost-effective disposal
Safety assessment using RESRAD-OFFSITE to determine a safe activity concentration range for conditional clearance, derived from a dose criterion of 1mSv/year, aiming the disposal of O&G NORM waste in industrial landfills

## Slide 4: Reference scenario
The analysis is based on a reference scenario, focusing on long-term exposure of adult individuals living and farming near an industrial landfill
Landfill model based on Brazilian standard NBR 10.157: impermeabilization, liner, and cover layer
Deposition of 60,000 drums of scales and oil sludges
Main sources of radioactivity  U-238 and Th-232 decay chains
Primary radionuclides of concern  Ra-226, Ra-228, Pb-210, Th-228, and Po-210
Release times are determined based on the half-life of the liner

## Slide 5: Reference scenario
Future use of the area: rural dwelling
Dose estimates leaching, dust transport, and root uptake as release pathways
Exposure pathways  ingestion, inhalation, and external exposure
Soluble concentrations of radionuclides are based on estimated solubility limits
Code used  RESRAD-OFFSITE 4.0
Fruit ranch – 5640 m²
Pasturage – 13920 m²
Grain – 5640 m²
Garden – 2800 m²
Well

## Slide 6: Reference scenario
Parameter group | Parameter | Value
Preliminary inputs | Basic radiation dose limit | 1 mSv/yr
Inventory | Specific concentrations for Ra-226, Ra-228, Pb-210 | 1 Bq/g
Hydrology | Precipitation Rainfall erosion index | 1.5 m 462.6
Clean cover | Thickness Erosion rate (calculated) Cover soil erodibility | 1 m 1.77E-4 m/yr 0.23
Primary contamination (PC) | X-Y-Z dimensions Hydraulic conductivity Erosion rate (calculated) Evapotranspiration coefficient Slope-length-steepness factor Fraction area of fruit crops Root depth of non-leafy vegetables | 54.3 x 32.5 x 10 m 3.15 m/yr 3.0E-4 m/yr 0.77 1 0.178 1 m
Unsaturated zone | Thickness Hydraulic conductivity | 1.5 m 3.15 m/yr
Saturated zone | Distance from PC edge to well Hydraulic conductivity Total/effective porosity Hydraulic gradient to well Depth of aquifer contributing to well | 0 m 3.15 m/yr 0.45 0.15 10 m
Transport | Bulk density Kd for Ra, Pb, Th, Po | 1.46 g/cm3 2500, 2000, 1900, 210 cm3/g
Key input parameters used in Resrad-Offsite in the present work

## Slide 7: Simulation results
Safety assessment for radionuclides in O&G NORM wastes considers effective doses and pathways
Total specific dose over time for reference scenario (activity concentrations of 1 Bq/g for Ra-226, Ra-228, and Pb-210)
Plant consumption is the major contributor to the dose due to agricultural areas above disposal area
Behavior influenced by Kd values used for radionuclide sorption during transport simulation in geosphere
Single-parameter sensitivity analysis conducted to quantify the influence of input parameters on effective dose estimates for plant ingestion pathway. Most sensitive parameters identified: fraction area of fruit crops, depth root of non-leafy vegetables, cover erosion parameters
Waterborne pathways influenced by Kd for Ra-226 in unsaturated zone, saturated zone hydraulic conductivity, and precipitation
Analysis helps identify relevant parameters and will be used for additional uncertainty analysis

## Slide 8: Simulation results
Total specific dose for all radionuclides and pathways considered
(radon excluded)
Specific dose for Ra-226 and progenies for all pathways considered (radon excluded)

## Slide 9: Simulation results
Specific dose for all radionuclides for each pathway considered (radon excluded)
Soil guideline for Ra-226 (all pathways considered, except radon exposure)

## Slide 10: Conclusion and recommendations
Further work needs to evaluate derivative reference values, combine results for each radionuclide, and include radon dose input
Preliminary estimation suggests Ra-226 clearance level between 1-10 Bq/g, while Ra-228 and Pb-210 levels may be higher
Assessment of O&G waste inventory in Brazil indicates up to 40% could be conditionally cleared for disposal in industrial landfills
Optimizing engineering barriers for O&G NORM disposal ensures dose criteria and sustainability in social, economic, and environmental aspects

## Slide 11
Thank you!
Rafael Almeida
rafael.almeida@cdtn.br
+55313439-9524
www.gov.br/cdtn
www.gov.br/cnen