## Slide 1: Progress in Off-site Environmental Remediation in Japan
November 2023
MORI Yoshitomo, Ph.D.
Ministry of the Environment, Japan
International Conference on the Safety of Radioactive Waste Management, Decommissioning, Environmental Protection and Remediation: Ensuring Safety and Enabling Sustainability

## Slide 2
Progress of Decontamination
Full-scale decontamination was completed in 100 municipalities of 8 prefectures both in the Special Decontamination Areas (SDA), and the Intensive Contamination Survey Areas (ICSA), by March 19, 2018, except for the Restricted Areas. In the Restricted Areas, decontamination still continues (e.g. in the Specified Reconstruction and Revitalization Base Areas).
Decontamination of Residents
Demolition of houses, etc.
Intensive Contamination Survey Areas
(decontamination implemented by municipalities)
Completed in March 2018
Special Decontamination Areas
(decontamination implemented by the national gov.)
Completed in March 2017
Municipalities designated as Intensive Contamination Survey Areas
Municipalities where designation of Special Decontamination Areas or Intensive Contamination Survey Areas has been lifted
Full-scale decontamination completed in Special Decontamination Areas
Special Decontamination Areas
Restricted Areas
Specified Reconstruction and Revitalization Base Areas

## Slide 3
Efforts in the Restricted Areas (Decontamination, demolition of houses and other buildings in Specified Reconstruction and Revitalization Base Areas)
Evacuation order was lifted on August 30, 2022
Evacuation order was lifted on June 30, 2022
Evacuation order was lifted on March 31, 2023
Evacuation order was lifted on April 1, 2023
Evacuation order was lifted on May 1, 2023
Evacuation order was lifted on Jun 12, 2022
特定復興再生拠点区域
帰還困難区域
津島地区
室原地区
末森地区
帰還困難区域
特定復興再生拠点区域
Interim Storage Facility
FDNPS
特定復興再生拠点区域
帰還困難区域
特定復興再生拠点区域
帰還困難区域
長泥地区
特定復興再生拠点区域
帰還困難区域
野行地区
特定復興再生拠点区域
帰還困難区域
For the Restricted Areas, mayors of municipalities prepared plans for the areas of the Specified Reconstruction and Revitalization Base Areas (SRRBA) and environmental improvement (e.g. decontamination, infrastructure development) within the areas in accordance with the Act on Special Measures for the Reconstruction and Revitalization of Fukushima.
Based on the plan, decontamination and demolition of houses, etc. have been implemented in the SRRBA, and all evacuation orders in the SRRBA were lifted by May 2023 (Katsurao Village: June 12, 2022, Okuma Town: June 30, 2022, Futaba Town: August 30, 2022, Namie Town: March 31, 2023, Tomioka Town: April 1, 2023, Iitate Village: May 1, 2023), except for some part of roads.
Futaba Town (approved on Sep. 15, 2017, approx. 560 ha)
Okuma Town (approved on Nov. 10, 2017, approx. 860 ha)
Tomioka Town (approved on Mar. 9, 2018, approx. 390 ha)
Namie Town (approved on Dec. 22, 2017, approx. 660 ha)
Iitate Village (approved on Apr. 20, 2018, approx. 190 ha)
Katsurao Village (approved on May 11, 2018, approx. 95 ha)
Nagadoro District
Restricted Area
SRRBA
Restricted Area
SRRBA
Tsushima District
Murohara District
Suenomori District
Restricted Area
SRRBA
Restricted Area
SRRBA
Restricted Area
SRRBA
Restricted Area
SRRBA
Noyuki District
Interim Storage Facility
FD
NPS

## Slide 4
Treatment of Removed Soil and Waste (within Fukushima Prefecture)
For final disposal outside Fukushima Prefecture
Interim Storage Facility
Note: Waste other than the Specified Waste will be treated in accordance with Waste Management Law. For particular, categories of waste, approaches in the Act on Special Measures is applied.
Landfill Facility for Specified Waste
Temporary Storage Sites
Treatment plants
Removed Waste
Removed Soil
Decontamination
For recycling
Temporary Storage Sites
Treatment plants
100,000 Bq/kg
or less
More than
100,000 Bq/kg
For recycling
Designated Waste
Waste in the Countermeasure Area
Specified Waste

## Slide 5
Transportation to the Interim Storage Facility
Transportation of removed soil and waste to the Interim Storage Facility (ISF) has been implemented from FY2015, and almost all of the removed soil and waste have been transported to the ISF, by March 2022, other than the Restricted Areas.
Approximately 13.46 million m3 of removed soil and waste (including those in the Restricted area) have been transported to the ISF (as of the end of Mar. 2023).
Volume transported in a single year
(cubic meters) (bar graph)
Cumulative transportation volume
(cubic meters) (line graph)
FY2015
FY2016
FY2017
FY2018
FY2019
FY2020
FY2021
FY2022
Approx. 50,000m3
Approx. 190,000m3
Approx. 550,000m3
Approx. 1,840,000m3
Approx. 4,060,000m3
Approx. 3,870,000m3
Approx.
2,340,000m3
Approx.
570,000m3
Change over time for the volume of removed soil and waste transported to the ISF
Approx. 2,620,000m3
Approx. 6,680,000m3
Approx. 10,550,000m3
Approx. 12,890,000m3
Approx. 13,460,000m3
(as of Mar. 31, 2023)
Okuma IC in service
Joban Futaba IC in service

## Slide 6
Overview of the Interim Storage Facility
The Interim Storage Facility (ISF) was built to manage and store removed soil and waste arising from decontamination activities in Fukushima Prefecture and incinerated ash (>100,000 Bq/kg), safely and in an integrated manner, until final disposal outside Fukushima Prefecture, which is stipulated in the Japanese law, to be completed within 30 years (by March 2045) from the start of transportation to the ISF.
The ISF occupies around 1,600 ha (almost same area with Shibuya City in Tokyo). Okuma Town and Futaba Town accepted the ISF, by making very difficult decisions. The MOE will continue to work on the ISF project by placing first priority on its safety.
Soil Storage Facility, etc.
(Futaba construction area 2)
Soil Storage Facility
(Okuma construction area 1)
Soil Storage Facility
(Futaba construction area 3)
Waste Storage Facility
(Okuma construction area 1)
Soil Storage Facility
(Okuma 5 construction area)
Waste Storage Facility
(Futaba construction area 2)
Soil Storage Facility
(Okuma construction area 4)
Soil Storage Facility
(Okuma construction area 2)
Soil Storage Facility
(Okuma construction area 3)
Waste Storage Facility
(Futaba construction area 1)
Futaba Temporary Incineration Facility and Temporary Ash Treatment Facility
(No. 1) (No. 2)
Soil Storage Facility, etc.
(Futaba construction area 1)
Okuma Temporary Incineration Facility
Legend
Conveyer belt
Soil Storage Facility
Soil Separation Facility
Temporary Incineration Facility and Temporary Ash Treatment Facility
Transportation and Conveyance route
Waste Storage facility
Stock Yards
Screening Facility

## Slide 7
The Interim Storage Facility (1)
Source: Interim Storage Facility Information Center (https://www.jesconet.co.jp/interim_infocenter/index.html)

## Slide 8
Source: Interim Storage Facility Information Center (https://www.jesconet.co.jp/interim_infocenter/index.html)
The Interim Storage Facility (2)

## Slide 9
Source: Interim Storage Facility Information Center (https://www.jesconet.co.jp/interim_infocenter/index.html)
The Interim Storage Facility (3)

## Slide 10
Necessity for Recycling of Removed Soil
Amount of removed soil and waste transported to the Interim Storage Facility:
Equivalents to volume of 11 Tokyo Domes (Baseball park)
Toward final disposal outside the Fukushima Prefecture:
Volume Reduction before the final disposal is a key measure
Recycled soil
Covering soil
Recycling
Recycling under management in public work projects, etc.
Chart: 
| 8,000Bq/kg超 | 8,000Bq/kg以下
 | 0.241 | 0.759
Complete final disposal outside Fukushima within 30 years from the start of transportation to the Interim Storage Facility
After the volume reduction
Soil with relatively low
radioactivity concentration
Distribution of radioactivity concentration in removed soil
8,000 Bq/kg or lower
Approx. 3/4
More than 8,000 Bq/kg
Approx. 1/4

## Slide 11
(Overview)
The following demonstration projects using removed soil as a basis of farmlands has been implemented in Nagadoro District, Iitate Village.
(1) Agricultural land development: In April 2021, large-scale agricultural land development (approx. 22 ha) using removed soil (approx. 230,000 m3) started.
(2) Paddy field tests: Since FY2021, tests have been conducted on the functions required for paddy fields (e.g. permeability, soil strength) and it was confirmed that the results generally fell in within the range of acceptable values.
(3) Demonstrative flower cultivation with local residents
(Results)
The radioactivity in cultivated foods was well below the criterion of 100 Bq/kg (0.1 - 2.3 Bq/kg).
The monitoring results to date have shown no increase in air dose rates, etc. caused by the recycled materials and its safety was confirmed.
Demonstration area
(2) Rice paddies
(3) Flower cultivation
Recycled soil yard site
(Removed in FY2022)
Prefectural
road 62
Hiso River
(1) Agricultural land
development area
(1) Construction section No. 2
As of November 2022
(2) Paddy fields
(3) Flower cultivation
Demonstration Projects for Recycling in Fukushima Prefecture

## Slide 12
Nationwide Dialogue Forum
Installation of Potted Plants using Removed Soil
Nine meetings have been totally held. All of the dialogues were recorded and available online.
In FY2022, potted plants using removed soil were installed at METI, MLIT and other relevant ministries and agencies (17 facilities outside Fukushima Prefecture as of the end of January 2023).
Site tours were held for the Soil Storage Sites in the Interim Storage Facility and the demonstration project area in the Nagadoro district of Iitate Village.
Site Visits
← Removed soil with radioactvity concentration of approx. 5,100 Bq/kg is used.
Prime Minister’s Office
Planter
(MOE Headquarter )
Participants in Davos Meeting
Site Visit to the Demonstration Project Site
Site Visit to the Interim Storage Facility
University students from outside Fukushima Prefecture
Efforts to Build Understanding toward Final Disposal and Recycling (inside Japan)
Office of the Minister of the Environment
Dialogue forum in Tokyo (Aug. 19, 2023)

## Slide 13
Efforts to Build Understanding toward Final Disposal and Recycling (international)
Since shortly after the accident, the MOE has had a number of opportunities to discuss and exchange views on off-site remediation activities through missions, meetings with the IAEA, and bilateral meeting with countries with experience to address similar challenges.
In 2022 and 2023, tours were held for press of foreign countries to disseminate progress made for decontamination activities and remaining issues to be addressed.
Taking opportunities of international conferences (e.g. The 27th Conference of the Parties (COP27) to the United Nations Framework Convention on Climate Change (UNFCCC), G7 Summit in Hiroshima), reconstruction efforts following the Great East Japan Earthquake and the accident at TEPCO's Fukushima Daiichi Nuclear Power Station were disseminated.
G7 Summit (Hiroshima)
Experts Meeting with the IAEA
Tours for foreign press
COP27 (Egypt)
Source: Foreign Press Center Japan

## Slide 14: IAEA-MOE Japan 1st Experts Meeting on Volume Reduction and Recycling of Removed Soil Arising from Decontamination Activities (2023 - )
Flower and tree cultivation in plastic greenhouses
Overview of the 1st meeting
Date / Place
Schedule: Monday, May 8 - Friday, May 12, 2023
May 8: Meeting with the Ministry of the Environment
May 9-10: Site visit to Fukushima Prefecture (Interim Storage Facility, demonstration area for environmental restoration in Nagadoro District, Iitate Village, discussions with Iitate Village Office staff and Nagadoro District residents, courtesy visits to Iitate Village Mayor, Futaba Town Mayor, and Okuma Town Mayor, etc.)
11th-12th: Meeting with the Ministry of the Environment, courtesy visit to the Minister of the Environment
Main agenda
1) Status of progress of recycling and final disposal of removed soil, and promotion of public understanding
2) Progress made on the Technology Development Strategy for Volume Reduction and Recycling of Removed Soil
This meeting was held by the International Atomic Energy Agency (IAEA) upon the request of the Ministry of the Environment (MOE), Japan. The meeting was intended to exchange views concerning the measures taken by the MOE Japan on the recycling of removed soil, final disposal in the future, and to conduct the site visits to the Interim Storage Facility and demonstration area for environmental restoration in Nagadoro District, Iitate Village. Provision of international assessment and advice from technical and social perspectives was expected.
The final report will be produced by the IAEA after the 3rd Experts Meeting.
Background
Main results of the 1st Meeting
Main statements by the IAEA
We have seen a lot of work already done with a constant commitment to demonstrating safety.
The demonstration project is really important. Through the demonstration project, important information for interested parties can be provided on the recycling of removed soil.
Site visits
Demonstration of paddy fields
Flower and ornament plant cultivation in greenhouses in the demonstration facility of Nagadoro District
Note: The summary report of the 1st IAEA-MOE 1st Experts Meeting was published on Sep. 1, 2023 and it is available at: https://www.env.go.jp/en/press/press_01843.html

## Slide 15
Summary
  (Decontamination)
  Full-scale decontamination activities were completed by March 2018, other than the Restricted Area (RA). In conjunction with progress of other reconstruction activities, evacuation orders were lifted by March 2020, other than the RA.
  In the RA, decontamination activities have been still in progress, and the evacuation orders in the Specified Reconstruction and Revitalization Base Areas (SRRBA) in 6 municipalities were lifted by May 2023.
  (Transportation, Storage of generated soil and waste)
  Soil and waste arising from the decontamination activities in Fukushima Prefecture have been transported into the Interim Storage Facility (ISF), and almost all of the removed soil and waste had been transported into the ISF by March 2022, other than the RA.
  More than 13 million m3 of soil and waste have been transported into the ISF, and treated soil is stored in the ISF, which are supposed to be transported again out of the ISF, to be finally disposed of outside Fukushima Prefecture by March 2045.
  (Promotion of volume reduction and recycling)
  Taking account of the difficulties to find out the place to accommodate all of the removed soil and waste, as well as high occupancy of removed soil with relatively low radioactivity concentration, volume reduction and recycling of removed soil have been promoted.
  Based on the Strategy, technology development and demonstration projects have been simultaneously promoted, aiming at completion of development of necessary basic technologies by March 2025. Efforts to build nationwide public understanding, as well as sharing information with international communities have been also implemented, taking the opportunities of international meetings, conferences and tours for foreign media.
  (Cooperation with international society)
  The MOE has shared wide range of experience and lessons learned obtained through more than 12-year off-site remediation activities. This effort will be continued through Experts Meeting with the IAEA and bilateral discussion with other countries.

## Slide 16
For more information: http://josen.env.go.jp/en/
yoshitomo_mori@env.go.jp
Thank you