## Slide 1
Introducing NACARTE:
Neural Network Assisted CAD-based Real Time dose-Estimator
Mario Belottia, Javier Aguacila,b, Rafael Juareza, Javier Sanza
aUNED, Calle de Juan del Rosal 12, Madrid, 28040, Spain, Madrid
b Instituto de Fusión Nuclear “Guillermo Velarde”, Universidad Politécnica de Madrid, Madrid, Spain
Original CAD
Radiation field
Simplified CAD
MCNP model
Current workflow for radiation field prediction
NACARTE: Neural Network Assisted CAD-based Analytical Real-Time Estimator
Original CAD
Radiation field
Simplified CAD
The current workflow for radiation field estimations is MCNP centered, making it:
Very accurate
Very slow
Scheduled, long-term & well-resourced safety-related studies
Scoping, iterative & design conceptualizations (e.g., Hot Cell Complex)
Rough estimations
Real-time calculation
Powerful 3D engine: Integration into the CAD software SpaceClaim
Analytical method: Point Kernel
Enhanced accuracy: Neural Network to forecast build-up factor
The point-kernel method estimates radiation dose by integrating contributions from point sources using a ray-based kernel function
Introduction
Point Kernel implementation into Space-Claim
Neural Network based Build-up factor prediction
Point Kernel method
Challenges |  | 
Build-up factor estimation |  | Real-time dose estimations
The Build-Up factor () accounts for the scattered contribution. It is case-sensitive and needs gross assumptions or tailored prediction |  | As 3D complexity grows, ray-tracing get noticeably slower
Challenges |  | 
Build-up factor estimation |  | Real-time dose estimations
 |  | As 3D complexity grows, ray-tracing get noticeably slower
Two adjacent rooms with a point source contains most of the physics to be covered in most of the radiation shielding cases. This is a template for training
We propose a Multi-layer Perceptron (MLP) that maps the unique features of this configuration to predict a Build-up factor.
Training
Database: suite of 2631 MCNP cases with varying wall thickness, source energy and source position.
Loss function:
Comparison of build-up factor MLP vs. MCNP
SpaceClaim as 3D engine for direct CAD-based estimate  no meshing, no translation to CSG
Ray tracing algorithms - use of accelaration structures (Bounding Volume Hierarchy) to speed-up intersection operations
GPU implementation - thousands of cores available for calculation. CUDA based libraries.
Calculation time reduced by several orders of magnitude compared to a brute application of already built-in functions in Space-Claim for body intersections.
Application to the ITER Hot Cell Complex
NACARTE application
Future work
The future work will be articulated around:
Alternative neural-network architectures to show a better performance beyond the range of training. Particularly in relation to varying geometries.
Extended training once the NN architecture is established. A wider range of cases, including larger spans of wall thickness, source energy, and different shielding shapes.
Lineal, surface and volumetric sources as integration of point sources to represent any sort of radiation source.
Prediction of build-up factor considering multilayered shielding, including different materials and angle between walls.
Application to diverse topics of relevance in ITER and comparison versus MCNP as validation of the tool in pertinent environments
Ray tracing times in an unknown geometry
Comparison of dose estimation NACARTE vs. MCNP
Dose rate estimate with NACARTE
Standard radiation scenario
Operation | Time (ms)
Ray tracing | 72
Build-up factor calculation | 118
Rendering mesh texture | 1576
Total | 1766
 | Brute force | Accelerated
N. rays | ≈ 50 | ≈ 500k
Time [s] | ≈ 120 | ≈ 1E-2
NACARTE performance on a 2 rooms case with a mesh of 64000 voxels
Real-time dose estimation
Conclusions
NACARTE shows the capability to predict dose rate estimates in relevant conditions:
Reliability within a factor x2
Real-time calculation (few seconds)
ITER Hot Cell Complex
NACARTE is the position to assist the design of ITER and many other nuclear facilities worldwide in an efficient manner
 saving thousands € in analysis and securing calendars!