## Slide 1
Shuo Wang1, Zongyu Yang1, Meihuizi He2, Xiaobo Zhu1, Yifei Zhao1,3, Guohui Zheng2, Fan Xia1 and Wulyu Zhong1
on behalf of HL-2A/3 Team and collaborators
1 Southwestern Institute of Physics (SWIP), Chengdu, China
2 Nankai university, Tianjin, China
3 Dalian university of technology, Dalian, China
AI-driven tokamak control in HL-2A/3
Workshop on Al for Accelerating Fusion and Plasma Science, 28th November -1st December 2023, in Vienna, Austria

## Slide 2
Outline
Brief introduction to HL-2A&HL-3
Progresses in HL-2A & HL-3
  AI-based disruption prediction
  ELM/L-H transition detector
  Identification of MHD Instabilities with AI
  Plasma reconstruction
  Fast prediction of beta limits in HL-3
Summary

## Slide 3
The HL-2A Tokamak
Lots of ML/AI researches can be done with the diagnostic data of HL-2A tokamak
  Intelligent operations
  Prediction & protection
  Plasma modeling

## Slide 4
ITER-related scenarios, such as baseline H-mode, hybrid & steady state. Explore high-performce operation regimes toward fusion reactors, such as N >3, high density with Greenwald fraction >1, etc.
Advanced divertor configuration concept and physics. Test and validate high heat flux PFCs.
Key plasma physics and technologies concernd by ITER, including EP / VDE / NTM / ELM control, disruption alerting & mitigation, etc.
D-T fusion experiments to explore buring plasma physics and technologies.
Addressing critical physics and technology issues for ITER & fusion reactors
HL-3 Parameters | 
Major radius | R = 1.78 m
Minor radius | a = 0.65 m
Plasma current | Ip = 2.5~3 MA
Toroidal field | BT = 2.2~3 T
Elongation | = 1.8
Triangularity | δ > 0.5
Heating power | >30 MW
HL-3 Parameters | 
Major radius | R = 1.78 m
Minor radius | a = 0.65 m
Plasma current | Ip = 2.5~3 MA
Toroidal field | BT = 2.2~3 T
Elongation | 
Triangularity | δ > 0.5
Heating power | >30 MW
HL-3 Tokamak (formerly known as HL-2M)

## Slide 5
First Plasma
2022
1MA limiter configuration
2020
2023
Mar.
Snowflake
1MA divertor configuration
Apr.
Aug.
Sep.
Nov.
1MA H mode
Timeline of HL-3
First divertor configuration
Upgrade
First H-mode
Jul.

## Slide 6
Outline
Brief introduction to HL-2A&HL-3
Progresses in HL-2A & HL-3
  AI-based disruption prediction
  ELM/L-H transition detector
  Identification of MHD Instabilities with AI
  Plasma reconstruction
  Fast prediction of beta limits in HL-3
Summary

## Slide 7
Disruptions in tokamaks
Major disruptions of tokamak plasmas have been the subject of intense investigations
It is not always easy to classify disruptions
  The events that lead to a disruption are a complex combination of several factors
F C Schuller 1995 Plasma Phys. Control. Fusion 37 A135
Hyatt A.W. et al 2001 Bull. Am. Phys Soc. 45 300

## Slide 8
AI Disruption Prediction and Mitigation in HL-2A
Algorithm backbone
  NN structure: 1.5D CNN+LSTM（A customized structure that performs well on fusion data)
  Performance: 96.1% accuracy with 30ms in advance
Interpretability, transferability and real-time capacity integrated in one framework
Interpretable: significance analysis for 6 disruption causes in HL-2A
Transferable：Output of the cross-tokamak disruption predictor on HL-3
Real-time：Vertical displacement induced disruption mitigated by SMBI during closed-loop online testing
Highly commended for KU Itoh Project Prize in EPS 2022

## Slide 9
AI Disruption Prediction and Mitigation in HL-3
Developed AI algorithm : VDE predictor (AUC~0.97) and multi-type predictor.
  Training set extremely limited: ~600 shots
Implemented closed loop : real-time disruption prediction and mitigation in PCS
  Time consumption of a calculation cycle: ~0.6ms
AI-based VDE prediction algorithm
Comparison of halo currents during VDE and MGI induced disruptions
Receiver operator characteristic curves of the VDE predictor and the multi-type disruption predictor
A detailed report will be given in 29 Nov by Dr. Zongyu Yang

## Slide 10
Outline
Brief introduction to HL-2A&HL-3
Progresses in HL-2A & HL-3
  AI-based disruption prediction
  ELM/L-H transition detector
  Identification of MHD Instabilities with AI
  Plasma reconstruction
  Fast prediction of beta limits in HL-3
Summary

## Slide 11
ELM/L-H transition detector
H-mode Operation (Ip=0.5 MA)
[IAEA-FEC 10/2023]
Type-I edge localized mode (ELM) is dangorous for ITER & future fusion plants
  Energy losses in Type I ELMs can lead to melting, erosion, and evaporation of proposed divertor materials
The type-I ELM should be suppressed or mitigated to small ELMs
How to detect the ELMs in real time?

## Slide 12
The training process of ELM detection
Input
  HL-2A #20000-25200, 760shots
  Divertor Dα emission
  Stored energy WE
  Line-average density ne
  Plasma current Ip
Label
  Duration of ELM : 1
  Others : 0
Detector Model
  Conv1DLSTMTCN
Yao Huang et al，Nulcear Fusion & Plasma Physics (in Chinese) 40(4) 300-306

## Slide 13
Application of AI-ELM-detector in HL-2A
Yixuan Li et al，Nulcear Fusion & Plasma Physics (in Chinese) , accepted
Disadvantage:
  Several ELMs are missed in the beginning of H mode
One possible method: try to find the L-H transition time

## Slide 14
Identification of the L-H transition
Label
  Start time of L-H transition: Limit-cycle oscillation (LCO)
  End time of L-H transition: The first ELM
  L-H transition -> 1
  Partial L-H transition -> 2
  W/O L-H transition -> 0
Results
  73/81 of the L-H transition is achieved by the model
Jun Cheng et al， J. Nucl. Mater. (2015) 463 455-458
LH begin
LH end
NBI start
NBI end +300ms
2
2
1
10ms
5ms
? ms
0
0

## Slide 15
Outline
Brief introduction to HL-2A&HL-3
Progresses in HL-2A & HL-3
  AI-based disruption prediction
  ELM/L-H transition detector
  Identification of MHD Instabilities with AI
  Plasma reconstruction
  Fast prediction of beta limits in HL-3
Summary

## Slide 16
Identification of FB mode in HL-2A
The fishbone (FB) mode can be identified by spectrum analysis
The spectrum varies -> Not easy to identify the mode by programs
FB spectrum on HL-2A
Input
  780 shots
  Mirnov probes signal -> FFT
  Time window: 10 ms, 1MHz
  Frequency: 5-35 kHz
Label
  FB mode : 1
  Others : 0
Model
  ResNet-like

## Slide 17
Identification of FB mode in HL-2A
Test results
  Accuracy~94.7% for all the data slices

## Slide 18
Multi-MHD identification
Jiont identification of fishbone mode, tearing mode and long-live mode
  Multi-task learning could improve the accuracy for the identification of each mode
Accuracy | FB mode | TM | LL mode
Single-task learning | 94.7% | 92.7% | 94.1%
Multi-task learning | 95.5% | 93.7% | 95.3%

## Slide 19
Outline
Brief introduction to HL-2A&HL-3
Progresses in HL-2A & HL-3
  AI-based disruption prediction
  ELM/L-H transition detector
  Identification of MHD Instabilities with AI
  Plasma reconstruction
  Fast prediction of beta limits in HL-3
Summary

## Slide 20
Plasma reconstruction
[L L Lao et al 2022 PPCF 64 074001]
The plasma reconstruction is important
  Fundamental to tokamak research and operation
  The important part of fusion data analysis and plasma control
The off-line EFIT cannot be used for plasma control
The RT-EFIT is not sufficient for kinetic control

## Slide 21
Plasma reconstuction with NN in HL-3
Plasma current（1）
Magnetic pick up probes（39）
FLux loops（10）
PF/CS/TF coils current（18）
EFITNN
Dense+DeConv2D Net
Multi-task learning model
FLux on grid
Configuration parameters
The magnetic flux and configuration parameters are generated by off-line EFIT
Multi-task learning model is adopted to train the flux computational model and parameters computational model

## Slide 22
The flux and current density reconstruction
Fully connected NN + DeconvNet
Training set: Shot 1200-3199
Time: grid 33*33 -> 0.4 ms
grid 129*129 -> 2.0 ms
Relative error
  Flux -> 0.4%
  Current density -> 1.8%

## Slide 23
The parameters reconstruction
Fully connected NN
Additional confinement by reconstruction of flux and plasma current density
Training set: Shot 1200 – 3200
Test set: Shot 3201-4077
Results
  MRE : 0.12
  Absolute error：
    li：0.00618
    q95：0.200
    a：0.782 cm
    δu：0.0203
    δd：0.0161
    κ：0.0182
    rcenter：1.17 cm
    Zcenter：0.855 cm

## Slide 24
Outline
Brief introduction to HL-2A&HL-3
Progresses in HL-2A & HL-3
  AI-based disruption prediction
  ELM/L-H transition detector
  Identification of MHD Instabilities with AI
  Plasma reconstruction
  Fast prediction of beta limits in HL-3
Summary

## Slide 25
  Fast prediction of beta limits in HL-3
The advanced tokamak needs high beta
  Fusion power
  Pfus ~ β2B4
  Bootstrap current fraction
  fbs~βp
High beta will drive MHD disabilities
  NTM  soft beta limit
  XK  hard beta limit
XK should be suppressed to achieve high performance
How to know the beta limit ?
  = 4li

## Slide 26
  Generation of database in HL-3
The equiliria are built by EFIT code
Elongation:
Triangularity:
Calculate the no-wall and ideal wall beta limit by MARS-F code
The off-line calculation of the beta limit for each equilibrium could cost sevral hours

## Slide 27
  Relationships between beta limit and the parameters
All the trends ensure the reliability of the database
  The plasma elongation generally enhances both limits
  The effect is more pronounced for positive triangularity plasmas (
  = cli
  decreases with increasing pressure peaking factor (ppf)

## Slide 28
  Construction of NN and CNN models
NN and CNN models are selected
 | Plasma boundary | Equilibrium | Other
NN | plasma elongation() & triangularity() | ,, | Li, ppf
CNN | RZ(19 points) | pressure profile(11 points) & safety factor profile(12 points) | Li, ppf
 | Plasma boundary | Equilibrium | Other
NN |  |  | Li, ppf
CNN | RZ(19 points) | pressure profile(11 points) & safety factor profile(12 points) | Li, ppf
Input

## Slide 29
  Results of NN and CNN models
(MRE) |  | 
NN | 0.043 | 0.05
CNN | 0.033 | 0.055
(MRE) |  | 
NN | 0.043 | 0.05
CNN | 0.033 | 0.055
The trained NNs predict both the no-wall and ideal-wall limits with as high as 95% accuracy
Test cases with Tokamak Simulation Code (TSC)
Within 7%  limit
Within 10%  limit
Yifei Zhao, et al 2022 Plasma Phys. Control. Fusion 64(4) 045010

## Slide 30
Outline
Brief introduction to HL-2A&HL-3
Progresses in HL-2A & HL-3
  AI-based disruption prediction
  ELM/L-H transition detector
  Identification of MHD Instabilities with AI
  Plasma reconstruction
  Fast prediction of beta limits in HL-3
Summary

## Slide 31
  Summary
ML/AI models have been trained for HL-2A/3 tokamak operation:
  Disruption prediction: successfully used to provide signal for MGI to mitigate major disruption
  Plasma reconstruction: for ISO-flux control in the future
  MHD recognition: ELM, TM/NTM, RWM and other instabilities control
What can we do in the future?
  AI-models optimization for the works above
  AI-PCS
  ……
[ David Humphreys, et al Journal of Fusion Energy (2020) 39:123–155]

## Slide 32
Thank you for your attention !